## Slide 1: S.R. 28 Road Reconstruction in Clinton County
Thursday, September 26, 2019
6 p.m.

## Slide 2: Welcome
Purpose of public hearing
Format
Visit our sign-in table
Informational handouts
Participate during public comment session
Submit written public comments
Project display area

## Slide 3: S.R. 28 Road Reconstruction in Clinton County
INDOT Project Team
  INDOT Crawfordsville District
  Project Management
  Public Involvement
  Communications
  Design/Engineering
  Environmental Analysis
  Real Estate
Recognition of elected and local public officials
Sign-in at attendance table to be added to project mailing list
Public hearing notice published in Frankfort Times 9/11 and 9/18
Mailed notification to known property owners within project area
Announcement of this meeting was posted to INDOT website. A media release was also issued
A copy of presentation and project documentation are available for review online via INDOT website

## Slide 4: Project Stakeholders
Indiana Department of Transportation
Federal Highway Administration
City of Frankfort
Clinton County
Elected & local officials
Residents and citizens
Commuters
Businesses
Emergency services
Schools
Churches
Community organizations

## Slide 5: How a Project Becomes a Project
INDOT - Transportation agency for State of Indiana
Six Districts – Central Office is located in Indianapolis
Project Selection
  Prioritize needs
  Call for Projects
  Program projects
  4 Year project listing – Statewide Transportation Improvement Program
  Project listing can be amended based on needs
  Development / Pre-Construction
    Requests for – Information, Qualifications, Proposals (RFI, RFQ, RFP)
    Consultant team selection
    Engineering
    Environmental Analysis
    Cultural Resource Evaluation
    Public Involvement / Community Outreach & Engagement
    Design (roadway, bridge)
    Utilities Coordination
    Real Estate Acquisition – appraising, buying, relocation
Project Delivery / Construction
  Project letting – contractor bidding process
  Construction, Maintenance, Operations

## Slide 6: Project Development
Project Selection
Early Coordination
Purpose & Need
Develop alternatives
Preliminary design phase
Environmental Analysis
PUBLIC INVOLVEMENT
Design
Environmental
Additional public involvement
Project Decision
Real Estate
Project Letting
Construction
Communicate project decision late 2019 / early 2020
Public hearing during environmental analysis phase 2019
Public Involvement:

## Slide 7: Environmental Consideration
  National Environmental Policy Act (NEPA)
  Requires INDOT to analyze and evaluate the impacts of a proposed project to the natural and socio-economic environments
  NEPA is a decision-making process
    Purpose and Need
    Develop & Screen Alternatives
    Preferred Alternative – determine a course of action
  Impacts are analyzed, evaluated and described in an environmental document
    What are the impacts this project might have on the community?
    How can impacts be avoided?
    Can impacts be minimized?
    Mitigation for impacts?
  Draft environmental document(s) released for public involvement August 2019
    Available for review via public repositories and online

## Slide 8: Types of items evaluated
  Right-of-way
  Streams, Wetlands, and Other Waters
  Floodplains
  Endangered Species
  Farmland
  Cultural Resources (Historic/Archaeological)
  Parks and Recreational Lands (Trails)
  Air Quality
  Community Impacts
  Public Involvement

## Slide 9: Environmental Analysis & Public Involvement
  Notice of Entry for Survey
    Letters were mailed to properties within general area adjacent to the public right-of-way
  Section 106 of National Historic Preservation Act – 2018 thru 2019
    Take into account proposal’s impact to historic & archaeological properties
    Public invited to participate
    Consulting Parties Meeting scheduled 11/1/18
      INDOT, FHWA and design consultant attended
      Invitations sent to identified local consulting parties, none attended the meeting
    Public notice issued with 30-day comment period
      Frankfort Times on 2/20/19
    “Adverse Effect Finding” finding issued by the Federal Highway Administration (FHWA)
  Draft environmental documents released for public involvement – August 2019
    Available for review via public repositories and online

## Slide 10: Project Resources
INDOT Crawfordsville District Office
  41 West 300 North, Crawfordsville, IN 47933
  http://www.in.gov/indot/2701.htm
  Planning, Project Development/Delivery, Construction, Maintenance for West Central Indiana
Frankfort Community Public Library
208 West Clinton Street, Frankfort, IN 46041
Phone: (765) 654-8746
INDOT Office of Public Involvement
  100 North Senate Avenue, Room N642, Indianapolis, IN 46204
  Phone: (317) 232-6601
  rclark@indot.in.gov
Transportation Services Call Center
Provides citizen and business customers with a single point-of-contact to request transportation services, obtain information, or provide feedback through multiple channels of communications.
855-463-6848 • INDOT4U.com • INDOT@indot.in.gov

## Slide 11: S.R. 28 Road Reconstruction – Project Limits
Approximately from intersection of S.R. 28 and C.R. 200 West, proceeding east along S.R. 28 to Hoke Avenue
Project length is 2.4 miles

## Slide 12: S.R. 28 Road Reconstruction
Resurface S.R. 28 from C.R. 200 West to Blinn St.
Reconstruct S.R. 28 from Blinn Street eastward to Hoke Avenue
Add right turn lane from (WB) S.R. 28 to (NB) Jackson Street
Reconstruct storm-water system, the sidewalks on the south side of S.R. 28 and replacing the sidewalk on the north side of S.R. 28 with a shared used path

## Slide 13: Purpose and Need
Purpose
  Address deteriorated pavement condition
  Improve safety within the corridor by adding turn lanes at Jackson and Clay intersections
  Improve pedestrian and bicycle infrastructure with ADA compliant facilities
    Emphasize ADA compliance due to proximity to downtown commercial district, city office building, Ivy Tech campus
    Address condition of sidewalks
    Bicycle accommodations do not exist along S.R. 28
Need
  Pavement condition is in need of repair / reconstruction
    Concrete pavement installed in 1971
    Most recent asphalt overlay installed in 2015
  Curbs within the project limits are in poor condition
  High number of vehicular accidents
    S.R. 28 at Jackson Street
    S.R. 28 at Clay Street

## Slide 14: Alternatives Considered
Do Nothing/No Build
  Perform routine maintenance only
  Does not meet purpose and need
Alternative 1
  Replace the existing pavement with full depth pavement
Alternative 2
  Rubblize (reduce pavement into rubble) the existing concrete pavement from begin project to Doyal Street, full depth replace asphalt pavement east of Doyal Street.
Alternative 3
  Full depth patch, profile mill and place a functional overlay on the existing pavement from begin of project to Doyal Street. Full depth replace asphalt pavement east of Doyal Street
Alternative 4 (Preferred)
  Mill & overlay to Blinn and replacement of existing pavement with full depth pavement east of Blinn

## Slide 15: Preferred Alternative
Pavement replacement and/or overlay with intersection improvements and pedestrian improvements
Roadway
  Mill and overlay from C.R. 200 W to Blinn Street
  Full depth replacement from Blinn Street to Hoke Avenue
  Dedicated left turn lanes at Clay Street
  Right turn lane at west approach leg of S.R. 28 at Jackson Street
  Replace existing curbs and gutters, existing storm sewer system, extend storm sewer east on Walnut Street past pavement replacement to Hoke Avenue, extending north to an unnamed tributary
  Bridge Deck overlay at Prairie Creek with repairs to curb and sidewalk on bridge
Sidewalk
  5-foot wide concrete sidewalk will be reconstructed along the south side of S.R. 28 from Blinn Street to Hoke Avenue to replace the existing sidewalk that started at West St.
  8-foot wide asphalt/concrete multi-use path will be constructed on the north side of S.R. 28 from C.R. 200W to Hoke Ave.
  Provide tree lawn between sidewalk/shared use path and curb – varying locations
  Trees will be replaced in the Historic District east of Prairie Creek
  New Rail crossing equipment

## Slide 16: Existing Roadway
Failing Pavement
Poor Drainage
Curbs and Sidewalks in Disrepair

## Slide 17: Typical Section
12-ft wide travel lanes
New Curb & gutter
8-ft wide multi-use path along the north side
5-ft wide sidewalk along the south side
2-way left turn lane from west end to Clay St.
Full depth pavement replacement east of Blinn
Improved Drainage - new inlets and storm sewers

## Slide 18: Maintenance of Traffic
Maintain local access to all businesses and residences during construction by maintaining one lane of traffic in the westbound direction.
Traffic will be phased with construction west of Jackson Street in 2020 and construction east of Jackson Street in 2021.
While each of these sections is under construction the eastbound traffic will be detoured and the westbound will remain open to one lane of traffic.

## Slide 19: Maintenance of Traffic – Detour 1

## Slide 20: Maintenance of Traffic – Detour 2

## Slide 21: Real Estate

## Slide 22: Real Estate Acquisition Process
Uniform Act of 1970
  All federal, state and local governments must comply
  Requires an offer for just compensation
Acquisition Process
  Appraisals
  Review Appraisals
  Negotiations
Right-of-way (ROW)
    Permanent
      Permanent ROW is land, once purchased by INDOT from the legal land owner, becomes ROW owned by INDOT
      Approximately 0.3 acre required for improvement
    Temporary
      Temporary ROW is land required during the construction of a project and is used for the purposes of construction-related activity
      INDOT pays legal land owner a fee for land use during construction
      Approximately 0.4 acre required for improvement

## Slide 23: Project Schedule
Preliminary design, evaluate community and environmental impact 2019
Public Hearing 2019
Complete Environmental Analysis Phase 2019
Real estate acquisition activities 2019-2020
  Appraising
  Negotiations/buying
Utilities relocations 2019 - 2020
Construction 2020 - 2021

## Slide 24: Submit Public Comments
Submit public comments using the options described in first page of information packet:
  Public Comment Form
  Via e-mail
  Participate during public comment session following formal presentation
INDOT respectfully requests comments be submitted by Monday, October 14, 2019
All comments submitted will become included in an official public hearings transcript and made part of the public record
Comments will be reviewed, evaluated and given full consideration during decision-making process

## Slide 25: Next Steps
Public and project stakeholder input
  Submit comments via options described on page 1 of information packet
INDOT review and evaluation
  All comments given full consideration during decision-making process
  Finalize/approve environmental document, complete project design
Communicate a decision
  INDOT will notify project stakeholders of decision
  Work through local media, social media outlets, paid legal notice
  Make project documents accessible via repositories
Questions? Contact Public Involvement Team

## Slide 26: Thank You
Please visit with INDOT project team following the presentation and public comment session
Project Open House
  Project maps, displays, INDOT project team and informal Q & A
  INDOT Crawfordsville District page http://www.in.gov/indot/2701.htm