WHITE COUNTY BUILDING DEPT. INSPECTION NOTIFICATION SCHEDULE

FAILURE TO REQUEST A REQUIRED INSPECTION FEE IS $50 PER INSPECTION!

# Call the Building & Planning Department at least 24 to 48 hours prior to inspection at 574-583-7355

Office hours are Mon-Fri 8:00 am to 4:00 pm, except for holidays. Have permit number, address, type of inspection, and phone number ready prior to calling.  It shall be the duty of the person doing the work &/or the home owner authorized by a permit to notify the building official that such work is ready for inspection.  It shall be the duty of the person requesting any inspections required by this code to provide access to and means for inspection of such work.

- Foundation/Post Hole Inspection: A) Inspection of the foundation/holes shall be made after poles or piers are set or trenches or basement areas 						   are excavated and any required forms erected and any required reinforcing steel is in place and prior to the 						   placing of concrete (minimum of 36” from bottom of foundation to finish grade).

- The pre-slab inspection: shall include excavations for thickened slabs intended for the support of bearing walls, partitions, structural supports, or equipment and special requirements for wood foundations.  Sanitary lines shall be air tested (5-PSI for 15 minutes).  If joints in supply lines must be used, an air test of at least 50-PSI is required.

- Plumbing, mechanical, gas and electrical systems inspection:  Rough inspection of plumbing, mechanical, gas and electrical systems shall be made prior to covering or concealment, before fixtures or appliances are set or installed, during frame inspection.  EXCEPTION: Ground-source heat pump loop systems tested in accordance with Section 2105.1 shall be permitted to be backfilled prior to inspection.

- Frame & Masonry Inspection:  Inspection of framing and masonry construction shall be made after the roof, masonry; all framing, firestopping, draftstopping and bracing are in place.

- Pre-Drywall: Inspection of insulation/vapor barrier.

- Final Inspection:  Final inspection shall be made after the permitted work is complete and prior to occupancy.  Dwellings and buildings shall not be occupied without an official Certificate of Occupancy.  Failure to obtain an official C/O can result in fines up to $300/day.

If needed, after each individual inspection, a list will be given to the builder stating necessary corrections to be done.  A follow up inspection will be required prior to concealment of repairs.  If all repairs haven’t been made at this time, a second follow-up inspection must be made.

A $35.00 charge will be assessed for second follow-up inspection and thereafter.  This charge must be paid prior to any additional inspections. If an inspection is scheduled and the structure is not ready, this may be treated as the first inspection.

No Certificate of Occupancy can be issued until all fees are paid and all requirements are met.

Failure to pay a fee is a Building Ordinance violation subject to fines up to $300/day.