CHECKLIST FOR RIGHT-OF-WAY PLANS

| 1. | Section-line and section-corner locations identified. |  |
| --- | --- | --- |
| 2. | Civil and congressional township information and county name shown. |  |
| 3. | All apparent property lines identified. |  |
| 4. | Names of last property owners of record shown. |  |
| 5. | Apparent existing right-of-way lines identified. |  |
| 6. | Property-corner monumentation identified, including iron pins, etc. |  |
| 7. | All proposed and temporary right of way identified, including purposes for temporary right of way. |  |
| 8. | Centerline bearing identified. |  |
| 9. | Right-of-way lines made to match up with those on abutting sheets or abutting projects. |  |
| 10. | Right-of-way project number and code number shown on each sheet. |  |
| 11. | Approach table completed. |  |
| 12. | Cross sections not furnished. |  |
| 13. | Note, “All R/W described from Line “__”, except as shown,” appears on all Plan and Profile sheets. |  |
| 14. | If more than one survey line is shown, the line intended as the construction line is identified as such. |  |
| 15. | R/W Index labeled as such. |  |
| 16. | Signature block included, equivalent to the one shown on the Right-of-Way Plans title sheet frame. |  |
| 17. | Construction limits shown to be inside the right-of-way lines. |  |
| 18. | Drafting line styles used as shown in IDM Chapters Fourteen and Fifteen. |  |
| 19. | The right-of-way lines and names of property owners shown on Plat No. 1 match those shown on the Plan and Profile sheets. |  |
| 20. | Equations and enough reference points included for old survey lines that original right of way was acquired from so that they can be re-established by the Office of Real Estate. |  |
| 21. | Station and offset of the nearest building corner shown and labeled for each building within 25 m (75 ft) of the new right-of-way line. |  |
| 22. | All subdivision names, lot lines, and numbers identified. |  |
| 23. | All mitigation sites delineated and labeled. |  |