TRAFFIC VEHICLE DETECTION LOOP SHAPE

The Specifications are revised as follows:

SECTION 805, BEGIN LINE 261, INSERT AS FOLLOWS:

Loops shall be of a regular octagon shape with side of 0.75 m (2.5 ft) in length or a circular shape with a 1.83 m (6 ft) diameter. An outline shall be laid out and painted where the loops shall be sawed. The loop locations shall be subject to the review and approval of the District Traffic Engineer. The District Traffic Engineer shall be notified 48 h prior to such field review.