DEMOLITION/RENOVATION NOTIFICATION TO IDEM

The Standard Specifications are revised as follows.

SECTION 202, AFTER LINE 33, INSERT AS FOLLOWS:

In accordance with IAC 14-10, the Contractor shall complete and submit a demolition/renovation notification to IDEM when demolition or renovation of buildings, houses, canopies, and bridges are part of the contract. This notification shall be submitted regardless of whether asbestos containing material is present. Each notification form submitted to IDEM may have a maximum of 10 structures listed on the form. For the purposes of this form, a structure includes a building, house, canopy, or a bridge. Fees for this demolition/renovation notification are $50.00 per notification and shall be paid to IDEM by the Contractor.

Copies of the demolition/renovation notification form can be obtained at: www.in.gov/icpr/webfile/formsdiv/44593.pdf. Questions concerning the completion of the demolition/renovation notification should be addressed to IDEM's Office of Air Management's toll free number (888) 547-8150. Office hours are Monday through Friday between the hours of 6:30 a.m. and 4:30 p.m. An inspector will assist in proper completion of the notification.

Initial notification to IDEM shall be by certified mail, return receipt requested, or by hand delivery. Verification of this notification shall be provided to the Engineer. The Contractor shall provide such notification 10 work days prior to the date on which demolition or renovation operations are anticipated to begin. If the Contractor postpones the beginning date of demolition or renovation operations, IDEM shall be provided written notice of the new start date, postmarked at least five work days or delivered at least two work days before these operations begin. Verification of this notification shall also be provided to the Engineer.

SECTION 202, BEGIN LINE 275, DELETE AND INSERT AS FOLLOWS:

202.06.1 Inspection and Removal of Asbestos. The Contractor shall comply with all applicable environmental regulations including but not limited to those as follows:

(a)	326 IAC 14-10 requires notification to the IDEM of all demolition or renovation operations. Notification is required for renovation operations only if reportable quantities of asbestos are broken, dislodged or disturbed during the renovation procedure. Initial notification to IDEM shall be by certified mail, return receipt requested, or by hand delivery. Verification of this notification shall be provided to the Engineer. The Contractor shall provide such notification 10 work days prior to the date on which removal or demolition operations are anticipated to begin. In accordance with 202.02 and IAC 14-10, a demolition/renovation notification is to be submitted to IDEM 10 work days prior to the start of demolition or renovation operations. During the 10 work day period, the IDEM may make a determination of the existence of asbestos materials. If the Contractor postpones the beginning date of demolition or removal operations, the IDEM shall be provided written notice of the new start date, postmarked at least five work days or delivered at least two work days before removal or demolition begins. Verification of this notification shall also be provided. Local governmental agencies may have additional regulations that must be followed. The Contractor shall contact IDEM's air management office to determine what local agencies have regulations.