Facility Name                                                        Ammonia Nitrogen (NH3-N)        SM 4500 NH3 D.

Chlorine Present  Yes  /   No      Removed by __________________________________________________

Analyst___________Analysis Date__________Analysis Start Time________Analysis Stop Time_________

Calibration Standards Prepared____________________________  Stock Standard Lot #:______________

Check Standard Prepared_________________________________  Stock Standard Lot #:______________

Standards and Samples Analyzed at the Same Temperature  Yes  / No    Check Std.                       % Rec.

Slope Check: Initial mVo_______  Final mVo_______  Δ mVo________ Acceptable = 58 ±  3 mVo @ 20o C

or 57 ±  3 mVo @ 25o C

Calibration Data

| Standard Concentration | Initial Reading Initial Reading | Adjusted Reading | Slope |
| --- | --- | --- | --- |

Analysis Data – Samples not analyzed on Sample Date preserved to pH < 2 with H2SO4 and Refrigerated

| Sample ID | Sample Date | Sample Comp or Grab | Date Preserved | Preserved by | Sample Volume (mL) | Final Volume (mL) | Initial Result (mg/L) | *Dilution Factor | Report Value (mg/L) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Check Std. |  |  |  |  |  |  |  |  |  |
| Dup. |  |  |  |  |  |  |  |  |  |
| Spike |  |  |  |  |  |  |  |  | ----- |
| Blank |  |  |  |  |  |  |  |  |  |

*Dilution Factor = Final Volume (mL)      	               Initial Sample Result (mg/L) x Dilution Factor = Report Value (mg/L)

Sample Volume (mL)

Spike Added (ug) = Concentration of Spike Added (mg/L) x Volume of Spike Added (mL)

% Spike Recovery = [(Spiked Sample Initial Result)(Final Volume) – (Sample Initial Result)(Final Volume)] x 100  =  ___%

### Spike Added

### Ammonia-N – recommended.doc    Created 12/2008 (Revised 1/2011)