Facility Name                                                                       Mixed Liquor Data              SVI – SM 2710 D.

Settled Sludge Volume – SM 2710 C.

Sample/Analysis Date_______________________						    DO – SM 4500-O G.

DO Meter Calibration

| Time | Analyst | NA – Meter Autocals | Barometric Pressure - mm Hg | Temperature oC | Meter Adjusted to mm | Meter Adjusted to mg/L |
| --- | --- | --- | --- | --- | --- | --- |

Dissolved Oxygen

| Sample ID | Analyst | Sample Time | *Preserved | **Analysis Time | DO (mg/L) | Temperature oC |
| --- | --- | --- | --- | --- | --- | --- |

* - Sulfamic acid – copper sulfate added if not analyzed by portable DO meter           ** - NA if analyzed by portable DO Meter

Settled Sludge Volume

| Sample ID | Analyst | Sample Volume (mL) | Time Set | Time Read | 30 minute Solids Level (mL) | % Settleable Solids | *TSS mg/L | SVI |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

Sample ID_____________Solids Level (mL) at _________ 5  _________ 10  _________ 15  _________ 20  _________ 25 minutes

Sample ID_____________Solids Level (mL) at _________ 5  _________ 10  _________ 15  _________ 20  _________ 25 minutes

Sample ID_____________Solids Level (mL) at _________ 5  _________ 10  _________ 15  _________ 20  _________ 25 minutes

Sample ID_____________Solids Level (mL) at _________ 5  _________ 10  _________ 15  _________ 20  _________ 25 minutes

% Settleable Solids at 30 minutes = [(Solids Level (mL) at 30 minutes/Sample Volume (mL)] x 100

* - Result from TSS bench sheet

SVI = [(30 minute Solids Level)(1000/Sample Volume)] x 1000

TSS (mg/L)

Microscope Evaluation:_______________________________________________________________________________________

____________________________________________________________________________________________________________

____________________________________________________________________________________________________________

Mixed Liquor Data    Created 12/2008