Required Pumping Data for Phase II Wellhead Protection Plans

The first step in updating your Wellhead Protection Plan is to gather all the information about your well(s) that is needed to determine whether or not the Phase I delineation is still appropriate for the current operating conditions. This information includes a listing of all wells, their location, and their current operating status, along with pumping records for the past five years.  Follow the process below for reviewing the data:

A.  Gather Pumping data used in the Phase I delineation

i. If your delineation was determined through modeling - list for each wellfield 		      and well (including all high capacity wells within the vicinity of the wellfield).   		      Usually rounded estimates were used. This information should be found in 	 	      your delineation report for the Phase I WHP Plan.

ii.  Identify units – either gallons per day, gallons per minute or Ft3 per day

iii.  If a fixed radii was approved, go to part B.

B.  Provide Current Pumping Data

i.  Using annual totals, calculate the annual average pumping for each wellfield 			for each year  over  the past 5 years.

ii.  List all operating wells and identify those that are new and those

that have been shut down along with their locations

iii. List peak daily or monthly pumping rates (if available)

iv. Calculate  an annual average pumping rate based upon the

highest pumping year.

C.  Compare Pumping Rates

i.  In the case of a fixed, radii, all values should be less than

100,000 gpd to continue to qualify for a fixed radii

ii.  In the case of modeling, if any values are 10% greater

than the total modeled pumping rate in the Phase I or if there

are significant changes in the wellfield configuration, then

a “new” delineation may be required.*

D.  Submit all information for review by IDEM staff.

i.   Use  the attached form if you  want an informal preliminary determination 		prior to your submittal due date.

ii.   After you are given preliminary approval of your current delineation, you still need to submit a complete Phase II application including your pumping data, well location information, updated maps, and description for final review .

iii. If not approved, follow IDEM recommendations for additional information or 		for a re-delineation.*

* A re-delineation will require the oversight of a Licensed Professional Geologist.

| Wellfield | Well ID | Average Daily Pumping Rate by Year |
| --- | --- | --- |
|  |  | 20__ | 20__ | 20__ | 20__ | 20__ |
| Units (Please Check the Appropriate Box) |  |  |
| ft3/day | □ | Gallons Per Minute (GPM) | □ |
| Gallons Per Day (GPD) | □ |