Storm Water Quality						327 IAC 15-13-16(c)(1)

An MS4 operator shall use a combination of practices to reduce the impact of pollutants in storm water run-off on receiving waters while utilizing the following requirements:

- infiltration practices will not be allowed in wellhead protection areas.

Solid Waste Landfills						329 IAC 10-16-11(b)

For solid waste landfills:

- new and lateral expansions must not be located in the 5 year time of travel; or

- within 3,000 feet of a community water supply well, if no 5 year time of travel established.

Spill Reporting							327 IAC 2-6.1-5(2)

The following spills from a facility that has been notified in writing by a water utility that it is located in a delineated public water supply wellhead protection area as approved by the department under 327 IAC 8-4.1 [shall be reported]:

- hazardous substance or extremely hazardous substances in excess of 100 pounds or the reportable quantity, whichever is less;

- spills of petroleum in excess of 55 gallons;

- spills of objectionable substances.

Secondary Containment of Hazardous Materials    		 327 IAC 2-10-3(a)(11)

New facilities must provide secondary containment unless there is:

- less than 660 gallons at a facility that is not in a delineated wellhead protection area as approved by the department under 327 IAC 8-4.1; or

- less than 275 gallons at a facility that has been notified in writing by a water utility that it is in a delineated wellhead protection area as approved by the department under 327 IAC 8-4.1.

Underground Storage Tanks 					327 IAC 9-2-1.1

New UST systems within a 1 year time of travel to a community public water supply well must be constructed with:

- a double walled tank;

- double walled piping; and

- a secondary barrier system.

Risk-Integrated System of Closures  				Non-Rule Policy

Ground water remediation in wellhead protection areas should:

- cleanup contaminated ground water to drinking water standards;

- apply treatment to contaminated ground water at the well to ensure delivered water meets drinking water standards; or

- implement exposure prevention with concurrence of public water supply and IDEM.