Indiana Department of Transportation LEVEL 2 Project Constructability Review 1 Stage 1 Preventative Maintenance Plan Review Project Manager/Construction Manager/Maintenance Manager

Primary DES No. 	 Contract No.

Route 	 District

Work Type	 RFC Date

Project Location

Project Description

County/City/Town 	 Designer

Project Manager _________________ Maintenance Manager _____________

Construction Manager 	         	Date ______________________

Evaluation of Project Constructability Quality

| CONSTRUCTABILITY | Y | N | N/A | Note | Flag |
| --- | --- | --- | --- | --- | --- |
| A. Site Investigation |  |  |  |  |  |
| * | Is the location survey complete? Does it include horizontal and vertical control? |  |  |  |  |  |
| * | 2. Is there adequate access to the construction site? |  |  |  |  |  |
| * | 3. Are there areas where the alignment can be improved? |  |  |  |  |  |
| * | 4. If shoulder will be used to carry traffic during staged construction, are they wide enough? Structurally adequate? Or should reconstruction be required? |  |  |  |  |  |
| * | 5. Does the existing pavement have a concrete base that is not shown? |  |  |  |  |  |
| * | 6. Will sawed joints be required for pavement removal? |  |  |  |  |  |
| * | 7. Are there hazardous materials on the project? |  |  |  |  |  |
| * | 8. If staged construction, are detours required? |  |  |  |  |  |
| * | 9. Does locality have noise limits that restrict night work? |  |  |  |  |  |
| * | 10. What are the locations of Geotech investigations? When were they taken? |  |  |  |  |  |
| * | 11. Has Geotech taken cores of the existing pavement and shoulder to verify the structure of the existing roadway? Where were cores taken? |  |  |  |  |  |
|  | Y | N | N/A | Note | Flag |
| B. Plans |  |  |  |  |  |
| * | 1. Do plans accurately show existing field conditions? |  |  |  |  |  |
| * | 2. Are control points included and are accurate to match the work to existing conditions? |  |  |  |  |  |
| * | 3. Are control points noted from project limits to project limits? |  |  |  |  |  |
| * | 4. Control points should be on both sides of a structure. |  |  |  |  |  |
| * | 5. Are the typical sections appropriate? |  |  |  |  |  |
| * | 6. Is the horizontal alignment appropriate? |  |  |  |  |  |
| * | 7. Is the vertical alignment appropriate? |  |  |  |  |  |
| * | 8. Will any right of entry or construction easements be required? |  |  |  |  |  |
| * | 9. Have pedestrian accommodations been addressed? |  |  |  |  |  |
| * | 10. Are the project limits appropriate? |  |  |  |  |  |
| * | 11. Can overloads/widths be hauled through job? What is load limit? |  |  |  |  |  |
| * | 12. Is the structure sizing and type selection appropriate? |  |  |  |  |  |
| * | 13. Is all previous repair work noted on the plans or as-built? |  |  |  |  |  |
| * | 14. Do the channel change layout details appropriately tie into the existing channel and surrounding topography? |  |  |  |  |  |
| * | 15. Are the mainline culverts located appropriate for the project and has construction phasing been considered? |  |  |  |  |  |
| * | 16. Is existing drainage affected by the temporary pavement? |  |  |  |  |  |
| * | 17. Does proposed drainage function during construction phases? |  |  |  |  |  |
| * | 18. Is storm sewer design appropriate for the project? |  |  |  |  |  |
| * | 19. Has offsite drainage been considered (beyond construction limits)? |  |  |  |  |  |
| * | 20. Is there sufficient room for access requirements? |  |  |  |  |  |
| * | 21. Any existing or proposed drainage issues to be addressed? |  |  |  |  |  |
| C. Utilities and R/W |  |  |  |  |  |
| * | 1. Is utility location & identification in progress? |  |  |  |  |  |
| * | 2. Is subsurface utility exploration (SUE) appropriate? |  |  |  |  |  |
|  | Y | N | N/A | Note | Flag |
| * | 3. Are there utilities that will be impacted? |  |  |  |  |  |
| * | 4. Check for overhead utility conflicts. |  |  |  |  |  |
| * | 5. Is existing right-of-way and property line determination complete? |  |  |  |  |  |
| * | 6. Is there enough room for all permanent retaining wall elements to fit within the proposed R/W? |  |  |  |  |  |
| * | 7. Do the structures fit in the R/W? |  |  |  |  |  |
| * | 8. Is there enough work room to build the structures on the R/W? |  |  |  |  |  |
| D. General Considerations |  |  |  |  |  |
| * | 1. Have conflicts with other projects in area been identified? |  |  |  |  |  |
| * | 2. Is there adequate access to the construction sites? |  |  |  |  |  |
| * | 3. Can any improvement be made in the alignment? |  |  |  |  |  |
| * | 4. Does existing pavement have a concrete base? |  |  |  |  |  |
| * | 5. Will sawed joints be required for pavement removal? |  |  |  |  |  |
| * | 6. Is there sufficient clearance in the work zone for construction operations? |  |  |  |  |  |
| * | 7. If staged construction, will detours be required? |  |  |  |  |  |
| * | 8. Will school buses, mail carriers, fire trucks, emergency vehicles, or other local traffic require special maintenance of traffic operations? |  |  |  |  |  |
| * | 9. Are the necessary restrictions (lane closures, hours of operations, holiday, weekend and major events restrictions) indicated? |  |  |  |  |  |
| * | 10. Can left or right turn lanes be maintained during construction? Or can they be closed during certain phases? |  |  |  |  |  |
| * | 11. Will temporary signals be required? |  |  |  |  |  |
| * | 12. Is the project compatible with future widening projects? |  |  |  |  |  |
| * | 13. Has the desired completion date been identified or letting date appropriate? |  |  |  |  |  |
| Note No. | REVIEWER COMMENTS |
| Note No. | DESIGNER COMMENTS |

(Attach additional sheets as necessary)