Indiana Department of Transportation LEVEL 2 Preventive Maintenance Post Construction Review Project Engineer/Supervisor/Contractor Superintendant

Primary DES No. 	 Contract No.

Route 	 District

Work Type	 RFC Date

Project Location

Project Description

County/City/Town 	 Designer

Project Manager

Construction Manager 	Date

Evaluation of Project Constructability Quality

| Evaluation Criteria | Y | N | N/A | Note | Flag |
| --- | --- | --- | --- | --- | --- |
| CONSTRUCTABILITY |  |  |  |  |  |
| A. Plans – Road |  |  |  |  |  |
| * | 1. Were the plans accurate with existing conditions? |  |  |  |  |  |
| * | 2. Were there conflicts between plans and standard drawings? |  |  |  |  |  |
| * | 3. Were control points included and match the work to existing conditions? |  |  |  |  |  |
| * | 4. Could existing drainage patterns be maintained during construction? |  |  |  |  |  |
| * | 5. Did driveway/turnout grades meet allowable standards? |  |  |  |  |  |
| * | 6. Were special structures required because of pipe size or number of pipes? |  |  |  |  |  |
| * | 7. Were paving limits shown? |  |  |  |  |  |
| * | 8. Was milling required? |  |  |  |  |  |
| * | 9. Could existing roadway materials be salvaged for other use? |  |  |  |  |  |
| * | 10. Did Geotech take cores of the existing pavement and shoulder to verify the structure of the existing roadway? Where were cores taken? |  |  |  |  |  |
| Evaluation Criteria | Y | N | N/A | Note | Flag |
| * | 11. What were the locations of Geotech investigations? When were they taken? |  |  |  |  |  |
| * | 12. Was the geotechnical engineering completed as necessary? |  |  |  |  |  |
| * | 13. Was there sufficient room for concrete pavement construction phasing? |  |  |  |  |  |
| * | 14. Were there conflicts with existing/proposed drainage. |  |  |  |  |  |
| * | 15. Was existing drainage affected by the temporary pavement? |  |  |  |  |  |
| B. Pay Items & Cost Estimate |  |  |  |  |  |
| * | 1. Were pay items appropriate? |  |  |  |  |  |
| * | 2. Were pay items consistent with specifications? |  |  |  |  |  |
| * | 3. Did the estimate include a pay item for all work included in the plans? Did pay items reflect scope of work? |  |  |  |  |  |
| * | 4. Were all temporary items for maintenance of traffic included? |  |  |  |  |  |
| * | 5. Pavement Removal item? |  |  |  |  |  |
| * | 6. RPM Removal item? |  |  |  |  |  |
| * | 7. Remove Traffic Signal item? |  |  |  |  |  |
| * | 8. Pipe Removal item? |  |  |  |  |  |
| * | 9. CZ Units for Barrier Wall item? |  |  |  |  |  |
| * | 10. Mob/Demob for seeding item? |  |  |  |  |  |
| C. Quantities |  |  |  |  |  |
| * | 1. Were quantities reliable and verifiable? |  |  |  |  |  |
| * | 2. Were quantity estimates developed to appropriate level? |  |  |  |  |  |
| D. Special Provisions |  |  |  |  |  |
| * | 1. Did special provisions include measurement and basis of payment? |  |  |  |  |  |
| * | 2. Were any special provisions omitted? |  |  |  |  |  |
| * | 3. Were there any apparent conflicts between plans, specifications or special provisions? |  |  |  |  |  |
| * | 4. Were all required permits detailed in special provisions? |  |  |  |  |  |
| * | 5. Were required lanes and closure periods clearly identified? |  |  |  |  |  |
| * | 6. Was special coordination required, RR, Permits, Regulatory? |  |  |  |  |  |
| * | 7. Were the environmental restriction period impacts identified? |  |  |  |  |  |
| * | 8. Were unique Special Provisions developed as needed? |  |  |  |  |  |
| Evaluation Criteria | Y | N | N/A | Note | Flag |
| E. Utilities and Railroad |  |  |  |  |  |
| * | 1. Were utility conflicts identified? |  |  |  |  |  |
| * | 2. Were all known utilities indicated on plans? |  |  |  |  |  |
| * | 3. Were driveways/sidewalks checked for conflicts with utilities. |  |  |  |  |  |
| * | 4. Could reasonable changes have been made to avoid utility conflicts? |  |  |  |  |  |
| * | 5. Were utilities to be maintained during construction? If so, were provisions in place? |  |  |  |  |  |
| * | 6. Were pole relocations in conflict with proposed sidewalks and ada requirements? |  |  |  |  |  |
| * | 7. Was railroad coordination in progress as required? |  |  |  |  |  |
| * | 8. Did the structures fit in the R/W? |  |  |  |  |  |
| F. Environmental |  |  |  |  |  |
| * | 1. Had Environmental restrictions period impacts been identified? |  |  |  |  |  |
| * | 2. Had all permit requirements been met? Rule 5? |  |  |  |  |  |
| * | 3. Were dust and noise control measures identified? |  |  |  |  |  |
| * | 4. If the work is located adjacent to a residential area or occupied building, were there provisions to minimize the impact of noise producing activities, such as restricted work hours or temporary noise barriers. |  |  |  |  |  |
| * | 5. Were required environmental permits identified & applications drafted? Hazardous Materials Investigative Report? |  |  |  |  |  |
| * | 6. Were there any Environmental active commitment instead of permits? |  |  |  |  |  |
| * | 7. Were the mitigation requirements identified & plans developed? |  |  |  |  |  |
| * | 8. If present, were historical structures identified on plans with clear instruction on limitations and handling? |  |  |  |  |  |
| G. Right of Way |  |  |  |  |  |
| * | 1. Sufficient R/W available for all operations? |  |  |  |  |  |
| * | 2. Was temporary R/W for construction access identified? |  |  |  |  |  |
| * | 3. Was there sufficient R/W to relocate all utilities? |  |  |  |  |  |
| * | 4. Was the required R/W been identified and sufficient for the project and all necessary construction operations? |  |  |  |  |  |
| Evaluation Criteria | Y | N | N/A | Note | Flag |
| * | 5. Access to work areas? |  |  |  |  |  |
| * | 6. Was there sufficient r/w to construct erosion control measures? |  |  |  |  |  |
| H. Construction Phasing |  |  |  |  |  |
| * | 1. Were work zone widths adequate for construction equipment needs? |  |  |  |  |  |
| * | 2. Were there grade changes between phases that restricted access to adjacent properties? |  |  |  |  |  |
| * | 3. Was there enough horizontal clearance for barriers, shoring, and construction access? |  |  |  |  |  |
| * | 4. Were proposed construction phases appropriate and constructible? |  |  |  |  |  |
| * | 5. Was there Unique Special Revisions required by the construction phasing? |  |  |  |  |  |
| * | 6. Was there areas with restricted access? |  |  |  |  |  |
| * | 7. Were travel lanes adequate? Width? Number? Wide Loads? |  |  |  |  |  |
| * | 8. Did staging cause special conditions (i.e. structural adequacy/stability)? If shoulders were required to carry traffic during stage construction, were they structurally adequate or was reconstruction required? |  |  |  |  |  |
| * | 9. Were there proposed adjacent contracts, restrictions, constraints identified and accounted for? |  |  |  |  |  |
| * | 10. Did traffic signal preformed loops work with phasing? |  |  |  |  |  |
| * | 11. Did proposed drainage function during construction phases? |  |  |  |  |  |
| I. Traffic Maintenance & Traffic Management Plans |  |  |  |  |  |
| * | 1. Emergency vehicle travel through closure areas? |  |  |  |  |  |
| * | 2. “Drop offs” due to construction phasing addressed to safely maintain traffic lanes? |  |  |  |  |  |
| * | 3. Were pedestrian, bicycle, ADA needs considered? |  |  |  |  |  |
| * | 4. Were exits and entrances to work zones adequate and safe? |  |  |  |  |  |
| * | 5. Was detour necessary for averting delays/congestion? |  |  |  |  |  |
| * | 6. Was there adequate vertical clearance in all phases of the MOT? |  |  |  |  |  |
| * | 7. Were approach and driveway grade appropriate and was construction phasing and property owner access provided? |  |  |  |  |  |
| Evaluation Criteria | Y | N | N/A | Note | Flag |
| * | 8. Adequate turn lanes provided to avoid traffic backups? |  |  |  |  |  |
| * | 9. Did the TMP adequately address site conditions and traffic volumes? |  |  |  |  |  |
| * | 10. Did the MOT plan address adequate work area for construction operations? |  |  |  |  |  |
| * | 11. Were conflicts with other work in area of project addressed? |  |  |  |  |  |
| * | 12. Did signing meet traffic needs in each phase? |  |  |  |  |  |
| * | 13. Were work zones large enough for equipment access? |  |  |  |  |  |
| J. Schedule & Special Considerations |  |  |  |  |  |
| * | 1. Was letting schedule appropriate for desired completion date? |  |  |  |  |  |
| * | 2. Did schedule address other work in area or related contracts in project? |  |  |  |  |  |
| * | 3. Did schedule address environmental restriction periods? |  |  |  |  |  |
| * | 4. Did schedule address local events, holidays, etc.? |  |  |  |  |  |
| * | 5. Did schedule address utility relocation timeline? |  |  |  |  |  |
| Note No. | REVIEWER COMMENTS |
| Note No. | REVIEWER COMMENTS |
| (Attach additional sheets as necessary) |
| Note No. | DESIGNER COMMENTS |
| (Attach additional sheets as necessary) |