## Slide 1: US 24 at C.R. 600 East and Logansport Road J-Turn Intersection Improvement
Tuesday, June 27, 2017

## Slide 2: Welcome
Purpose/explanation of public information meeting
Public information meeting format
Visit our sign-in table
Informational handouts
Submitting written public comments
Project display area

## Slide 3: Welcome
Introduction of INDOT Project Team
  Project Management
  Public Involvement
  LaPorte District – INDOT Regional Office
  Environmental Services
  Design
Recognition of elected and local public officials
Sign-in at attendance table to be added to project mailing list
Announcement of this public information meeting was posted to INDOT website
Media release issued
Local and elected officials notified
A copy of presentation and project documentation is available on-line via INDOT website

## Slide 4: Project Stakeholders
Indiana Department of Transportation
Indiana Division Federal Highway Administration
Cass County & City of Logansport
Elected & Local officials
Residents and citizens
Commuters
Businesses
Emergency services
Schools
Churches
Community Organizations

## Slide 5: Project Development
Project Selection
Early Coordination
Environmental phase begins
Purpose & Need
Develop alternatives
Preliminary design phase
Release environmental document for public review and comment
Additional work to finalize environmental document and project design
Real Estate Acquisition
Construction
Public Information Meeting
Communicate project decision
Offer opportunity to request a public hearing
Public Involvement:

## Slide 6: Environmental Document
  National Environmental Policy Act (NEPA)
  Requires INDOT to analyze and evaluate the impacts of a proposed project to the natural and socio-economic environments
  NEPA is a decision-making process
    Purpose and Need
    Alternatives Screening
    Preferred Alternative
  Impacts are analyzed, evaluated and described in an environmental document
    What are the impacts this project might have on the community?
    How can impacts be avoided?
    Can impacts be minimized?
    Mitigation for impacts?
  Draft environmental document to be released for public involvement
    Will be available for review via public repositories

## Slide 7: Project Resource Locations
INDOT LaPorte District Office
  315 E. Boyd Boulevard, LaPorte, IN 46350
  Toll Free 1-855-464-6368
  LaPorteDistrictCommunications@indot.in.gov
  http://www.in.gov/indot/2705.htm
  Planning, Project Development/Delivery, Construction, Maintenance for Northwest Indiana
Logansport Public Library - 616 East Broadway, Logansport, IN 46947
INDOT Office of Public Involvement
  100 North Senate Avenue, Room N642, Indianapolis, IN 46204
  Phone (317) 232-6601
  rclark@indot.in.gov

## Slide 8: US 24 at C.R. 600 East and Logansport Road
Project purpose is to enhance intersection safety
Project Needed due to high crash rates
  Significant number of vehicular conflicts (crashes) occurring at each intersection
  U.S. 24 at C.R. 600
    43 crashes occurring between 2010 - 2016
  U.S. 24 at Logansport Road
    42 crashes occurring between 2010 - 2016

## Slide 9: Crash Data
Crash Data for U.S. 24 at C.R. 600 East (2010-2016) |  |  |  |  |  | 
SEVERITY |  |  |  |  |  | Total
Property damage |  |  |  |  |  | 12
Non-Incapacitating Injury |  |  |  |  |  | 15
Incapacitating Injury |  |  |  |  |  | 13
Fatal |  |  |  |  |  | 3
TOTAL |  |  |  |  |  | 43
Crash Data for U.S. 24 at Logansport Road (2010-2016) |  |  |  |  |  | 
SEVERITY |  |  |  |  |  | Total
Property damage |  |  |  |  |  | 20
Non-Incapacitating Injury |  |  |  |  |  | 18
Incapacitating Injury |  |  |  |  |  | 4
Fatal |  |  |  |  |  | 0
TOTAL |  |  |  |  |  | 42

## Slide 10: US 24 at C.R. 600 East
U.S. 24 at C.R. 600 East
  43 crashes between 2010 – 2016
  Number of fatal and incapacitating injury crashes (16); additional 15 non-capacitating crashes
    Traffic from C.R. 600E failing to yield to traffic on U.S. 24
    Traffic from C.R. 600E, after crossing the median, involved in crashes with U.S. 24 traffic

## Slide 11: U.S. 24 and C.R. 600 East

## Slide 12: U.S. 24 at C.R. 600 East

## Slide 13: US 24 at Logansport Road
U.S. 24 at Logansport Road
  42 crashes between 2010 - 2016
  Number of injury crashes (22)
    Traffic from Logansport Road failing to yield to U.S. 24 traffic
    Traffic from Logansport Road, after crossing the median, involved in crashes with U.S. 24 traffic

## Slide 14: U.S. 24 at Logansport Road

## Slide 15: U.S. 24 at Logansport Road

## Slide 16: J-Turn intersections enhance safety
  Crashes most often involve through movements and left turns being struck on the far side of the wide intersection.

## Slide 17: Alternatives Considered
No Build
  Would not improve safety at intersection
Signalized Intersection
  Signals are not warranted. Signal warrants are determined by the amount of traffic traveling in all directions at an intersection. Unwarranted signal may cause crashes, especially on a high speed, four-lane divided highway
Realign the cross-road to intersect at 90 degrees
  Both intersections are at a slight skew which contributes to the failure to yield. This would help and result in reduction of crashes, however would also involve significant real estate acquisition impact
Build a bridge
  Would reduce the number of crashes by eliminating conflict between U.S. 24, C.R. 600E and Logansport Road traffic. Significant real east acquisition impact, cost and does not allow for mobility between U.S. 24 and local roads
Build an interchange
  Would reduce crashes, however the crash reduction would be comparable to the reduction realized by a J-Turn intersection. Significant real estate acquisition impact and cost
J-Turn Intersection (Preferred Alternative)
  Meets purpose & need of project
  Enhances safety at intersection by eliminating or significantly reducing injury crashes

## Slide 18: J-Turn – INDOT Preferred Alternative
Left turns and crossing minor roads are made using U-turn movement on major road.
Left turns from major road are made under yield (as current)

## Slide 19: Benefits of J-Turns
Conflict points are dramatically reduced
Conventional
Intersection
J-Turn
Intersection

## Slide 20: Benefits of J-Turns
Improved Capacity
Reduced Intersection Delay
Low Cost relative to other improvement alternatives
  No additional Right-of-Way necessary
May delay the need for traffic signal or interchange

## Slide 21: Traffic Simulation – Example
North

## Slide 22: Recent Case Study
US 41 at SR 114, near Morocco, IN
First J-turn intersection in Indiana
Improvement needed to reduce injury accidents
New intersection alignment opened in May, 2015
Zero injury accidents in two years since opening
Before:
After:
US 41
SR 114
US 41
SR 114

## Slide 23: Project Schedule
Public Information Meeting: 6/27/17
  Public comments requested by 7/17/17
Draft NEPA document complete - Fall 2017
  Additional public involvement – offering opportunity to request a public hearing
NEPA Document and Design complete - Fall 2017
Construction: 2018

## Slide 24: Submit Public Comments
Submit public comments using the options described in first page of information packet:
  Public Comment Form
  Via e-mail
INDOT respectfully requests comments be submitted by Monday, July 17, 2017
All comments submitted will be reviewed, evaluated and given full consideration during decision making process.

## Slide 25: Next Steps
Public and project stakeholder input
  Submit comments via options described on page 1 of information packet
INDOT review and evaluation
  All comments are given full consideration during decision-making process
  Finalize/approve environmental document, complete project design
Communicate a decision
  INDOT will notify project stakeholders of decision
  Work through local media, social media outlets; paid legal notice
  Make project documents accessible via repositories
Questions? Contact Public Involvement Team

## Slide 26: Thank You
Please visit with the design team and INDOT project officials following the presentation and Q&A.
Project Open House
  Project maps, displays, real estate acquisition table, INDOT project team and informal Q & A
  INDOT LaPorte District page http://www.in.gov/indot/2705.htm
  LaPorteDistrictCommunications@indot.in.gov