## Slide 1
Hydraulics Updates to the IndianaDesign Manual
David Finley, PE
INDOT Hydraulics Engineer
dfinley@indot.in.gov
Mark Bailey, PE
Manager, INDOT Office of Hydraulics
mbailey1@indot.in.gov
March 8, 2017

## Slide 2: Updates to the IDM
How-to Information
Helpful set of presentations on the Office of Hydraulics website

## Slide 3: Updates to the IDM
Status of the current updates…
Mmmm…
It is done!

## Slide 4: Updates to the IDM
Bridge REPLACEMENT Updates…
ONE FOOT

## Slide 5: Updates to the IDM
Bridge REPLACEMENT Updates…

## Slide 6: Updates to the IDM
Bridge Replacement
Backwater…
First assess the existing backwater
Basic backwater criteria:
If the existing backwater is… | The allowable backwater will be…
> 3 feet | 3 feet or less
Between 0.14 and 3 feet | Match or improve existing
Less than 0.14 feet | Up to 0.14 feet
This can be affected by other factors →

## Slide 7: Updates to the IDM
Bridge Replacement
Backwater: Check velocity…
Requires judgment
Evidence of instability?
If the existing bridge is unstable, the average velocity in the proposed bridge waterway should be ≤ 1.5 * the downstream channel velocity.

## Slide 8: Updates to the IDM
Bridge Replacement
Backwater: U/S structures…

## Slide 9: Updates to the IDM
Bridge Replacement
Backwater: U/S structures…
Lowest adjacent land grade
“Target” water surface elevation
1 Foot

## Slide 10: Updates to the IDM
Bridge Replacement
Lowest adjacent land grade
Is the “Target” water surface elevation less than 1 foot of backwater?
Existing backwater
(More than 1 foot)
Backwater: U/S structures…

## Slide 11: Updates to the IDM
Bridge Replacement
Lowest adjacent land grade
“Target” water surface elevation = 1.5 feet of backwater. GOOD!
Existing backwater
(More than 1 foot)
Backwater: U/S structures…

## Slide 12: Updates to the IDM
Bridge Replacement
Lowest adjacent land grade
“Target” water surface elevation < 1.0 feet of backwater. OOPS!
Existing backwater
(More than 1 foot)
Backwater: U/S structures…
Proposed water surface elevation for 1.0 feet of backwater. Allowed!

## Slide 13: Updates to the IDM
Bridge Replacement
Backwater: Waterway areas…
Gross Waterway Area

## Slide 14: Updates to the IDM
Bridge Replacement
Backwater: Waterway areas…
Net Waterway Area

## Slide 15: Updates to the IDM
Bridge Replacement
Backwater: Waterway areas…
Request plans at: http://www.in.gov/indot/2345.htm

## Slide 16: Updates to the IDM
Bridge Replacement
Other Criteria: Freeboard…
Current criteria:
Ideal is 2’ or…
maybe 1’ or…
maybe 3’
New criteria:
What do I
need to
achieve?

## Slide 17: Updates to the IDM
Bridge Replacement
Other Criteria: Freeboard…
Goal: Meet the existing criteria
Three possibilities:
  The existing low structures is above the goal
  The existing low structure is in pressure flow
  The existing low structure is above the 1% EP elevation, but no pressure flow

## Slide 18: Updates to the IDM
Bridge Replacement
Other Criteria: Freeboard…
Matching existing freeboard
Debris issues?
Yes: Meet the current
criteria
0.81’

## Slide 19: Updates to the IDM
Bridge Replacement
Other Criteria: Freeboard…
Matching existing freeboard
Debris issues?
Yes: Meet the current
Criteria
No: Can match the PROFILE
0.81’

## Slide 20: Updates to the IDM
Bridge Replacement
Two-Span Structures

## Slide 21: Updates to the IDM
Culvert REPLACEMENT Updates…
Replacement in Kind…

## Slide 22: Updates to the IDM
Culvert REPLACEMENT Updates…
Replacement in Kind… Is now the main policy!

## Slide 23: Updates to the IDM
Culvert Replacement
Replacement in Kind… Is now the main policy!
Proposed backwater can be as much as 3 feet provided is less than the existing backwater
But what if an upstream structure would be affected? See the bridge design criteria…
Backwater…

## Slide 24: Updates to the IDM
Culvert Replacement
Existing Span
Other Criteria…
Existing Waterway Area
Span and
Waterway Area:
Proposed
≥
Existing
1% EP Water Surface

## Slide 25: Updates to the IDM
Culvert Replacement
Other Criteria…
Outlet Velocity ≤
1.5 x Channel Velocity
Does the pipe have a scour issue?

## Slide 26: Updates to the IDM
Culvert Replacement
Other Criteria…
Outlet Velocity ≤
1.5 x Channel Velocity
Exceptions:
  Minimum outlet velocity = 6.5 ft/sec
  1 foot of backwater

## Slide 27: Updates to the IDM
Culvert Replacement
Culvert Extension
If the culvert is extended, what happens to the headwater here?
The headwater elevation has to stay the same
Remember: HEADwater, not BACKwater
How to deal with that?

## Slide 28: Updates to the IDM
Culvert Replacement
Other Things…
When making a submittal, include the electronic files – and mention the version that is used.
Is there concern about downstream impacts?
Contact the Office of Hydraulics.

## Slide 29: Updates to the IDM
Inlet Spacing Design
50% Clogging Factor…
REQUIRED
NOT REQUIRED
Bridge deck drains
Sags with flanking inlets

## Slide 30: Updates to the IDM
Inlet Spacing Design
Flanking Inlets…
Required for curb and gutter sections.
Required for median and side ditches unless there is a good place for the water to go.

## Slide 31: Updates to the IDM
New set of standard drawings…
Cover is now based on pipe type and size
Pipe Cover

## Slide 32: Updates to the IDM
Find information on the INDOT Hydraulics website
http://in.gov/indot/3595.htm
More to come…
Culvert Lining and more…

## Slide 33
Hydraulics Updates to the IndianaDesign Manual
David Finley, PE
INDOT Hydraulics Engineer
dfinley@indot.in.gov
Mark Bailey, PE
Manager, INDOT Office of Hydraulics
mbailey1@indot.in.gov
March 8, 2017
THANKS