## Slide 1
NOVEMBER 2020
Asset Lifecycle Strategies
Pavement
Indiana
Department of Transportation

## Slide 2
Table of Contents
Glossary | 2
Background and Context | 4
Overview Of Asset Lifecycle Strategies | 8
Pavement Lifecycle Investment Planning | 10
Pavement Lifecycle Strategies | 20
Data & Data Governance Linkages | 31
Financial Analysis & Optimization of Strategies | 34
Pavement Treatment Types and Triggers | 39
Pavement Project Prioritization Rules | 51
Appendix | 54

## Slide 3
Glossary

## Slide 4
Glossary of Terms & Acronyms
HMA: Hot Mix Asphalt
IDM: Indiana Design Manual
IRI: International Roughness Index
KPI: Key Performance Indicator
Major S.: Major structural treatment
MS: Minor structural treatment
MPO: Metropolitan Planning Organization
O&M: Operations and Maintenance
OPEX: Operating and Maintenance Expenditures
NHS: National Highway System
NPC: Net Present Cost
NPV: Net Present Value
PCCP: Portland Cement Concrete Pavement
PMG: Program Management Group
PM: Preventive Maintenance Treatments
PQI: Pavement Quality Index
RUT: Rutting of pavement
SAMP: Strategic Asset Management Plan
SPMS: Scheduling Project Management System (INDOT’s project scheduling and tracking system)
STIP: Statewide Transportation Improvement Program
TAMP: Transportation Asset Management Plan
TIP: Transportation Improvement Program, managed by an MPO
TPM: Federal Highway Transportation Performance Measures
UBWC: Ultrathin Bonded Wearing Course
ADT: Average Daily Traffic
AADT: Annual Average Daily Traffic
AADTT: Annual Average Daily Truck traffic
CAPEX: Capital Expenditures
CPR: Concrete Pavement Restoration
DBA: Distress Box Area – represents % of pavement area with cracking based on Pathways (vendor) algorithms / processes
Des. Number: Designation Number, unique project identifier in SPMS
dTIMS: Deighton Total Infrastructure Management System
EFT: Executive Funds Team
FHWA: Federal Highway Administration
FY: Fiscal Year (Indiana’s fiscal year is July 1 through June 30)
GLOSSARY

## Slide 5
Background and Context

## Slide 6: Overview of INDOT’s Asset Management Program
Introduction
The Indiana Department of Transportation (INDOT) is responsible for the management of all state owned transportation assets within the State of Indiana, including roads and bridges. INDOT has developed a strategic, systematic, and disciplined approach to operate, maintain, and improve its physical assets. The goal of INDOT’s asset management program is to achieve and sustain a desired state of good repair over the lifecycle of the assets at a practical cost. By successfully implementing the asset management program, this will help ensure INDOT effectively maintains its infrastructure in the long term and achieves a safe, high-quality, and sustainable transportation network. The desired outcomes of INDOT’s asset management program are aligned to the service objectives outlined within INDOT’s Strategic Plan to help ensure road safety, enhance mobility, and achieve asset sustainability.
INDOT has established both short and long-term condition targets for bridges and pavement and has set forth 20-year bridge and pavement plans to achieve the desired states of good repair. Through the April 2017 passage of Next Level Indiana, championed by Governor Eric Holcomb, INDOT has received the necessary funding to support its asset management program and achieve steady and consistent improvement in its bridges and pavement. By improving bridge and pavement quality through implementation of the 20-year plan, this will improve safety along the transportation system, increase mobility, eliminate delays, and foster economic growth for the State.
BACKGROUND AND CONTEXT

## Slide 7: Purpose of the Asset Lifecycle Strategies
Objectives of the Asset Lifecycle Strategies
The purpose of the INDOT Asset Lifecycle Strategies is to document INDOT’s processes for making decisions on its bridge and pavement assets over the course of their lifecycles. The Asset Lifecycle Strategies demonstrate that INDOT is managing its bridges and pavement in an effective and cost-efficient manner, preparing lifecycle strategies based on an assessment of various treatment strategies, and selecting those treatment strategies that provide the lowest costs throughout the assets’ lifecycles while maintaining a minimum level of service and balancing risk.
The Asset Lifecycle Strategies intend to:
Provide an overview of INDOT’s lifecycle planning and investment decision-making processes for its assets;
Document the business rules and considerations used to determine treatment strategies;
Identify the various treatment types for consideration when preparing lifecycle strategies;
Consider both capital and operating expenditures;
Evaluate the costs associated with INDOT’s investment options; and
Demonstrate that INDOT has a strategy in place to help achieve its established condition targets for the transportation network at the lowest lifecycle cost.
BACKGROUND AND CONTEXT
Content of the Asset Lifecycle Strategies
The Asset Lifecycle Strategies provide an overview of INDOT’s lifecycle planning and decision-making processes and summarize INDOT’s investment strategies for the transportation network over the assets’ lifecycles. Key components of the Asset Lifecycle Strategies include the following:
    Overview of INDOT’s processes for preparing lifecycle strategies;
    A lifecycle cost analysis of various investment scenarios and their anticipated impacts on the assets’ conditions;
    Capital and O&M treatment strategies;
    Overview of processes for data governance;
    Pavement treatment categories and types;
    INDOT’s business rules and considerations when preparing lifecycle strategies;
    INDOT’s project prioritization and capital planning processes.

## Slide 8: The Asset Lifecycle Strategies and the Asset Management System
Operating Context of the Asset Lifecycle Strategies
The Asset Lifecycle Strategies for bridges and pavement are one component within INDOT’s overall “management system for asset management.” The asset management system includes all processes, policies, procedures, documents, and the supporting framework that enables the achievement of good practice asset management.
Such documents within the asset management system include INDOT’s Transportation Asset Management Plan (TAMP) and Strategic Asset Management Plan (SAMP). The TAMP describes the existing conditions of INDOT’s transportation network and identifies planned enhancements within the 10-year horizon for managing the State highway system. The SAMP summarizes the guiding principles and processes to support asset management planning and translates INDOT’s strategic objectives into asset management objectives. In turn, the Asset Lifecycle Strategies describe the decision-making processes and considerations for preparing bridge and pavement treatment strategies, providing a tactical approach to achieve the objectives and implement the improvement plans outlined in the TAMP and SAMP.
The Asset Lifecycle Strategies form a component of INDOT’s greater operating environment. Other documents that help establish INDOT’s strategic objectives and initiatives include INDOT Strategic Plan, Next Level Indiana, Multimodal Freight & Mobility Plan, and
BACKGROUND AND CONTEXT
INDOT’s Long-Range Transportation Plan. These documents establish INDOT’s long-term priorities for the transportation network, which translate to the asset management objectives and priorities outlined in the SAMP and TAMP. The Asset Lifecycle Strategies describe the decision-making processes used to prepare INDOT’s 20-year plans for bridges and pavement, developed in alignment with the priorities outlined in the SAMP and TAMP. In turn, these serve as the foundation for preparing INDOT’s capital program by establishing the priority projects for inclusion in the Statewide Transportation Improvement Program (STIP).

## Slide 9
Overview of Asset Lifecycle Strategies

## Slide 10: INDOT’s Process for Preparing Lifecycle Strategies
Chart: 
Chart: 
  Consistent with industry good practice, INDOT maintains bridge and pavement management systems to support management of the State’s bridges and pavement. INDOT’s bridge and pavement databases are known as BIAS and Roads and Highways, respectively. These store the asset inventory and condition data that then serve as the foundation for the lifecycle treatment modeling performed using Deighton’s Total Infrastructure Management System (dTIMS) software. The triggers, or criteria, used to determine treatment type and timing are captured in INDOT’s bridge and pavement treatment rules. Details surrounding the asset conditions and associated data attributes that trigger certain treatments are captured in these rules. Collectively, BIAS, Roads and Highways, dTIMS, and INDOT’s treatment rules form the Department’s bridge and pavement systems, which are required by Federal regulations. The outcome of various alternative pavement treatment strategies according to INDOT’s treatment rules can be visualized as depicted in the adjacent figures.
  Based on the bridge and pavement data stored in INDOT’s databases, and using the triggers and treatment logic, dTIMS software uses simulation modeling to forecast the deterioration for each asset and recommend treatments based on user-defined constraints, such as budgetary constraints and expected bridge and pavement performance. The dTIMS software then considers all potential eligible treatment strategies per asset, for all assets, and identifies an optimal benefit and cost strategy that provides the most cumulative benefit to the network (portfolio) when considering the known budgetary constraints.
OVERVIEW OF ASSET LIFECYCLE STRATEGIES
  Figure 1: Illustrative Lifecycle Strategies for Pavement
HMA A1 Asset Decay Curve
Do Nothing
Alternative
Preferred
HMA C2 Asset Decay Curve
Year
Do Nothing
Alternative
Preferred
Good
Fair
Poor
Poor
Fair
Good
0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65
Year
0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | 110 | 120

## Slide 11
Pavement Lifecycle Investment Planning

## Slide 12
Lifecycle Investment Planning
PAVEMENT LIFECYCLE INVESTMENT PLANNING
INDOT’s asset lifecycle strategies for asphalt and concrete pavement present an optimal sequencing of treatments while considering the costs and benefits of investments. INDOT’s lifecycle investment planning is based on an assessment of various treatment options and selection of those that provide the lowest costs throughout the asset’s lifecycle while maintaining the minimum required level of service and balancing risk.
To assess lifecycle costs, INDOT compares the costs of its preferred treatment strategy against a baseline alternative scenario and a do-nothing scenario. The alternative scenario represents if INDOT were to do only the minimum treatments required to maintain the required level of service over its lifecycle. The do-nothing scenario represents if INDOT were to perform zero treatments over the asset’s lifecycle. Both the net present cost (NPC) and equivalent annual cost (EAC) have been assessed for the preferred and alternative scenarios for the financial analysis. This cost assessment is conducted uniquely for asphalt and concrete type pavement and uniquely per roadway category and sub-category to reflect the differences in INDOT’s treatment strategies based on pavement material and roadway type.
The lifecycle investment planning presented here reflects INDOT’s overall asset strategies for asphalt and concrete pavement within each roadway category. As such, the asset strategies and lifecycle cost analyses have been developed based on theoretical conditions and assumptions. Strategies for specific pavement segments should be verified against actual field conditions and current data available.
Lifecycle Cost Analysis
Key Assumptions
+
+
+
+
    1 Preferred Scenario
    per roadway category and pavement type
    Strategies based on theoretical conditions
    4.5%
    Discount Rate
+
+
+
+
    HMA Treatments
    Pavement Preservation Treatments
    Preventive Maintenance Treatments
    Minor Structural Treatments
    Major Structural Treatments
+
+
+
+
    Alternative Scenario
    refers to the minimum required treatments performed over the lifecycle
    Capital
    + O&M
    Treatments included in lifecycle cost analysis
    PCCP Treatments
    Pavement Preservation Treatments
    Preventive Maintenance Treatments
    Major Structural Treatments
  Figure 2: Lifecycle Cost Analysis Assumptions

## Slide 13
PAVEMENT LIFECYCLE INVESTMENT PLANNING
Road Category |  | Sub-Category |  | Description
A | Interstates | A1 | Urban Interstates and High Volume Interstates | Interstate with average daily traffic >40,000
 |  | A2 | Rural Interstates | Interstate with average daily traffic <40,000
B | Freeways and Principal Arterials | B1 | Urban High Volume NHS Roads | Freeway or principal arterial with average daily traffic >5,000 per lane
 |  | B2 | Rural High Volume | Freeway or principal arterial with average daily traffic <5,000 per lane
C | Remaining Roads | C1 | Urban Low Volume | Any other INDOT-owned road with average daily traffic >5,000
 |  | C2 | Rural Low Volume | Any other INDOT-owned road with average daily traffic <5,000
Roadway Category Framework for Investment Planning
INDOT’s lifecycle strategies vary based on the pavement type (e.g., asphalt and concrete) and roadway category to reflect the unique service level requirements and needs, associated with each category. INDOT’s roadway category framework is comprised of six individual categories, which roll up to three groups: Interstates, Freeways and Principal Arterials, and Remaining Roads.
Capital and operating and maintenance (O&M) related target levels of service are assigned to each category, and, while targets may vary by category, they are uniform across the State, for each category. When preparing lifecycle strategies, INDOT assesses treatment options based on those that provide the lowest lifecycle costs while maintaining the level of service for the roadway category and balancing risk.
Table 1: Roadway Category Framework1
_____
1The framework provides general guidelines on INDOT’s roadway categories. The Districts have adjusted the thresholds within the roadway categories to account for corridor continuity and other factors. .

## Slide 14
Chart: Year
Lifecycle Strategy Financial Optimization – HMA A1
PAVEMENT LIFECYCLE INVESTMENT PLANNING
The following presents an illustrative asset lifecycle deterioration curve for HMA type pavement within A1 category roads, comparing the preferred, alternative, and do-nothing scenario against the impacts of each treatment scenario on the pavement’s condition over the asset’s lifecycle.
Do Nothing Scenario
Alternative Scenario
Preferred Scenario
Figure 3: Illustrative Asset Decay Curves, HMA A1
Preventive Maintenance Treatment
Minor Structural Treatment
Major Structural Treatment
0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65

## Slide 15
Chart: Year
Preventive Maintenance Treatment
Minor Structural Treatment
Major Structural Treatment
Lifecycle Strategy Financial Optimization – HMA A2
PAVEMENT LIFECYCLE INVESTMENT PLANNING
The following presents an illustrative asset lifecycle deterioration curve for HMA type pavement within A2 category roads, comparing the preferred, alternative, and do-nothing scenario against the impacts of each treatment scenario on the pavement’s condition over the asset’s lifecycle.
Do Nothing Scenario
Alternative Scenario
Preferred Scenario
Figure 4: Illustrative Asset Decay Curves, HMA A2
0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80

## Slide 16
Chart: Year
Preventive Maintenance Treatment
Minor Structural Treatment
Major Structural Treatment
Lifecycle Strategy Financial Optimization – HMA B1
PAVEMENT LIFECYCLE INVESTMENT PLANNING
The following presents an illustrative asset lifecycle deterioration curve for HMA type pavement within B1 category roads, comparing the preferred, alternative, and do-nothing scenario against the impacts of each treatment scenario on the pavement’s condition over the asset’s lifecycle.
Do Nothing Scenario
Alternative Scenario
Preferred Scenario
Figure 5: Illustrative Asset Decay Curves, HMA B1
0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90

## Slide 17
Chart: Year
Preventive Maintenance Treatment
Minor Structural Treatment
Major Structural Treatment
Lifecycle Strategy Financial Optimization – HMA B2
PAVEMENT LIFECYCLE INVESTMENT PLANNING
The following presents an illustrative asset lifecycle deterioration curve for HMA type pavement within B2 category roads, comparing the preferred, alternative, and do-nothing scenario against the impacts of each treatment scenario on the pavement’s condition over the asset’s lifecycle.
Preferred Scenario
Alternative Scenario
Do Nothing Scenario
Figure 6: Illustrative Asset Decay Curves, HMA B2
0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95

## Slide 18
Chart: Year
Lifecycle Strategy Financial Optimization – HMA C1
PAVEMENT LIFECYCLE INVESTMENT PLANNING
Preferred Scenario
Alternative Scenario
Do Nothing Scenario
The following presents an illustrative asset lifecycle deterioration curve for HMA type pavement within C1 category roads, comparing the preferred, alternative, and do-nothing scenario against the impacts of each treatment scenario on the pavement’s condition over the asset’s lifecycle.
Figure 7: Illustrative Asset Decay Curves, HMA C1
0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100

## Slide 19
Chart: Year
Lifecycle Strategy Financial Optimization – HMA C2
PAVEMENT LIFECYCLE INVESTMENT PLANNING
The following presents an illustrative asset lifecycle deterioration curve for HMA type pavement within C2 category roads, comparing the preferred, alternative, and do-nothing scenario against the impacts of each treatment scenario on the pavement’s condition over the asset’s lifecycle.
Do Nothing Scenario
Alternative Scenario
Preferred Scenario
Figure 8: Illustrative Asset Decay Curves, HMA C2
0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100 | 105 | 110 | 115 | 120

## Slide 20
Chart: Year
Normal Decay PQI | 100 | 99.8 | 99.4 | 98.8 | 98 | 97 | 95.8 | 94.4 | 92.8 | 91 | 89 | 87.2 | 85.5 | 83.9 | 82.4 | 81 | 79.7 | 78.5 | 77.4 | 76.4 | 75.5 | 74.6 | 73.7 | 72.8 | 71.9 | 71.2 | 70.5 | 69.8 | 69.1 | 68.4 | 67.9 | 67.4 | 66.9 | 66.4 | 65.9 | 65.6 | 65.3 | 65 | 64.7 | 64.4 | 64.3 | 64.2 | 64.1 | 64 | 63.9
Preferred PQI | 100 | 99.8 | 99.4 | 98.8 | 98 | 97 | 95.8 | 94.4 | 92.8 | 96.8 | 95.1 | 93.6 | 92.3 | 91.2 | 90.3 | 89.6 | 89.1 | 93.1 | 91.4 | 89.9 | 88.6 | 87.5 | 86.6 | 85.9 | 85.4 | 93.4 | 91.7 | 90.2 | 88.9 | 87.8 | 86.9 | 86.2 | 85.7 | 89.7 | 88 | 86.5 | 85.2 | 84.1 | 83.2 | 87.2 | 85.5 | 84 | 82.7 | 81.6 | 93.6
Alternative PQI | 100 | 99.8 | 99.4 | 98.8 | 98 | 97 | 95.8 | 94.4 | 92.8 | 91 | 89 | 87.2 | 85.5 | 83.9 | 95.9 | 94.2 | 92.7 | 91.4 | 90.3 | 89.4 | 88.7 | 88.2 | 87.7 | 87.2 | 86.7 | 86.2 | 85.7 | 85.2 | 84.7 | 96.7 | 95 | 93.5 | 92.2 | 91.1 | 90.2 | 89.5 | 89 | 88.5 | 88 | 87.5 | 87 | 86.5 | 86 | 85.5 | 97.5
Lifecycle Strategy Financial Optimization – PCCP
PAVEMENT LIFECYCLE INVESTMENT PLANNING
The following presents an illustrative asset lifecycle deterioration curve for PCCP-type pavement within A, B, and C category roads, comparing the preferred, alternative, and do-nothing scenario against the impacts of each treatment scenario on the pavement’s condition over the asset’s lifecycle.
Do Nothing Scenario
Alternative
Scenario
Preferred
Scenario
CPR
CPR Profiling
PCC Replacement
Figure 9: Illustrative Asset Decay Curves, PCCP
0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45

## Slide 21
Pavement Lifecycle Strategies

## Slide 22
Overview
  After evaluating all costs and impacts, the software produces an optimal benefit-cost effective list of recommended projects, considering the programmed funding constraints against anticipated benefits across the network. Outputs of the model are then evaluated and verified by INDOT’s roadway engineers, who incorporate their local knowledge of the pavements to approve or update the list of recommendations.
Overview of Pavement Lifecycle Strategy Development
INDOT develops lifecycle strategies for pavement within the inventory over a 20-year horizon, using roadway condition data collected annually and uploaded into the pavement management system for evaluation. Measurement of pavement deterioration considers the following condition factors:
PAVEMENT LIFECYCLE STRATEGIES
  The dTIMS model considers four factors related to the deterioration of the pavement:
    International Roughness Index (IRI)
    (roughness of the ride)
Distress Box Area (DBA) (percentage of cracking along the segmentation)
    Faulting (Used for PCCP only; refers to cracks in the pavement at the joints or cracks along the roadway).
1
2
4
3
1. | International Roughness Index (IRI)
2. | RUT (HMA measurement only)
3. | Distress Box Area (DBA) %
4. | Faulting (PCCP measurement only)
Based on the deterioration models and triggers, the system provides the optimal mix of treatment strategies that will enable the asset to achieve a state of good repair, measured by whether the asset has met the INDOT-established condition target. Eligible treatment types are broken down into three categories: Preventive maintenance, minor structural, and major structural. Subsequent work types are a function of these categories and pavement type (i.e., asphalt or concrete). The dTIMS model provides suggestions for both an initial treatment strategy that would address the performance gaps in the short-term and a subsequent treatment or ancillary strategy as part of the overall strategy. This is used to demonstrate the overall benefit to the network for the length of evaluation.
RUT
(depressions or grooves in the roadway; used for HMA only)
  The output of the dTIMS model provides a list of candidate projects, with associated benefit-cost effectiveness, for inclusion in the capital program.

## Slide 23
Pavement Lifecycle: Design Life Considerations
When preparing pavement lifecycle strategies, INDOT’s primary goal is to determine an asset strategy (e.g., sequencing of treatment activities) that yields the least cost of ownership to INDOT while balanced against risks and maintaining the required minimum level of service.
In developing its pavement strategies, INDOT takes into account the various treatment alternatives that will result in the pavement achieving a minimum acceptable design life. These recommended design lives for the treatments are documented within the Indiana Design Manual (IDM).
INDOT considers the recommended design lives of treatments when selecting treatments and preparing the asset strategies. However, the recommended design lives are only one factor considered when preparing pavement strategies. Further, there may be instances when additional treatments are required in order to achieve the minimum acceptable design life of the pavement. Pavement work types provided in the IDM are shown in the adjacent graphic; additional details on the minimum acceptable design life years per work type can be found in the Pavement Design section of the IDM.
PAVEMENT LIFECYCLE Strategies
Continuously Reinforced Concrete Pavement
PCCP
Chip Seal
Asphalt Crack Fill
Bonded or Unbonded Concrete Overlay
HMA Pavement
HMA Overlay on Rubblized PCCP
HMA Overlay on Cracked and Seated PCCP
HMA Overlay
(PM, MS, Structural)
Cold or Hot In-Place Recycling
Cold Central Plan Recycling
Ultrathin Bonded Wearing Course (UBWC)
Thin HMA Overlay
Microsurface Overlay
CPR Techniques
Full Depth Reclamation
Figure 10: Pavement Work Types within the Indiana Design Manual (IDM)
Recommend deletion of slide – Have more current list of treatment types on slide 40.

## Slide 24
  INDOT has established maintenance and customer response measures to meet their Service Levels for INDOT’s roadways and other assets. INDOT’s Service Level maintenance activities are categorized by the nature of activity and the cause for occurrence. This table represents INDOT’s cyclical maintenance activities, and their frequencies, that are programmed according to INDOT’s Maintenance Owner’s Manual. Interventions are categorized into four groups: Pavement, Roadside, Drainage, and Traffic.
 | Pavement Treatments |  |  |  |  | 
 | Roadway Type |  |  |  |  | 
Treatment | A1 | A2 | B1 | B2 | C1 | C2
Asphalt Crack Seal | Every 3 years | Every 3 years | Every 3 years | Every 3 years | Every 3 years | Every 3 years
Blading Shoulders |  |  | Every 3 years | Every 3 years | Every 3 years | Every 3 years
Clipping Shoulders | Every 3 Years | Every 3 years | Every 3 years | Every 3 years | Every 3 years | Every 3 years
Chip Seal |  |  |  |  |  | Every 6 years
Roadway Operations & Maintenance (O&M) Intervention Strategy
PAVEMENT LIFECYCLE Strategies
 | Roadside Treatments |  |  |  |  | 
 | Roadway Type |  |  |  |  | 
Treatment | A1 | A2 | B1 | B2 | C1 | C2
Mowing | 5 cycles | 3 cycles | 5 cycles | 2 cycles | 2 cycles | 2 cycles
Herbicide | Annual | Annual | Annual | Annual | Annual | Annual
Attenuator Inspection | Annual | Annual | Annual | Annual | Annual | Annual
Guardrail End Treatment Inspection | 4 Years | 4 Years | 4 Years | 4 Years | 4 Years | 4 Years
Litter Removal | Monthly | 5x per Year | Monthly | As Needed | As Needed | As Needed
Sweeping (Urban Areas) | Monthly | N/A | Monthly | N/A | 2x Year | N/A
Table 2: O&M Treatments and Frequencies1
_____
1O&M treatment frequencies are approximate and may be subject to change over the lifecycle of the asset. For detailed maintenance cycles by roadway category and pavement type, please refer to the Appendix.

## Slide 25
 | Traffic Treatments |  |  |  |  | 
 | Roadway Type |  |  |  |  | 
Treatment | A1 | A2 | B1 | B2 | C1 | C2
Sign Modernization | 20 Years | 20 Years | 20 Years | 20 Years | 20 Years | 20 Years
Panel Sign Inspection | 5 Years | 5 Years | 5 Years | 5 Years | 5 Years | 5 Years
Delineator/Reflector Maintenance | Annual | Annual | Annual | Annual | Annual | Annual
Re-Striping (Paint Markings) | Annual | Annual | Annual | Annual | Annual | Annual
Special Markings Inspection | Annual | Annual | Annual | Annual | Annual | Annual
Signal PM | 2x Year | 2x Year | 2x Year | 2x Year | 2x Year | 2x Year
Flasher PM | Annual | Annual | Annual | Annual | Annual | Annual
Signal Indication Replacement | 10 Years | 10 Years | 10 Years | 10 Years | 10 Years | 10 Years
Signal Overhead Inspection | 5 Years | 5 Years | 5 Years | 5 Years | 5 Years | 5 Years
Lighting Surveillance | Monthly | Monthly | Monthly | Monthly | Monthly | Monthly
Lighting Re-Lamp (HPS) | 2 Years | 3 Years | 2 Years | 3 Years | 3 Years | 3 Years
Lighting Re-Lamp (LED) | 15 Years | 15 Years | 15 Years | 15 Years | 15 Years | 15 Years
Operations & Maintenance Intervention Strategy (continued)
PAVEMENT LIFECYCLE Strategies
 | Drainage Treatments |  |  |  |  | 
 | Roadway Type |  |  |  |  | 
Treatment | A1 | A2 | B1 | B2 | C1 | C2
Pipe Inspection | 4 Years | 4 Years | 4 Years | 4 Years | 4 Years | 4 Years
Drain Cleaning2 | Annual |  | Annual |  | Annual | 
Underdrain Outlet Cleaning and Inspection | Annual | Annual | Annual | Annual | Annual | Annual
Table 2: O&M Treatments and Frequencies (continued)
_____
2Drain cleaning typically does not occur on A2, B2, and C2 category roads, as drain cleaning occurs in urban areas where storm sewers exist.

## Slide 26
Operating and capital funding requirements are derived from the application of the preferred lifecycle strategy for bridge and pavement assets. The following table presents INDOT’s planned maintenance activities for A1 roadway category pavement, depicted over a 12-year maintenance cycle, beginning and ending with resurfacing treatments. Operating interventions are depicted below the timeline graphic, and capital interventions are depicted above the timeline graphic. For detailed maintenance cycles, please refer to the Appendix.
Lifecycle Strategy – Pavement Maintenance Cycles
PAVEMENT LIFECYCLE STRATEGIES
Construction
(Year 0)
CAPEX Interventions
OPEX Interventions
Year 0
Year 3
Year 6
Year 9
Year 12
HMA Overlay, PM
(Year 12)
Crack Seal
Patching
Crack Seal
Blading Shoulders
Brush/Tree Removal
Culvert Work
Blading Shoulders
Clipping Shoulders
Spot Ditching
Brush/Tree Removal
Culvert Work
Blading Shoulders
Patching
Crack Seal
Clipping Shoulders
Spot Ditching
Brush/Tree Removal
Culvert Work
Clipping Shoulders
Spot Ditching
Figure 11: Pavement Maintenance Cycles, A1
_____
The purpose of the graphic is to depict maintenance strategies over a 12-year maintenance cycle. The graphic above is not intended to show all CAPEX and OPEX interventions over the course of the asset lifecycle and therefore does not extend beyond the first 12 years. Note that, over time, the maintenance cycle intervals decrease as the pavement age increases.

## Slide 27
The following table presents INDOT’s planned maintenance activities for A2 roadway category pavement, depicted over a 12-year maintenance cycle, beginning and ending with resurfacing treatments. Operating interventions are depicted below the timeline graphic, and capital interventions are depicted above the timeline graphic. For detailed maintenance cycles, please refer to the Appendix.
Lifecycle Strategy – Pavement Maintenance Cycles
PAVEMENT LIFECYCLE STRATEGIES
Construction
(Year 0)
CAPEX Interventions
OPEX Interventions
Year 0
Year 3
Year 6
Year 9
Year 12
HMA Overlay, PM
(Year 12)
Crack Seal
Patching
Crack Seal
Blading Shoulders
Brush/Tree Removal
Blading Shoulders
Clipping Shoulders
Spot Ditching
Brush/Tree Removal
Blading Shoulders
Patching
Crack Seal
Clipping Shoulders
Spot Ditching
Brush/Tree Removal
Clipping Shoulders
Spot Ditching
Figure 12: Pavement Maintenance Cycles, A2
_____
The purpose of the graphic is to depict maintenance strategies over a 12-year maintenance cycle. The graphic above is not intended to show all CAPEX and OPEX interventions over the course of the asset lifecycle and therefore does not extend beyond the first 12 years. Note that, over time, the maintenance cycle intervals decrease as the pavement age increases.

## Slide 28
The following table presents INDOT’s planned maintenance activities for B1 roadway category pavement, depicted over a 12-year maintenance cycle, beginning and ending with resurfacing treatments. Operating interventions are depicted below the timeline graphic, and capital interventions are depicted above the timeline graphic. For detailed maintenance cycles, please refer to the Appendix.
Lifecycle Strategy – Pavement Maintenance Cycles
PAVEMENT LIFECYCLE STRATEGIES
Construction
(Year 0)
CAPEX Interventions
OPEX Interventions
Year 0
Year 3
Year 6
Year 9
Year 12
HMA Overlay, PM
(Year 12)
Crack Seal
Patching
Crack Seal
Blading Shoulders
Brush/Tree Removal
Blading Shoulders
Clipping Shoulders
Spot Ditching
Brush/Tree Removal
Blading Shoulders
Patching
Crack Seal
Clipping Shoulders
Spot Ditching
Brush/Tree Removal
Clipping Shoulders
Spot Ditching
Figure 13: Pavement Maintenance Cycles, B1
_____
The purpose of the graphic is to depict maintenance strategies over a 12-year maintenance cycle. The graphic above is not intended to show all CAPEX and OPEX interventions over the course of the asset lifecycle and therefore does not extend beyond the first 12 years. Note that, over time, the maintenance cycle intervals decrease as the pavement age increases.

## Slide 29
The following table presents INDOT’s planned maintenance activities for B2 roadway category pavement, depicted over a 13-year maintenance cycle, beginning and ending with resurfacing treatments. Operating interventions are depicted below the timeline graphic, and capital interventions are depicted above the timeline graphic. For detailed maintenance cycles, please refer to the Appendix.
Lifecycle Strategy – Pavement Maintenance Cycles
PAVEMENT LIFECYCLE strategies
Construction
(Year 0)
CAPEX Interventions
OPEX Interventions
Year 0
Year 3
Year 6
Year 9
Year 12
HMA Overlay, PM
(Year 13)
Patching
Crack Seal
Blading Shoulders
Clipping Shoulders
Brush/Tree Removal
Culvert Work
Blading Shoulders
Patching
Crack Seal
Clipping Shoulders
Spot Ditching
Brush/Tree Removal
Culvert Work
Patching
Crack Seal
Blading Shoulders
Spot Ditching
Brush/Tree Removal
Culvert Work
Clipping Shoulders
Spot Ditching
Figure 14: Pavement Maintenance Cycles, B2
Crack Seal
Blading Shoulders
Clipping Shoulders
Spot Ditching
Brush/Tree Removal
Culvert Work
_____
The purpose of the graphic is to depict maintenance strategies over a 13-year maintenance cycle. The graphic above is not intended to show all CAPEX and OPEX interventions over the course of the asset lifecycle and therefore does not extend beyond the first 13 years. Note that, over time, the maintenance cycle intervals decrease as the pavement age increases.

## Slide 30
The following table presents INDOT’s planned maintenance activities for C1 roadway category pavement, depicted over a 15-year maintenance cycle, beginning and ending with resurfacing treatments. Operating interventions are depicted below the timeline graphic, and capital interventions are depicted above the timeline graphic. For detailed maintenance cycles, please refer to the Appendix.
Lifecycle Strategy – Pavement Maintenance Cycles
PAVEMENT LIFECYCLE strategies
Construction
(Year 0)
CAPEX Interventions
OPEX Interventions
Year 0
Year 3
Year 6
Year 9
Year 12
Year 15
HMA Overlay, PM
(Year 15)
Crack Seal
Blading Shoulders
Clipping Shoulders
Spot Ditching
Brush/Tree Removal
Culvert Work
Blading Shoulders
Patching
Crack Seal
Blading Shoulders
Spot Ditching
Brush/Tree Removal
Culvert Work
Clipping Shoulders
Patching
Crack Seal
Blading Shoulders
Clipping Shoulders
Brush/Tree Removal
Culvert Work
Spot Ditching
Figure 15: Pavement Maintenance Cycles, C1
Patching
Crack Seal
Clipping Shoulders
Spot Ditching
Brush/Tree Removal
Culvert Work
_____
The purpose of the graphic is to depict maintenance strategies over a 15-year maintenance cycle. The graphic above is not intended to show all CAPEX and OPEX interventions over the course of the asset lifecycle and therefore does not extend beyond the first 15 years. Note that, over time, the maintenance cycle intervals decrease as the pavement age increases.

## Slide 31
Operating and capital investments are derived from the application of the preferred lifecycle strategy for bridge and pavement assets. The following table presents INDOT’s planned maintenance activities for C2 roadway category pavement, depicted over a 20-year maintenance cycle, beginning and ending with resurfacing. Operating interventions are depicted below the timeline graphic, and capital interventions are depicted above the timeline graphic. For detailed maintenance cycles, please refer to the Appendix.
Lifecycle Strategy – Pavement Maintenance Cycles
PAVEMENT LIFECYCLE strategies
Construction
(Year 0)
CAPEX Interventions
OPEX Interventions
Year 0
Year 3
Year 6
Year 9
Year 12
Year 15
Year 18
Year 21
Chip Seal
Patching
Blade Shoulders
Clip Shoulders
Spot Ditching
Brush/Tree Removal
Culvert Work
HMA Overlay, PM
(Year 20)
Blade Shoulders
Clip Shoulders
Spot Ditching
Brush/Tree Removal
Culvert Work
Patching
Crack Seal
Clipping Shoulders
Spot Ditching
Brush/Tree Removal
Culvert Work
Patching
Crack Seal
Blade Shoulders
Spot Ditching
Brush/Tree Removal
Spot Ditching
Patching
Crack Seal
Blade Shoulders
Spot Ditching
Brush/Tree Removal
Clip Shoulders
Crack Seal
Chip Seal
Figure 16: Pavement Maintenance Cycles, C2
Crack Seal
Patching
Crack Seal
Blade Shoulders
Clip Shoulders
Brush/Tree Removal
Culvert Work
Clip Shoulders
Blade Shoulders
_____
The purpose of the graphic is to depict maintenance strategies over a 20-year maintenance cycle. The graphic above is not intended to show all CAPEX and OPEX interventions over the course of the asset lifecycle and therefore does not extend beyond the first 20 years. Note that, over time, the maintenance cycle intervals decrease as the pavement age increases.

## Slide 32
Data & Data Governance Linkages

## Slide 33: Overview of INDOT’s Data Governance Structure
Introduction
INDOT’s processes for managing its bridge and pavement data are supported by its data governance structure. The data governance structure provides a framework by which to manage INDOT’s data across the asset classes and includes key data processes along with roles and responsibilities for managing data. The data governance structure is intended to:
DATA & DATA GOVERNANCE LINKAGES
Executive Sponsor
A senior executive that provides guidance and ensures buy-in across the agency
Sub-Committees
Permanent committees that support long-term challenges and objectives (e.g., security, retention)
Working Groups
Temporary groups that support specific initiatives (e.g., need to integrate a system, need to share new data)
Set strategy, approve policy, arbitrate
Oversee Data Domains, define function specific policy, process, tool decision
Monitor data quality, enforce policies, manage inquiries
Implement system policies within systems, control access, manage data flows
Gov.
Council
Data
Trustees
Data
Stewards
System Custodians
Data
Producers
Execution
Oversight
Perform.
Data
Consumers
Follow policies and procedures, report integrity issues, attend trainings
INDOT’s governance structure is organized using a top-down approach, where key stakeholders are responsible for the oversight of data governance, execution of data governance standards and policies, and performance of data governance. The adjacent graphic visualizes INDOT’s data governance model.
Implement a standardized method of structuring and enhancing data across the asset classes and across INDOT’s various groups;
Create a network of INDOT staff focused on data quality and access;
Define roles and responsibilities for entering, processing, and managing data;
Document how data and information flows across INDOT’s groups and the interdependencies of data across the organization;
Institute a shift away from a systems-centric focus on data to a focus on data Domains (e.g., Asset Management, Maintenance Operations, Construction, Capital Programs, etc.).
Figure 17: INDOT Data Governance Model

## Slide 34: Asset Management Data Process Overview
The Asset Management Domain is divided into the following Sub-Domains: Bridges, Large Culverts and Structures; Pavement, Small Culverts and Drainage; Road Inventory; Roadway Features; Mobility; ADA; Environmental; and Engineering. Each of the aforementioned areas is managed by a Sub-Domain Steward, responsible for ensuring data standards are followed, policies are enforced, and data quality is monitored and controlled within his/her respective area. Throughout the lifecycle of the asset, the stewards validate the integrity of the data within each phase. In turn, the System Custodians are responsible for managing and executing the data policies and standards for the data systems and applications that house the data throughout the asset’s lifecycle.
The below graphic is an illustrative example of the Asset Management Domain flow of data and roles within the governance structure, using the Pavement Sub-Domain as an example. For more details on the specific roles, responsibilities, and processes for managing data, please refer to the Asset Management Data Governance Structure.
DATA & DATA GOVERNANCE LINKAGES
Pavement
Jason Lowther
Small Culverts & Drainage
Todd Shields
Road Inventory
Mark McMahan
Roadway Features
Asset Mgmt
Louis Feagans
Domain
Trustee
Sub-Domain
Steward
Oversees Data Domains; define function specific policy, process and tool decisions, oversight of data inquiries
Ensure standards are followed, enforce policies, monitor data quality, handle data inquiries, identify data issues
Note: Some Systems (and System Custodians) may span multiple Domains
Datasets
Sub-Stewards
Pavement Sections Planned
Pavement Sections
Pavement Histories
Validate integrity of data (standards, inquiries, QA/ QC for specific asset attributes)
Engineering
WMS
Mark Joseph
dTIMS
Todd Shields
SPMS
April Leckie
Site Manager
Melissa Shaw
Data Whse
Mike Dockery
CADD
Derrick Fuller
TBD
BIAS
Maricar Gonzalez
Systems with AM Data
System Custodian
Develop, maintain, and modify systems and applications in support of Data Domains and functions
Figure 18: Illustrative Asset Management Data Governance Flow, Pavement
ADA
Mobility
Environmental
Bridges, Large Culverts, Structures
Anne Rearick
Pavement Condition
Pavement Cores

## Slide 35
Financial Analysis & Optimization of Strategies

## Slide 36
Lifecycle Strategy Financial Optimization – HMA Cost Assumptions
For purposes of analyzing the costs associated with INDOT’s preferred strategies against alternative (i.e., do-minimum) strategies, more intensive CAPEX interventions are considered as well as routine, interval-based OPEX interventions. The table on the left lists the CAPEX intervention inputs used to conduct the financial analysis, including the assumed cost per treatment type per category. The table on the right lists the OPEX intervention inputs, which are equivalent across all categories.
FINANCIAL ANALYSIS & OPTIMIZATION OF STRATEGIES
HMA Financial Analysis Inputs – OPEX Interventions | 
Treatment Costs*: All Categories ($/yd2) | 
Chip Seal | $1.50
Crack Seal | $0.142
Blading | $0.005
Clipping | $0.045
HMA Financial Analysis Inputs: CAPEX Interventions | 
Treatment Costs: A1 and A2 Categories ($/yd2) | 
Preventive Maintenance Treatment | $30.00
Minor Structural Treatment | $55.00
Major Structural Treatment | $355.00
Treatment Costs: B1 and B2 Categories ($/yd2) | 
Preventive Maintenance Treatment | $22.00
Minor Structural Treatment | $50.00
Major Structural Treatment | $200.00
Treatment Costs: C1 and C2 Categories ($/yd2) | 
Preventive Maintenance Treatment | $22.00
Minor Structural Treatment | $50.00
Major Structural Treatment | $200.00
Table 3: HMA Financial Analysis Inputs for CAPEX and OPEX Interventions1
_____
1Costs are for illustrative purposes only and do not represent actual treatments, which vary based on the specific pavement. OPEX intervention cost assumptions are based on typical treatment family costs as captured in INDOT’s WMS (Work Management System) for direct (i.e., materials and labor) costs. CAPEX intervention cost assumptions are based on typical treatment family costs as they were applied in dTIMS analysis as of June 2020.
Spreadsheet provided with calculations so they can be updated if / when costs are revised

## Slide 37
Lifecycle Strategy Financial Optimization Results – HMA
INDOT compares the costs of the preferred treatment strategy against the alternative, do-minimum strategy, demonstrating how INDOT’s preferred strategies provide a lower lifecycle cost option than its do-minimum strategy.1 The table on the right lists the results of the analysis, comparing the net present costs and equivalent annual costs of the preferred versus alternative treatment strategies.
Applying a 4.5% discount rate, this analysis reviews costs only and does not consider benefits; thus, results are presented as Net Present Cost (NPC) or Equivalent Annual Cost (EAC), as opposed to a Net Present Value (NPV) or benefit-cost analysis.
This analysis assumes no change in OPEX interventions between the preferred and alternative scenarios. However, less frequent but more intensive CAPEX interventions are assumed for the alternative scenarios. See the illustrative asset decay curves in the Pavement Lifecycle Investment Planning Section for greater detail on assumed CAPEX interventions.
FINANCIAL ANALYSIS & OPTIMIZATION OF STRATEGIES
HMA Financial Analysis Results |  |  | 
A1 and A2 Categories |  |  | 
Category | Treatment Scenario | NPC ($/yd2) | EAC ($/yd2)
A1 | Preferred | $73.70 | $3.52
 | Alternative | $116.23 | $5.55
A2 | Preferred | $62.39 | $2.91
 | Alternative | $96.36 | $4.49
B1 and B2 Categories |  |  | 
Category | Treatment Scenario | NPC ($/yd2) | EAC ($/yd2)
B1 | Preferred | $43.45 | $2.00
 | Alternative | $54.09 | $2.49
B2 | Preferred | $38.66 | $1.77
 | Alternative | $47.26 | $2.16
C1 and C2 Categories |  |  | 
Category | Treatment Scenario | NPC ($/yd2) | EAC ($/yd2)
C1 | Preferred | $31.77 | $1.45
 | Alternative | $47.08 | $2.14
C2 | Preferred | $22.08 | $1.00
 | Alternative | $30.75 | $1.39
Table 4: HMA Financial Analysis Results2
_____
1While the preferred strategy may not always provide the lowest cost when considering levels of service, benefits, and risk factor, the preferred strategy provides the lowest cost for the purpose of the illustrative financial optimization graphs.
2Costs are for illustrative purposes only and do not represent actual treatments, which vary based on the specific pavement.
Costs will need to be updated if unit cost inputs change

## Slide 38
Lifecycle Strategy Financial Optimization Results – PCCP
As with HMA, INDOT compares the costs of the preferred treatment strategy for concrete against an alternative, do-minimum strategy. The table on the left lists the inputs used for the concrete pavement financial analysis, and the table on the right lists the results of the analysis, comparing the net present costs and equivalent annual costs of the preferred versus alternative treatment strategies. This analysis also reviews costs only and does not consider benefits; thus, results are presented as Net Present Cost (NPC) or Equivalent Annual Cost (EAC), as opposed to a Net Present Value (NPV) or benefit-cost analysis. A 4.5% discount rate was applied in the analysis.
FINANCIAL ANALYSIS & OPTIMIZATION OF STRATEGIES
PCCP Financial Analysis Inputs | 
Treatment Costs: A Categories ($/yd2) | 
Concrete Pavement Restoration (CPR) | $50.00
Concrete Pavement Restoration (CPR): Profiling | $75.00
Concrete Pavement Replacement | $275.00
Treatment Costs: B, C Categories ($/yd2) | 
Concrete Pavement Restoration (CPR) | $50.00
Concrete Pavement Restoration (CPR): Profiling | $75.00
Concrete Pavement Replacement | $355.00
PCCP Financial Analysis Results |  |  | 
A, B, C Categories |  |  | 
Category | Treatment Scenario | NPC ($/yd2) | EAC ($/yd2)
A | Preferred | $136.45 | $7.12
 | Alternative | $253.46 | $13.23
B & C | Preferred | $147.49 | $7.70
 | Alternative | $327.20 | $17.08
While INDOT has prepared unique treatment strategies for each roadway sub-category for its asphalt pavement lifecycle cost analysis, for concrete pavement INDOT has prepared one preferred treatment strategy for all A category pavement (A1 and A2) and for all B and C category pavement and their associated sub-categories.
Similar to the asphalt pavements, this assumes less frequent but more intensive CAPEX interventions for the alternative scenarios. See the illustrative asset decay curves in the Pavement Lifecycle Investment Planning Section for greater detail on assumed CAPEX interventions.
Table 5: PCCP Financial Analysis Inputs and Results1
_____
1Costs are for illustrative purposes only and do not represent actual treatments, which vary based on the specific pavement.
Road Category Detail |  |  |  |  | 
Road Cat | CPR | HMA-PM | Minor Structural | Thin PCCP | Major / Replace
A1 | 23 | 26 | 42 |  | 185
A2 | 16 | 20 | 36 |  | 170
B1 | 15 | 17 | 33 | 40 | 150
B2 | 15 | 17 | 30 | 38 | 140
C1 | 14 | 17 | 27 | 36 | 60
C2 | 14 | 17 | 27 | 36 | 60
Small Town |  |  |  |  | 250
Based on Autumn’s comment from 11/16

## Slide 39
FINANCIAL ANALYSIS & OPTIMIZATION OF STRATEGIES
Lifecycle Strategy Financial Optimization – Network-Level Costs
Based on the preceding financial analysis and associated cost assumptions for the CAPEX and OPEX typical treatment family costs, approximate total equivalent annual costs (EAC) are provided by road category in the table below.
Roadway Category | CAPEX EAC | OPEX EAC | Total EAC | EAC Unit Costs ($/yd2)
A1 | $ 58,874,976 | $ 839,217 | $ 59,714,193 | $3.52
A2 | $ 53,599,758 | $ 927,655 | $ 54,527,412 | $2.91
B1 | $ 77,271,877 | $ 1,953,119 | $ 79,224,996 | $2.00
B2 | $ 59,081,217 | $ 1,984,410 | $ 61,065,627 | $1.77
C1 | $ 26,925,128 | $ 1,003,029 | $ 27,928,157 | $1.45
C2 | $ 54,283,441 | $ 13,643,645 | $ 67,927,086 | $1.00
Total EAC | $ 330,036,396 | $ 20,351,075 | $ 350,387,471 | 
Table 6: Total Equivalent Annual Costs (EAC) by Roadway Category1
_____
1Costs are for illustrative purposes only and do not represent actual treatments, which vary based on the specific pavement. Equivalent Annual Cost (EAC) is calculated based on costs per square yard. Estimates for costs per district and road category were based on INDOT’s lane mileage as of June 2020 assuming 7,040 square yards per lane mile.
.
Costs will need to be updated if unit cost inputs change

## Slide 40
Pavement Treatment Types and Triggers

## Slide 41
  Overview of the 20-Year Pavement Plan
  INDOT’s overall pavement strategies are developed using input from both INDOT’s long-range plans and short-term delivery programs. INDOT’s Multimodal Freight and Mobility Plan, Long-Range Transportation Plan, and Next Level Indiana plan identify INDOT’s long-term strategies over a 20-year horizon. These strategies serve as the foundation for developing INDOT’s shorter-term delivery programs, including the 5-Year Construction Plan and the Statewide Transportation Improvement Program (STIP).
  The 20-year Next Level Indiana plan, passed in April 2017, ensures that INDOT receives adequate funding to support its infrastructure investments for the upcoming 20 years. To achieve its condition targets for pavement and bridges, INDOT has established 20-year statewide treatment plans to support steady and consistent improvement in its pavement and bridges.
  The 20-year plan identifies INDOT’s projected Preventive maintenance, minor structural, and major structural treatments for its pavement assets through year 2040. The treatment categories and sequencing in the 20-year plan is then used to inform specific work types for the upcoming fiscal year as part of the annual capital call for projects. The adjacent figure lists the various intervention options identified within INDOT’s dTIMS, used to develop the upcoming fiscal year capital program during early pavement design collaboration. Treatments are listed in descending order, from least to greatest impact on the pavement.
PAVEMENT TREATMENT TYPES AND TRIGGERS
Overall Context of the 20-Year Plan Pavement Treatments
Patching
Crack Seal
Chip Seal
Pavement Preservation
Intersection Improvements
HMA Minor Structural
HMA Structural
HMA Replacement
Added Travel Lanes
New Road Construction
HMA Preventive Maintenance
Figure 19: 20-Year Plan Pavement Intervention Options in dTIMS
Expansion
Expansion

## Slide 42
Overview of Pavement Treatment Types
Pavement Types and Considerations
When preparing lifecycle strategies for pavement, the treatment types selected for pavement are based on a variety of factors, including project specific requirements and pavement type. INDOT pavement types include:
Aggregate: Consists of dense-graded compacted aggregate placed on a prepared subgrade, used on country roads, low-volume roads, State Parks, and occasionally in emergency situations on INDOT highways.
Asphalt: Typically consists of a Hot Mix Asphalt (HMA) surface course, on an HMA intermediate course, on either an HMA base or a compacted aggregate base, directly on a prepared subgrade. HMA surfaces comprise the majority of pavements seen on Indiana’s highway system.
Portland Cement Concrete Pavement (PCCP): Consists of concrete materials placed on a subbase for PCCP or dense subgrade, on a prepared subgrade. PCCP is typically used on the Interstate system, the NHS, or on state routes in high-volume traffic areas, such as areas with high truck volumes.
Composite: Consists of multiple pavement material types, for example HMA over PCCP or PCCP over asphalt.
The adjacent chart lists the major treatment categories for asphalt and concrete surfaces.
PAVEMENT TREATMENT TYPES AND TRIGGERS
Asphalt Treatment Categories
Pavement Preservation Treatments
Preventive Maintenance Treatments
Minor Structural Treatments
Major Structural Treatments
Pavement Preservation Treatments
Preventive Maintenance Treatments
Major Structural Treatments
Concrete Treatment Categories
Figure 20: Concrete and Asphalt Pavement Treatment Categories

## Slide 43
Treatment Categories: Hot Mix Asphalt (HMA)
The following summarizes the major pavement treatment categories for HMA pavement.
PAVEMENT TREATMENT TYPES AND TRIGGERS
Intended to preserve and extend the service life of existing good pavement.
Also considered a cost-effective technique that preserves the system, slows future deterioration, and maintains or improves functional condition without significantly increasing structural capacity.
Includes HMA mill and fill overlays, and hot in-place recycling.
Includes significant treatments to return existing HMA pavement to structural adequacy or replace pavement, if needed.
Includes treatments such as major structural overlays, pavement replacement, and pavement reconstruction.
The majority of major structural overlay projects add pavement structure with an overlay, including partial recycling of existing pavement, placement of additional surface materials, etc.
Intended to preserve and extend the service life of an existing good pavement.
Considered cost-effective treatments to an existing roadway system that preserve the system, slows future deterioration, and maintains or improves functional condition without significantly increasing structural capacity.
Includes crack sealing, fog seal, chip seal, scrub seal, and other Pavement Preservation Treatments.
Intended to extend the service life of pavement that has minor evidence of deterioration.
Preserves the system, slows future deterioration, and improves functional condition – may have a minor impact on structural capacity due to improved or added structural number.
Includes treatments such as cold in-place recycling, and HMA Overlay, Minor Structural.
Pavement Preservation Treatments
Preventive Maintenance (PM) Treatments
Minor Structural (MS) Treatments
Major Structural Treatments

## Slide 44
Treatment Categories: Portland Cement Concrete Pavement (PCCP)
The following summarizes the major pavement treatment categories for PCCP type pavement.
PAVEMENT TREATMENT TYPES AND TRIGGERS
Replacement of concrete pavement when concrete pavement is no longer structurally sufficient and has reduced serviceability.
Includes removal of existing PCCP type pavement structure and preparation of foundation and soil upgrade, if necessary, or recycle in case of rubblization, prior to placing a new pavement structure.
Includes unbonded concrete overlay.
May be used where the existing PCCP is structurally sufficient but has reduced serviceability.
Includes various treatments, such as partial or full depth patching and retrofit load transfer restoration.
CPR, Patching Only includes a full depth patching to PCCP type pavement.
CPR, Patching and Profiling includes a full depth patching and surface profiling to PCCP. For A road categories, this includes grooving. For B and C road categories, this includes diamond grinding only.
Preventive Maintenance (PM) Treatments
Major Structural Treatments
Intended to preserve and extend the service life of an existing good pavement.
Considered cost-effective treatments to an existing roadway system that preserve the system, slows future deterioration, and maintains or improves functional condition without significantly increasing structural capacity.
Includes crack sealing, profiling, joint sealing, and Concrete Pavement Preservation techniques.
Pavement Preservation Treatments

## Slide 45
Treatment Types by Category
Specific treatments within each of INDOT’s treatment categories include the following:
Crack Sealing : Cleaning and sealing of open cracks or joints in asphalt pavement and shoulders to prevent the entry of moisture and debris.
Fog Seal: Method of adding asphalt to an existing pavement surface to improve sealing or waterproofing, prevent further stone loss by holding aggregate in place, slow the age of hardening asphalt, and improve surface appearance. Typically performed in conjunction with chip sealing operations.
Seal Coat / Chip Seal / Scrub Seal: Treatment of pavement surface with liquid asphalt material and coarse aggregate to prevent deterioration of the surface, often called chip sealing. It provides waterproofing, low-severity crack sealing, and improved friction.
Micro-surface: Uses a thin, polymer-modified asphalt emulsion mixture to provide a new wearing course to arrest the oxidation of asphalt pavement, improve friction, or fill ruts.
Ultrathin Bonded Wearing Course (UBWC): Ultrathin bonded wearing course is a gap-graded, ultrathin HMA mixture applied over a thick polymer-modified asphalt emulsion membrane, used to seal the existing surface and produce high binder content at the interface of the existing roadway surface.
4.75 mm Surface: Consists of an asphalt mixture at 4.75 millimeters thickness placed over existing pavement surface.
1. Pavement Preservation
PAVEMENT TREATMENT TYPES AND TRIGGERS
2. Preventive Maintenance Treatments
HMA Overlay Preventive Maintenance: Process of grinding off the top layer of existing pavement and replacing with a new HMA surface (mill and fill overlay). Uses a single lift overlay.
Hot In-Place Recycling (HIR): Reuses existing materials and renews pavement through pavement recycling and reclaiming.
Concrete Pavement Restoration (CPR): May be used where the existing PCCP is structurally sufficient but has reduced serviceability. Includes various treatments, such as PCCP crack routing and sealing / cleaning and filling, PCCP joint sawing and sealing / cleaning and filling, retrofit load transfer restoration, surface profiling, partial or full depth patching, joint repairs, slab stabilization, slab jacking, joint or crack stitching, or precast concrete panels.

## Slide 46
Treatment Types by Category (continued)
HMA Overlay, Minor Structural: Treatments where HMA is laid over an existing pavement structure to repair minor damage or deterioration to the existing surface. Typically uses a two-lift overlay.
PCCP Crack and Seat and HMA Overlay: Consists of cracking the existing PCCP pavement and seating and providing an overlay with HMA based on MEPDG analysis.
Cold In-Place Recycling (CIR): Reuses existing materials and renews pavement through pavement recycling and reclaiming.
Thin-Bonded Concrete Overlay: Treatment where a thin layer of concrete is bonded directly to the pavement surface. Must have at least 3 inches of asphalt to be able to bond.
3. Minor Structural Treatments
PAVEMENT TREATMENT TYPES AND TRIGGERS
4. Major Structural Treatments
Pavement Reconstruction: Includes removal of existing pavement structure and preparation of foundation and soil subgrade prior to placing a new pavement structure.
Pavement Replacement: Includes removal of existing pavement structure and placement of new pavement structure.
Full-Depth Recycling: Recycling technique where the asphalt pavement and underlying materials are treated to produce a stabilized base course, using different types of additives. Includes widening and remixing the recycled material.
Cold Central Plant Recycling (CCPR): Pavement rehabilitation method that utilizes recycled materials.
PCCP Rubblization & HMA Overlay: Way to rehabilitate PCCP that has lost structural capacity through rubblization of existing pavement with an overlay with HMA based on MEPDG analysis.
Unbonded PCCP Overlay over Old PCCP: Overlays existing PCCP with an unbonded PCCP.
HMA Overlay, Major Structural: The majority of major structural overlay projects add pavement structure with an overlay, including partial recycling of existing pavement, placement of additional surface materials, etc. Includes at least three lifts of new HMA.

## Slide 47
Treatment Trigger Overview: Hot Mix Asphalt (HMA)
Treatment strategies for INDOT’s Hot Mix Asphalt (HMA) pavement are categorized by Preventive Maintenance, Minor Structural, and Major Structural activities. Treatments are recommended based on a series of triggers that prompt the need for the pavement’s treatment.
PAVEMENT TREATMENT TYPES AND TRIGGERS
The sequencing of treatments over the lifecycle of the pavement establishes INDOT’s overall asset lifecycle strategy for the pavement. Pavement strategies vary by roadway category to reflect the differing needs in the frequency and type of treatments performed based on the level of service and risk factor, coupled with the anticipated traffic.
Roughness of the pavement.
International Roughness Index (IRI)
Number of PMs the surface has received since the previous minor/major structural treatment
PM Count
    Age of the pavement since it was built or received a structural treatment.
Structural Age
Age of the surface of the pavement since it last received a Preventive maintenance or greater treatment.
Functional Age
Depressions or grooves in the roadway.
RUT
Roadway distress that can lead to potholes.
Cracking
(DBA)
Figure 21: HMA Pavement Treatment Triggers

## Slide 48
Treatment Triggers: Hot Mix Asphalt (HMA)
INDOT’s pavement strategies vary by road category and include Preventive maintenance, minor structural, and major structural treatments. Preventive maintenance activities are primarily triggered by timing and are performed at specific intervals. Each Preventive maintenance adds functionality to the pavement as a result of the improvement activity. Over time, the interval between Preventive maintenance decreases reflecting the effectiveness of the treatment as the pavement increases in age.
While Preventive maintenance treatments are prompted by timing, condition factors such as evidence of increased roughness in the pavement (IRI) or evidence of cracking in the pavement (DBA) are separate criteria that may prompt earlier treatments if the deterioration is occurring at a faster rate than design expectations. The treatment intervals that prompt Preventive maintenance treatments also vary based on the roadway category and traffic volume. For instance, the time intervals between initial Preventive maintenance is greater on C roadway category pavement than an A roadway category pavement, and time intervals between treatments may be greater for C2 (low-volume) type pavement than C1 (high-volume). This accounts for the differing needs in the frequency and type of treatments performed based on the level of service and risk factor and anticipated traffic volume on the pavement.
INDOT’s minor structural treatment activities are primarily triggered by timing and occur at various treatment intervals driven by the functional life of the treatment, decreasing in frequency overtime. Other triggers, including evidence of cracking (DBA), roughness of the pavement (IRI), and rutting (RUT), are separate criteria used to trigger early treatments if performance is worse than expected. As with Preventive maintenance activities, the triggers that prompt minor structural treatments vary based on the roadway category to reflect a desire to mitigate the need for a replacement in the timing that another roadway category would need. By performing the minor structural treatment, this helps commit to additional years of service for the pavement.
PAVEMENT TREATMENT TYPES AND TRIGGERS
Preventive Maintenance Triggers
Major structural treatments occur primarily due to the structural age of the pavement and occur following the application of Preventive maintenance and minor structural activities. Major structural treatments typically occur at a lower structural age for A categories than B and C categories. At a minimum, major structural treatments are considered when the pavement’s structural age is at least 60 years.
Minor Structural (MS) Triggers
Major Structural Triggers

## Slide 49
Treatment Trigger Overview: Portland Cement Concrete (PCCP)
Treatment strategies for INDOT’s PCCP include, but are not limited to, partial and full-depth patching, joint repair, surface profiling, joint sealing, major structural treatments, etc. PCCP profiling and grooving may also be included should roughness be a factor. Treatments are recommended based on a series of triggers that prompt the need for the pavement’s treatment.
PAVEMENT TREATMENT TYPES AND TRIGGERS
The sequencing of treatments over the lifecycle of the pavement establishes INDOT’s overall asset lifecycle strategy for the PCCP. Pavement strategies vary by roadway category to reflect the differing needs in the frequency and type of treatments performed based on the level of service, risk factor, and anticipated traffic.
Roughness of the PCCP.
International Roughness Index (IRI)
Number of profiling treatments performed over the structural life of the pavement. No more than two can be completed.
Profile Count
    Age of the pavement since it was built or received a structural treatment.
Structural Age
Displacement of pavement at the joints or cracks along the roadway.
Faulting
Roadway distress that can lead to potholes.
Cracking
(DBA)
Figure 22: PCCP Treatment Triggers

## Slide 50
Treatment Triggers: Concrete Pavement
Although Preventive maintenance treatments includes a variety of concrete pavement restoration treatments (e.g., full or partial-depth patching, joint repair, surface profiling, etc.), for the purposes of preparing its asset strategies, INDOT assumes the PM’s will entail full-depth patching or a combination of full-depth patching and profiling. When treatments are patching only, the primary triggers that prompt treatment are timing/ the age of the pavement. Secondary factors include evidence of cracking and the profile count. Patching typically occurs in intervals between six and ten years, with the length of time between patching decreasing overtime reflecting the effectiveness of the treatment as the pavement increases in age. Patching treatment has a positive impact on the pavement’s surface by reducing evidence of cracking, repairing individual distress in the pavement.
Patching and profiling includes both a full-depth patching and profiling. For pavement within A roadway categories, this includes grooving, whereas only diamond grinding is included for pavement within the B and C categories. Patching and profiling treatments are primarily triggered by the pavement’s roughness and timing. Secondary factors include evidence of cracking the pavement and the profile count. Patching and profiling positively impacts the condition of the pavement by reducing the pavement’s roughness, evidence of cracking, and faulting.
PAVEMENT TREATMENT TYPES AND TRIGGERS
Preventive Maintenance Treatments
Replacement or major structural treatments of PCCP type pavement is driven primarily by timing, measured in the structural age of the pavement. This typically occurs when the pavement’s structural age is at least 45 years for all roadway categories. Concrete major structural treatment positively impacts the condition of the pavement, and INDOT’s concrete asset strategies assumes this treatment resets the pavement’s roughness, cracking, and faulting levels.
Major Structural Treatments

## Slide 51
Overview of Pavement Asset Strategies
PAVEMENT TREATMENT TYPES AND TRIGGERS
INDOT’s asset lifecycle strategy for asphalt pavement includes a combination of O&M preservation treatments, followed by capital investments such as Preventive maintenance, minor structural, and major structural treatments. The sequencing of these treatments and frequency of occurrence varies based on the roadway category to account for the levels of service and risk factor associated with the roadway category, factoring the impact the treatment has on the pavement’s functional life and condition.
While the intervals between treatments differ for each roadway category and sub-category, overall, the general sequencing of treatments begins with pavement preservation treatments followed by Preventive maintenance. Typically, minor structural treatments occur as time elapses and the structural age of the pavement increases. Preventive maintenance treatments continue to occur throughout the lifecycle of the pavement, performed at an increasing rate of frequency over time. A major structural treatment occurs at the end of the treatment strategy, after all previously planned Preventive maintenance and minor structural treatments have occurred.
Hot Mix Asphalt (HMA) Asset Strategies
Asset lifecycle strategies for PCCP type pavement consists of a series of patching treatments, patching and profiling treatments, and major structural treatments and/or concrete pavement replacement. The sequencing and frequency of the treatment types is tailored based on the roadway category type and takes into account the impact of the treatments on the pavement’s condition.
Overall, the general sequencing of treatments for concrete pavement begins with a series of concrete pavement restoration patching treatments, followed by both patching and profiling when triggered by roughness. Patching treatments continue to occur on the pavement in intervals, corresponding to the structural age of the pavement. Finally, a major structural treatment or pavement replacement occurs at the end of the pavement’s treatment strategy after all previously planned concrete pavement restoration activities have occurred.
Concrete Pavement Asset Strategies

## Slide 52
Pavement Project Prioritization Rules

## Slide 53: Overview of Pavement Investment Decision-Making
Overview of Pavement Decision-Making
  INDOT’s Roadway Asset Team is responsible for establishing INDOT’s practices for developing the INDOT’s pavement investment strategy. INDOT uses data-driven decision making to identify cost-effective improvement projects for INDOT’s pavements, while meeting service levels and balancing the appropriate level of risk.
  INDOT begins its pavement investment decision-making process based on known budgetary constraints. Through Next Level Indiana, INDOT plans to invest an average of approximately $469 million annually over the next ten years (from FY20 to FY30) for its pavement preservation plan. INDOT has also developed budgetary forecasts for the upcoming five years using projections within the STIP, as well as estimates for the TAMP.
  INDOT uses the 20-year plan as the basis for its overall pavement asset strategy. From the 20-year plan, INDOT then develops an initial list of its pavement priorities using an optimized list of treatments provided by the pavement management system. The software uses simulation modeling to forecast pavement deterioration, identify potential performance gaps in relation to condition targets, and visualize the impacts of various alternative treatment strategies on the asset’s condition. The software considers all eligible treatment strategies to identify an optimal strategy for improving the condition of the portfolio. Based on user-defined costs, dTIMS develops cost estimates of treatments and produces a cost-effective strategy based on known budget constraints.
Decision-Making Criteria
Pavement Project Prioritization
  After identifying candidate projects recommended during the lifecycle cost analysis process, the Roadway Asset Team uses a project prioritization process to better understand how projects should be prioritized for the capital program. Scoring systems have been developed based on the pavement type to account for the individual needs of the surface type (e.g., asphalt versus concrete). INDOT reviews and updates its scoring methodology on an annual basis. INDOT uses project-level data on the condition and traffic to score pavement projects. Scoring of candidate projects are based on the following measures:1
Additionally, a Team Adjusted Priority Score is used to score any project where the data cannot illustrate, nor quantify, the condition and need. Based on the project scoring output, recommended projects are then considered for the capital program.
Cracking (DBA)
Truck Volume
Cost Effectiveness
Roadway Category
Roughness (IRI)
Pavement Scoring
_____
1Scoring rules evolve over time as INDOT reviews and updates its methodology.

## Slide 54: Pavement Project Prioritization for the Capital Program
PAVEMENT PROJECT PRIORITIZATION RULES
The Roadway Asset Team uses the aforementioned scoring criteria to assign project scores to candidate projects for the upcoming 5-year capital program. Based on the scores of each project, the Roadway Asset Team prepares a list of
projects recommended for programming in the capital program. INDOT leverages the following process to prepare the upcoming capital program:
Pavement Project Prioritization Process
  The Roadway Asset Team then reviews the list of recommended projects and evaluates projects based on purpose, need, and field knowledge. The Roadway Asset Team adapts or updates the recommended list, as needed.
  Project proposals are then submitted for review and statewide deliberation to the Asset Management Teams, to include members of the Central Office and Districts.
  Asset Management Teams review projects and create a prioritized list of recommended statewide projects based on need, project categories, priorities, funding limitations, and corridor planning.
  The Asset Management Teams then submit lists of recommended statewide projects to the Program Management Group (PMG) and Executive Funds Team (EFT) for review and approval. As part of this, the EFT divides available revenue among the Asset Management Teams based on estimated revenue for the 5-year program.
  The PMG provides final project recommendations for the capital program, and, following approval of the capital program, Districts are notified to input approved and funded projects into the Scheduling Project Management System (SPMS).
  The Roadway Asset Team uses the 20-year plan as the basis for developing an initial list of candidate projects, using the dTIMS pavement management system to develop and validate the plan. The model provides a summary of optimal project recommendations and treatment schedules based on a cost-benefit analysis of the candidate projects, given programmed funding constraints.
1
2
3
4
6
5

## Slide 55
Appendix

## Slide 56
Reference Materials
APPENDIX
For more details related to pavement asset lifecycle strategies and considerations for treatments, please refer to the following documents:
Indiana Design Manual, Part 6 (January 2020): Details INDOT’s Pavement Design considerations, including project categories and pavement types, pavement project elements, and lifecycle pavement cost analysis considerations. .
Indiana Department of Transportation, Transportation Asset Management Plan (August 2019):
  Managing Bridges (4-1): Includes INDOT’s pavement inventory; condition summary; process for network lifecycle planning; lifecycle cost analysis overview; process for developing INDOT’s pavement investment strategy; and project prioritization process.
  Appendix B: Provides tables of pavement treatments, condition triggers, and resets that comprise the decision trees within dTIMS.
  Appendix C: Provides a complete listing of all treatment types found in INDOT’s Scheduling Project Management System (SPMS) for pavement projects that correspond to the five FHWA work type categories.
INDOT Roadway Asset Scoring Rules (Revised October 2019): Includes project scoring rules for HMA and concrete pavement.
INDOT’s Pavement Deterioration and Triggers (March 2020): Spreadsheet that lists treatment triggers and resets for HMA and PCCP type pavement by roadway category and provides asset strategies for each pavement type and roadway category.

## Slide 57
HMA Treatment Triggers: A1 Category
 | Triggers |  |  |  |  |  |  | 
Treatment | IRI | RUT | DBA | PM Count | Functional Age | Cost | Time (Structural Age) | Reason for Treatment
Preventive Maintenance Treatments |  | <= 0.30 |  | <1 | >= 12 | $30 / square yard | < 30 | Timing
 |  | <= 0.30 |  | <1 | >= 11 |  | 30 – 50 | Timing
 |  | <= 0.30 |  | <1 | >= 10 |  | >50 | Timing
 | >120 | <= 0.30 |  | <1 | >= 8 |  |  | Roughness
 |  | <= 0.30 | >= 20 | <1 | >= 8 |  |  | Cracking
Minor Structural Treatments |  |  |  | >= 1 | >= 11 | $55 / square yard | < 30 | Timing
 |  |  |  | >= 1 | >= 11 |  | 30 – 50 | Timing
 |  |  |  | >= 1 | >= 11 |  | >50 | Timing
 |  | >0.30 |  |  |  |  |  | Rutting
 | >120 |  |  | >= 1 | >= 8 |  |  | Roughness
 |  |  | >= 20 | >= 1 | >= 8 |  |  | Cracking
Major Structural Treatments |  |  |  |  | >= 8 | $355 / square yard | >= 60 | 
APPENDIX
Table 7: HMA Treatment Triggers for A1 Roadway Category1
_____
1The costs of treatments and timing of treatment triggers will be updated as INDOT staff continue to review and update data.
.

## Slide 58
HMA Treatment Triggers: A2 Category
 | Triggers |  |  |  |  |  |  | 
Treatment | IRI | RUT | DBA | PM Count | Functional Age | Cost | Time (Structural Age) | Reason for Treatment
Preventive Maintenance Treatments |  | <= 0.30 |  |  | >= 12 | $30 / square yard | <= 30 | Timing
 |  | <= 0.30 |  | < 1 | >= 11 |  | 31 – 49 | Timing
 |  | <= 0.30 |  | < 1 | >= 10 |  | 50 – 69 | Timing
 | > 120 | <= 0.30 |  |  | >= 9 |  | <= 30 | Roughness
 |  | <= 0.30 | >= 20 |  | >= 9 |  | <= 30 | Cracking
 | > 120 |  |  | < 1 | >= 9 |  | > 30 | Roughness
 |  |  | >= 20 | < 1 | >= 9 |  | > 30 | Cracking
Minor Structural Treatments |  |  |  | >= 1 | >= 12 | $50 / square yard | 31 – 49 | Timing
 |  |  |  | >= 1 | >= 10 |  | 50 – 69 | Timing
 | > 120 |  |  | >= 1 | >= 9 |  |  | Roughness
 |  | > 0.30 | >= 20 | >= 1 | >= 9 |  |  | Cracking
 |  |  |  |  |  |  |  | Rutting
Major Structural Treatments |  |  |  | 1 | >= 8 | $275 / square yard | >= 70 | 
APPENDIX
Table 8: HMA Treatment Triggers for A2 Roadway Category

## Slide 59
HMA Treatment Triggers: B1 Category
 | Triggers |  |  |  |  |  |  | 
Treatment | IRI | RUT | DBA | PM Count | Functional Age | Cost | Time (Structural Age) | Reason for Treatment
Preventive Maintenance Treatments |  | <= 0.30 |  | < 2 | >= 12 | $22 / square yard | <= 40 | Timing
 |  | <= 0.30 |  | < 2 | >= 11 |  | 41 – 59 | Timing
 |  |  |  | < 2 | >= 10 |  | 60 – 79 | Timing
 | > 150 | <= 0.30 |  | < 2 | >= 9 |  |  | Roughness
 |  | <= 0.30 | >= 60 | < 2 | >= 9 |  |  | Cracking
Minor Structural Treatments |  |  |  | >= 2 | >= 12 | $50 / square yard | <= 60 | Timing
 |  |  |  | >= 2 | >= 10 |  | 61 – 79 | Timing
 | > 150 | <= 0.30 |  | >= 2 | >= 9 |  |  | Roughness
 |  | <= 0.30 | >= 60 | >= 2 | >= 9 |  |  | Cracking
 |  | > 0.30 |  |  |  |  |  | Rutting
Major Structural Treatments |  |  |  |  | >= 8 | $200 / square yard | >= 80 | 
APPENDIX
Table 9: HMA Treatment Triggers for B1 Roadway Category

## Slide 60
HMA Treatment Triggers: B2 Category
 | Triggers |  |  |  |  |  |  | 
Treatment | IRI | RUT | DBA | PM Count | Functional Age | Cost | Time (Structural Age) | Reason for Treatment
Preventive Maintenance Treatments |  | <= 0.30 |  | < 2 | >= 13 | $22 / square yard | <= 60 | Timing
 |  | <= 0.30 |  | < 2 | >= 12 |  | 61 – 79 | Timing
 |  |  |  | < 2 | >= 10 |  | 80 – 87 | Timing
 | > 150 | <= 0.30 |  | < 2 | >= 10 |  |  | Roughness
 |  | <= 0.30 | >= 65 | < 2 | >= 10 |  |  | Cracking
Minor Structural Treatments |  |  |  | >= 2 | >= 13 | $50 / square yard | <= 60 | Timing
 |  |  |  | >= 2 | >= 11 |  | 61 – 87 | Timing
 | > 150 | <= 0.30 |  | >= 2 | >= 10 |  |  | Roughness
 |  | <= 0.30 | >= 65 | >= 2 | >= 10 |  |  | Cracking
 |  | > 0.30 |  |  |  |  |  | Rutting
Major Structural Treatments |  |  |  |  | >= 8 | $140 / square yard | >= 88 | 
APPENDIX
Table 10: HMA Treatment Triggers for B2 Roadway Category

## Slide 61
HMA Treatment Triggers: C1 Category
 | Triggers |  |  |  |  |  |  | 
Treatment | IRI | RUT | DBA | PM Count | Functional Age | Cost | Time (Structural Age) | Reason for Treatment
Preventive Maintenance Treatments |  | <= 0.30 |  | < 2 | >= 15 | $22 / square yard | <= 55 | Timing
 |  | <= 0.30 |  | < 2 | >= 14 |  | 56 – 64 | Timing
 |  |  |  | < 2 | >= 12 |  | 65 – 94 | Timing
 | > 160 | <= 0.30 |  | < 2 | >= 12 |  |  | Roughness
 |  | <= 0.30 | >= 70 | < 2 | >= 12 |  |  | Cracking
Minor Structural Treatments |  |  |  | >= 2 | >= 15 | $50 / square yard | <= 55 | Timing
 |  |  |  | >= 2 | >= 11 |  | 56 – 94 | Timing
 | > 160 | <= 0.30 |  | >= 2 | >= 12 |  |  | Roughness
 |  | <= 0.30 | >= 70 | >= 2 | >= 12 |  |  | Cracking
 |  | > 0.30 |  |  |  |  |  | Rutting
Major Structural Treatments |  |  |  |  | >= 8 | $200 / square yard | >= 95 | Timing
APPENDIX
Table 11: HMA Treatment Triggers for C1 Roadway Category

## Slide 62
HMA Treatment Triggers: C2 Category
 | Triggers |  |  |  |  |  |  | 
Treatment | IRI | RUT | DBA | PM Count | Functional Age | Cost | Time (Structural Age) | Reason for Treatment
Preventive Maintenance Treatments |  | <= 0.30 |  | < 2 | >= 20 | $22 / square yard |  | Timing
 | > 180 | <= 0.30 |  | < 2 | >= 17 |  |  | Roughness
 |  | <= 0.30 |  | < 2 | >= 17 |  |  | Cracking
Minor Structural Treatments |  |  |  | >= 2 | >= 20 | $50 / square yard |  | Timing
 | > 180 | <= 0.30 |  | >= 2 | >= 17 |  |  | Roughness
 |  | <= 0.30 |  | >= 2 | >= 17 |  |  | Cracking
 |  | > 0.30 |  |  |  |  |  | Roughness
APPENDIX
Table 12: HMA Treatment Triggers for C2 Roadway Category

## Slide 63
PCCP Treatment Triggers: A Categories
 | Triggers |  |  |  |  |  |  | 
Treatment | IRI | Fault | DBA | Profile Count | Functional Age | Time (Structural Age) | Cost | Reason for Treatment
Pavement Preservation Treatments |  |  | > 5 |  |  | >= 10 | $40 / square yard | Timing
 |  |  | > 5 |  |  | >= 18 |  | 
 |  |  | > 5 |  |  | >= 26 |  | 
 |  |  | > 5 |  |  | >= 34 |  | 
 |  |  | > 5 |  |  | >= 40 |  | 
 |  |  | > 5 |  |  | >= 45 |  | 
Preventive Maintenance Treatments | > 120 |  | > 5 |  |  | >= 10 | $50 / square yard | Timing & Roughness
 | > 130 |  | > 5 | <= 2 |  | >= 26 |  | 
 | > 140 |  | > 5 | <= 2 |  | >= 34 |  | 
 | > 150 |  | > 5 | <= 2 |  | >= 40 |  | 
Major Structural Treatments |  |  |  |  |  | >= 50 | $275 / Square yard | Timing
APPENDIX
Table 13: PCCP Treatment Triggers for A Roadway Categories

## Slide 64
PCCP Treatment Triggers: B and C Categories
 | Triggers |  |  |  |  |  |  | 
Treatment | IRI | Fault | DBA | Profile Count | Functional Age | Time (Structural Age) | Cost | Reason for Treatment
Pavement Preservation Treatments |  |  | > 5 |  |  | >= 10 | $40 / square yard | Timing
 |  |  | > 5 |  |  | >= 18 |  | 
 |  |  | > 5 |  |  | >= 26 |  | 
 |  |  | > 5 |  |  | >= 34 |  | 
 |  |  | > 5 |  |  | >= 40 |  | 
 |  |  | > 5 |  |  | >= 45 |  | 
Preventive Maintenance Treatments | > 120 |  | > 5 |  |  | >= 10 | $50 / square yard | Timing & Roughness
 | > 130 |  | > 5 |  |  | >= 18 |  | 
 | > 130 |  | > 5 | <= 2 |  | >= 26 |  | 
 | > 140 |  | > 5 | <= 2 |  | >= 34 |  | 
 | > 150 |  | > 5 | <= 2 |  | >= 40 |  | 
Major Structural Treatments |  |  |  |  |  | > 55 | $275 / square yard | Timing
APPENDIX
Table 14: PCCP Treatment Triggers for B and C Roadway Categories

## Slide 65
Pavement Maintenance Cycles: A1 Category
APPENDIX
Table 15: Maintenance Cycles for A1 Roadway Category Pavement
Year | Resurface | Patching | Crack Seal | Seal Coat | Blading Shoulders | Clipping Shoulders | Brush and Tree Removal | Spot Ditching | Culvert Work
0 | X |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  | X |  | X | X | X | X | X
4 |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  |  | 
6 |  | X | X |  | X | X | X | X | X
7 |  |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  |  | 
9 |  | X | X |  | X | X | X | X | X
10 |  |  |  |  |  |  |  |  | 
11 |  |  |  |  |  |  |  |  | 
12 | X |  |  |  |  |  |  |  | 
13 |  |  |  |  |  |  |  |  | 
14 |  |  |  |  |  |  |  |  | 
15 |  |  | X |  | X | X | X | X | X
16 |  |  |  |  |  |  |  |  | 
17 |  |  |  |  |  |  |  |  | 
18 |  | X | X |  | X | X | X | X | X
19 |  |  |  |  |  |  |  |  | 
20 |  |  |  |  |  |  |  |  | 
21 |  | X | X |  | X | X | X | X | X
22 |  |  |  |  |  |  |  |  | 
23 |  |  |  |  |  |  |  |  | 
24 | X |  |  |  |  |  |  |  | 
25 |  |  |  |  |  |  |  |  | 
26 |  |  |  |  |  |  |  |  | 
27 |  |  | X |  | X | X | X | X | X
28 |  |  |  |  |  |  |  |  | 
29 |  |  |  |  |  |  |  |  | 
30 |  | X | X |  | X | X | X | X | X

## Slide 66
APPENDIX
Table 15: Maintenance Cycles for A1 Roadway Category Pavement (cont’d)
Year | Resurface | Patching | Crack Seal | Seal Coat | Blading Shoulders | Clipping Shoulders | Brush and Tree Removal | Spot Ditching | Culvert Work
31 |  |  |  |  |  |  |  |  | 
32 |  |  |  |  |  |  |  |  | 
33 |  | X | X |  | X | X | X | X | X
34 |  |  |  |  |  |  |  |  | 
35 |  |  |  |  |  |  |  |  | 
36 | X |  |  |  |  |  |  |  | 
37 |  |  |  |  |  |  |  |  | 
38 |  |  |  |  |  |  |  |  | 
39 |  |  | X |  | X | X | X | X | X
40 |  |  |  |  |  |  |  |  | 
41 |  |  |  |  |  |  |  |  | 
42 |  | X | X |  | X | X | X | X | X
43 |  |  |  |  |  |  |  |  | 
44 |  |  |  |  |  |  |  |  | 
45 |  | X | X |  | X | X | X | X | X
46 |  |  |  |  |  |  |  |  | 
47 | X |  |  |  |  |  |  |  | 
48 |  |  |  |  |  |  |  |  | 
49 |  |  |  |  |  |  |  |  | 
50 |  |  | X |  | X | X | X | X | X
51 |  |  |  |  |  |  |  |  | 
52 |  |  |  |  |  |  |  |  | 
53 |  | X | X |  | X | X | X | X | X
54 |  |  |  |  |  |  |  |  | 
55 |  | X | X |  | X | X | X | X | X
56 |  |  |  |  |  |  |  |  | 
57 | X |  |  |  |  |  |  |  | 
58 |  |  |  |  |  |  |  |  | 
59 |  |  |  |  |  |  |  |  | 
60 |  |  | X |  | X | X | X | X | X
61 |  |  |  |  |  |  |  |  | 
62 |  |  |  |  |  |  |  |  | 
63 |  | X | X |  | X | X | X | X | X
64 |  |  |  |  |  |  |  |  | 
65 | X |  |  |  |  |  |  |  | 

## Slide 67
Pavement Maintenance Cycles: A2 Category
APPENDIX
Table 16: Maintenance Cycles for A2 Roadway Category Pavement
Year | Resurface | Patching | Crack Seal | Seal Coat | Blading Shoulders | Clipping Shoulders | Brush and Tree Removal | Spot Ditching | Culvert Work
0 | X |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  | X |  | X | X | X | X | 
4 |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  |  | 
6 |  | X | X |  | X | X | X | X | 
7 |  |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  |  | 
9 |  | X | X |  | X | X | X | X | 
10 |  |  |  |  |  |  |  |  | 
11 |  |  |  |  |  |  |  |  | 
12 | X |  |  |  |  |  |  |  | 
13 |  |  |  |  |  |  |  |  | 
14 |  |  |  |  |  |  |  |  | 
15 |  |  | X |  | X | X | X | X | 
16 |  |  |  |  |  |  |  |  | 
17 |  |  |  |  |  |  |  |  | 
18 |  | X | X |  | X | X | X | X | 
19 |  |  |  |  |  |  |  |  | 
20 |  |  |  |  |  |  |  |  | 
21 |  | X | X |  | X | X | X | X | 
22 |  |  |  |  |  |  |  |  | 
23 |  |  |  |  |  |  |  |  | 
24 | X |  |  |  |  |  |  |  | 
25 |  |  |  |  |  |  |  |  | 
26 |  |  |  |  |  |  |  |  | 
27 |  |  | X |  | X | X | X | X | 
28 |  |  |  |  |  |  |  |  | 
29 |  |  |  |  |  |  |  |  | 
30 |  | X | X |  | X | X | X | X | 
31 |  |  |  |  |  |  |  |  | 
32 |  |  |  |  |  |  |  |  | 
33 |  | X | X |  | X | X | X | X | 
34 |  |  |  |  |  |  |  |  | 
35 |  |  |  |  |  |  |  |  | 

## Slide 68
APPENDIX
Table 16: Maintenance Cycles for A2 Roadway Category Pavement (cont’d)
Year | Resurface | Patching | Crack Seal | Seal Coat | Blading Shoulders | Clipping Shoulders | Brush and Tree Removal | Spot Ditching | Culvert Work
36 | X |  |  |  |  |  |  |  | 
37 |  |  |  |  |  |  |  |  | 
38 |  |  |  |  |  |  |  |  | 
39 |  |  | X |  | X | X | X | X | 
40 |  |  |  |  |  |  |  |  | 
41 |  |  |  |  |  |  |  |  | 
42 |  | X | X |  | X | X | X | X | 
43 |  |  |  |  |  |  |  |  | 
44 |  |  |  |  |  |  |  |  | 
45 |  | X | X |  | X | X | X | X | 
46 |  |  |  |  |  |  |  |  | 
47 |  |  |  |  |  |  |  |  | 
48 | X |  |  |  |  |  |  |  | 
49 |  |  |  |  |  |  |  |  | 
50 |  |  | X |  | X | X | X | X | 
51 |  |  |  |  |  |  |  |  | 
52 |  |  |  |  |  |  |  |  | 
53 |  | X | X |  | X | X | X | X | 
54 |  |  |  |  |  |  |  |  | 
55 |  |  |  |  |  |  |  |  | 
56 |  | X | X |  | X | X | X | X | 
57 |  |  |  |  |  |  |  |  | 
58 | X |  |  |  |  |  |  |  | 
59 |  |  |  |  |  |  |  |  | 
60 |  |  | X |  | X | X | X | X | 
61 |  |  |  |  |  |  |  |  | 
62 |  |  |  |  |  |  |  |  | 
63 |  | X | X |  | X | X | X | X | 
64 |  |  |  |  |  |  |  |  | 
65 |  |  |  |  |  |  |  |  | 
66 |  | X | X |  | X | X | X | X | 
67 |  |  |  |  |  |  |  |  | 
68 | X |  |  |  |  |  |  |  | 
69 |  |  |  |  |  |  |  |  | 
70 |  |  |  |  |  |  |  |  | 
71 |  |  | X |  | X | X | X | X | 
72 |  |  |  |  |  |  |  |  | 
73 |  |  |  |  |  |  |  |  | 
74 |  | X | X |  | X | X | X | X | 
75 |  |  |  |  |  |  |  |  | 
76 | X |  |  |  |  |  |  |  | 

## Slide 69
Pavement Maintenance Cycles: B1 Category
APPENDIX
Table 17: Maintenance Cycles for B1 Roadway Category Pavement
Year | Resurface | Patching | Crack Seal | Seal Coat | Blading Shoulders | Clipping Shoulders | Brush and Tree Removal | Spot Ditching | Culvert Work
0 | X |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  | X |  | X | X | X | X | 
4 |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  |  | 
6 |  | X | X |  | X | X | X | X | 
7 |  |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  |  | 
9 |  | X | X |  | X | X | X | X | 
10 |  |  |  |  |  |  |  |  | 
11 |  |  |  |  |  |  |  |  | 
12 | X |  |  |  |  |  |  |  | 
13 |  |  |  |  |  |  |  |  | 
14 |  |  |  |  |  |  |  |  | 
15 |  |  | X |  | X | X | X | X | 
16 |  |  |  |  |  |  |  |  | 
17 |  |  |  |  |  |  |  |  | 
18 |  | X | X |  | X | X | X | X | 
19 |  |  |  |  |  |  |  |  | 
20 |  |  |  |  |  |  |  |  | 
21 |  | X | X |  | X | X | X | X | 
22 |  |  |  |  |  |  |  |  | 
23 |  |  |  |  |  |  |  |  | 
24 | X |  |  |  |  |  |  |  | 
25 |  |  |  |  |  |  |  |  | 
26 |  |  |  |  |  |  |  |  | 
27 |  |  | X |  | X | X | X | X | 
28 |  |  |  |  |  |  |  |  | 
29 |  |  |  |  |  |  |  |  | 
30 |  | X | X |  | X | X | X | X | 
31 |  |  |  |  |  |  |  |  | 
32 |  |  |  |  |  |  |  |  | 
33 |  | X | X |  | X | X | X | X | 
34 |  |  |  |  |  |  |  |  | 
35 |  |  |  |  |  |  |  |  | 

## Slide 70
APPENDIX
Table 17: Maintenance Cycles for B1 Roadway Category Pavement (cont’d)
Year | Resurface | Patching | Crack Seal | Seal Coat | Blading Shoulders | Clipping Shoulders | Brush and Tree Removal | Spot Ditching | Culvert Work
36 | X |  |  |  |  |  |  |  | 
37 |  |  |  |  |  |  |  |  | 
38 |  |  |  |  |  |  |  |  | 
39 |  |  | X |  | X | X | X | X | 
40 |  |  |  |  |  |  |  |  | 
41 |  |  |  |  |  |  |  |  | 
42 |  | X | X |  | X | X | X | X | 
43 |  |  |  |  |  |  |  |  | 
44 |  |  |  |  |  |  |  |  | 
45 |  | X | X |  | X | X | X | X | 
46 |  |  |  |  |  |  |  |  | 
47 |  |  |  |  |  |  |  |  | 
48 | X |  |  |  |  |  |  |  | 
49 |  |  |  |  |  |  |  |  | 
50 |  |  |  |  |  |  |  |  | 
51 |  |  | X |  | X | X | X | X | 
52 |  |  |  |  |  |  |  |  | 
53 |  |  |  |  |  |  |  |  | 
54 |  | X | X |  | X | X | X | X | 
55 |  |  |  |  |  |  |  |  | 
56 |  |  |  |  |  |  |  |  | 
57 |  | X | X |  | X | X | X | X | 
58 |  |  |  |  |  |  |  |  | 
59 | X |  |  |  |  |  |  |  | 
60 |  |  |  |  |  |  |  |  | 
61 |  |  |  |  |  |  |  |  | 
62 |  |  | X |  | X | X | X | X | 
63 |  |  |  |  |  |  |  |  | 
64 |  |  |  |  |  |  |  |  | 
65 |  | X | X |  | X | X | X | X | 
66 |  |  |  |  |  |  |  |  | 
67 |  | X | X |  | X | X | X | X | 
68 |  |  |  |  |  |  |  |  | 
69 | X |  |  |  |  |  |  |  | 
70 |  |  |  |  |  |  |  |  | 
71 |  |  |  |  |  |  |  |  | 
72 |  |  | X |  | X | X | X | X | 
73 |  |  |  |  |  |  |  |  | 
74 |  |  |  |  |  |  |  |  | 
75 |  | X | X |  | X | X | X | X | 

## Slide 71
APPENDIX
Table 17: Maintenance Cycles for B1 Roadway Category Pavement (cont’d)
Year | Resurface | Patching | Crack Seal | Seal Coat | Blading Shoulders | Clipping Shoulders | Brush and Tree Removal | Spot Ditching | Culvert Work
76 |  |  |  |  |  |  |  |  | 
77 |  |  |  |  |  |  |  |  | 
78 |  | X | X |  | X | X | X | X | 
79 |  |  |  |  |  |  |  |  | 
80 | X |  |  |  |  |  |  |  | 
81 |  |  |  |  |  |  |  |  | 
82 |  |  |  |  |  |  |  |  | 
83 |  |  | X |  | X | X | X | X | 
84 |  |  |  |  |  |  |  |  | 
85 |  |  |  |  |  |  |  |  | 
86 |  | X | X |  | X | X | X | X | 
87 |  |  |  |  |  |  |  |  | 
88 | X |  |  |  |  |  |  |  | 

## Slide 72
Pavement Maintenance Cycles: B2 Category
APPENDIX
Table 18: Maintenance Cycles for B2 Roadway Category Pavement
Year | Resurface | Patching | Crack Seal | Seal Coat | Blading Shoulders | Clipping Shoulders | Brush and Tree Removal | Spot Ditching | Culvert Work
0 | X |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  | X |  | X | X | X | X | X
4 |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  |  | 
6 |  | X | X |  | X | X | X | X | X
7 |  |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  |  | 
9 |  | X | X |  | X | X | X | X | X
10 |  |  |  |  |  |  |  |  | 
11 |  | X | X |  | X | X | X | X | X
12 |  |  |  |  |  |  |  |  | 
13 | X |  |  |  |  |  |  |  | 
14 |  |  |  |  |  |  |  |  | 
15 |  |  |  |  |  |  |  |  | 
16 |  |  | X |  | X | X | X | X | X
17 |  |  |  |  |  |  |  |  | 
18 |  |  |  |  |  |  |  |  | 
19 |  | X | X |  | X | X | X | X | X
20 |  |  |  |  |  |  |  |  | 
21 |  |  |  |  |  |  |  |  | 
22 |  | X | X |  | X | X | X | X | X
23 |  |  |  |  |  |  |  |  | 
24 |  | X | X |  | X | X | X | X | X
25 |  |  |  |  |  |  |  |  | 
26 | X |  |  |  |  |  |  |  | 
27 |  |  |  |  |  |  |  |  | 
28 |  |  |  |  |  |  |  |  | 
29 |  |  | X |  | X | X | X | X | X
30 |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  |  |  | 
32 |  | X | X |  | X | X | X | X | X
33 |  |  |  |  |  |  |  |  | 
34 |  |  |  |  |  |  |  |  | 
35 |  | X | X |  | X | X | X | X | X

## Slide 73
APPENDIX
Table 18: Maintenance Cycles for B2 Roadway Category Pavement (cont’d)
Year | Resurface | Patching | Crack Seal | Seal Coat | Blading Shoulders | Clipping Shoulders | Brush and Tree Removal | Spot Ditching | Culvert Work
36 |  |  |  |  |  |  |  |  | 
37 |  | X | X |  | X | X | X | X | X
38 |  |  |  |  |  |  |  |  | 
39 | X |  |  |  |  |  |  |  | 
40 |  |  |  |  |  |  |  |  | 
41 |  |  |  |  |  |  |  |  | 
42 |  |  | X |  | X | X | X | X | X
43 |  |  |  |  |  |  |  |  | 
44 |  |  |  |  |  |  |  |  | 
45 |  | X | X |  | X | X | X | X | X
46 |  |  |  |  |  |  |  |  | 
47 |  |  |  |  |  |  |  |  | 
48 |  | X | X |  | X | X | X | X | X
49 |  |  |  |  |  |  |  |  | 
50 |  | X | X |  | X | X | X | X | X
51 |  |  |  |  |  |  |  |  | 
52 | X |  |  |  |  |  |  |  | 
53 |  |  |  |  |  |  |  |  | 
54 |  |  |  |  |  |  |  |  | 
55 |  |  | X |  | X | X | X | X | X
56 |  |  |  |  |  |  |  |  | 
57 |  |  |  |  |  |  |  |  | 
58 |  | X | X |  | X | X | X | X | X
59 |  |  |  |  |  |  |  |  | 
60 |  |  |  |  |  |  |  |  | 
61 |  | X | X |  | X | X | X | X | X
62 |  |  |  |  |  |  |  |  | 
63 |  |  |  |  |  |  |  |  | 
64 | X |  |  |  |  |  |  |  | 
65 |  |  |  |  |  |  |  |  | 
66 |  |  |  |  |  |  |  |  | 
67 |  |  | X |  | X | X | X | X | X
68 |  |  |  |  |  |  |  |  | 
69 |  |  |  |  |  |  |  |  | 
70 |  | X | X |  | X | X | X | X | X
71 |  |  |  |  |  |  |  |  | 
72 |  |  |  |  |  |  |  |  | 
73 |  | X | X |  | X | X | X | X | X
74 |  |  |  |  |  |  |  |  | 
75 |  |  |  |  |  |  |  |  | 

## Slide 74
APPENDIX
Table 18: Maintenance Cycles for B2 Roadway Category Pavement (cont’d)
Year | Resurface | Patching | Crack Seal | Seal Coat | Blading Shoulders | Clipping Shoulders | Brush and Tree Removal | Spot Ditching | Culvert Work
76 | X |  |  |  |  |  |  |  | 
77 |  |  |  |  |  |  |  |  | 
78 |  |  |  |  |  |  |  |  | 
79 |  |  | X |  | X | X | X | X | X
80 |  |  |  |  |  |  |  |  | 
81 |  |  |  |  |  |  |  |  | 
82 |  | X | X |  | X | X | X | X | X
83 |  |  |  |  |  |  |  |  | 
84 |  | X | X |  | X | X | X | X | X
85 |  |  |  |  |  |  |  |  | 
86 | X |  |  |  |  |  |  |  | 
87 |  |  |  |  |  |  |  |  | 
88 |  |  |  |  |  |  |  |  | 
89 |  |  | X |  | X | X | X | X | X
90 |  |  |  |  |  |  |  |  | 
91 |  |  |  |  |  |  |  |  | 
92 |  | X | X |  | X | X | X | X | X
93 |  |  |  |  |  |  |  |  | 
94 | X |  |  |  |  |  |  |  | 

## Slide 75
Pavement Maintenance Cycles: C1 Category
APPENDIX
Table 19: Maintenance Cycles for C1 Roadway Category Pavement
Year | Resurface | Patching | Crack Seal | Seal Coat | Blading Shoulders | Clipping Shoulders | Brush and Tree Removal | Spot Ditching | Culvert Work
0 | X |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  | X |  | X | X | X | X | X
4 |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  |  | 
6 |  | X | X |  | X | X | X | X | X
7 |  |  |  |  |  |  |  |  | 
8 |  |  |  |  |  |  |  |  | 
9 |  | X | X |  | X | X | X | X | X
10 |  |  |  |  |  |  |  |  | 
11 |  |  |  |  |  |  |  |  | 
12 |  | X | X |  | X | X | X | X | X
13 |  |  |  |  |  |  |  |  | 
14 |  |  |  |  |  |  |  |  | 
15 | X |  |  |  |  |  |  |  | 
16 |  |  |  |  |  |  |  |  | 
17 |  |  |  |  |  |  |  |  | 
18 |  |  | X |  | X | X | X | X | X
19 |  |  |  |  |  |  |  |  | 
20 |  |  |  |  |  |  |  |  | 
21 |  | X | X |  | X | X | X | X | X
22 |  |  |  |  |  |  |  |  | 
23 |  |  |  |  |  |  |  |  | 
24 |  | X | X |  | X | X | X | X | X
25 |  |  |  |  |  |  |  |  | 
26 |  |  |  |  |  |  |  |  | 
27 |  | X | X |  | X | X | X | X | X
28 |  |  |  |  |  |  |  |  | 
29 |  |  |  |  |  |  |  |  | 
30 | X |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  |  |  | 
32 |  |  |  |  |  |  |  |  | 
33 |  |  | X |  | X | X | X | X | X
34 |  |  |  |  |  |  |  |  | 
35 |  |  |  |  |  |  |  |  | 

## Slide 76
APPENDIX
Table 19: Maintenance Cycles for C1 Roadway Category Pavement (cont’d)
Year | Resurface | Patching | Crack Seal | Seal Coat | Blading Shoulders | Clipping Shoulders | Brush and Tree Removal | Spot Ditching | Culvert Work
36 |  | X | X |  | X | X | X | X | X
37 |  |  |  |  |  |  |  |  | 
38 |  |  |  |  |  |  |  |  | 
39 |  | X | X |  | X | X | X | X | X
40 |  |  |  |  |  |  |  |  | 
41 |  |  |  |  |  |  |  |  | 
42 |  | X | X |  | X | X | X | X | X
43 |  |  |  |  |  |  |  |  | 
44 |  |  |  |  |  |  |  |  | 
45 | X |  |  |  |  |  |  |  | 
46 |  |  |  |  |  |  |  |  | 
47 |  |  |  |  |  |  |  |  | 
48 |  |  | X |  | X | X | X | X | X
49 |  |  |  |  |  |  |  |  | 
50 |  |  |  |  |  |  |  |  | 
51 |  | X | X |  | X | X | X | X | X
52 |  |  |  |  |  |  |  |  | 
53 |  |  |  |  |  |  |  |  | 
54 |  | X | X |  | X | X | X | X | X
55 |  |  |  |  |  |  |  |  | 
56 |  |  |  |  |  |  |  |  | 
57 |  | X | X |  | X | X | X | X | X
58 |  |  |  |  |  |  |  |  | 
59 |  |  |  |  |  |  |  |  | 
60 | X |  |  |  |  |  |  |  | 
61 |  |  |  |  |  |  |  |  | 
62 |  |  |  |  |  |  |  |  | 
63 |  |  | X |  | X | X | X | X | X
64 |  |  |  |  |  |  |  |  | 
65 |  |  |  |  |  |  |  |  | 
66 |  | X | X |  | X | X | X | X | X
67 |  |  |  |  |  |  |  |  | 
68 |  |  |  |  |  |  |  |  | 
69 |  | X | X |  | X | X | X | X | X
70 |  |  |  |  |  |  |  |  | 
71 | X |  |  |  |  |  |  |  | 
72 |  |  |  |  |  |  |  |  | 
73 |  |  |  |  |  |  |  |  | 
74 |  |  | X |  | X | X | X | X | X
75 |  |  |  |  |  |  |  |  | 

## Slide 77
APPENDIX
Table 19: Maintenance Cycles for C1 Roadway Category Pavement (cont’d)
Year | Resurface | Patching | Crack Seal | Seal Coat | Blading Shoulders | Clipping Shoulders | Brush and Tree Removal | Spot Ditching | Culvert Work
76 |  |  |  |  |  |  |  |  | 
77 |  | X | X |  | X | X | X | X | X
78 |  |  |  |  |  |  |  |  | 
79 |  |  |  |  |  |  |  |  | 
80 |  | X | X |  | X | X | X | X | X
81 |  |  |  |  |  |  |  |  | 
82 | X |  |  |  |  |  |  |  | 
83 |  |  |  |  |  |  |  |  | 
84 |  |  |  |  |  |  |  |  | 
85 |  |  | X |  | X | X | X | X | X
86 |  |  |  |  |  |  |  |  | 
87 |  |  |  |  |  |  |  |  | 
88 |  | X | X |  | X | X | X | X | X
89 |  |  |  |  |  |  |  |  | 
90 |  |  |  |  |  |  |  |  | 
91 |  | X | X |  | X | X | X | X | X
92 |  |  |  |  |  |  |  |  | 
93 |  |  |  |  |  |  |  |  | 
94 | X |  |  |  |  |  |  |  | 
95 |  |  |  |  |  |  |  |  | 
96 |  |  |  |  |  |  |  |  | 
97 |  |  | X |  | X | X | X | X | X
98 |  |  |  |  |  |  |  |  | 
99 |  |  |  |  |  |  |  |  | 
100 |  | X | X |  | X | X | X | X | X
101 |  |  |  |  |  |  |  |  | 
102 | X |  |  |  |  |  |  |  | 

## Slide 78
Pavement Maintenance Cycles: C2 Category
APPENDIX
Table 20: Maintenance Cycles for C2 Roadway Category Pavement
Year | Resurface | Patching | Crack Seal | Seal Coat | Blading Shoulders | Clipping Shoulders | Brush and Tree Removal | Spot Ditching | Culvert Work
0 | X |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  | X |  | X | X | X | X | X
4 |  |  |  |  |  |  |  |  | 
5 |  |  |  |  |  |  |  |  | 
6 |  | X | X |  | X | X | X | X | X
7 |  |  |  |  |  |  |  |  | 
8 |  |  |  | X |  |  |  |  | 
9 |  | X | X |  | X | X | X | X | 
10 |  |  |  |  |  |  |  |  | 
11 |  |  |  |  |  |  |  |  | 
12 |  | X | X |  | X | X | X | X | X
13 |  |  |  |  |  |  |  |  | 
14 |  |  |  | X |  |  |  |  | 
15 |  | X | X |  | X | X | X | X | 
16 |  |  |  |  |  |  |  |  | 
17 |  |  |  |  |  |  |  |  | 
18 |  | X | X |  | X | X | X | X | X
19 |  |  |  |  |  |  |  |  | 
20 | X |  |  |  |  |  |  |  | 
21 |  |  |  |  |  |  |  |  | 
22 |  |  |  |  |  |  |  |  | 
23 |  |  | X |  | X | X | X | X | X
24 |  |  |  |  |  |  |  |  | 
25 |  |  |  |  |  |  |  |  | 
26 |  | X | X |  | X | X | X | X | X
27 |  |  |  |  |  |  |  |  | 
28 |  |  |  | X |  |  |  |  | 
29 |  | X | X |  | X | X | X | X | 
30 |  |  |  |  |  |  |  |  | 
31 |  |  |  |  |  |  |  |  | 
32 |  | X | X |  | X | X | X | X | X
33 |  |  |  |  |  |  |  |  | 
34 |  |  |  | X |  |  |  |  | 
35 |  | X | X |  | X | X | X | X | 

## Slide 79
APPENDIX
Table 20: Maintenance Cycles for C2 Roadway Category Pavement (cont’d)
Year | Resurface | Patching | Crack Seal | Seal Coat | Blading Shoulders | Clipping Shoulders | Brush and Tree Removal | Spot Ditching | Culvert Work
36 |  |  |  |  |  |  |  |  | 
37 |  |  |  |  |  |  |  |  | 
38 |  | X | X |  | X | X | X | X | X
39 |  |  |  |  |  |  |  |  | 
40 | X |  |  |  |  |  |  |  | 
41 |  |  |  |  |  |  |  |  | 
42 |  |  |  |  |  |  |  |  | 
43 |  |  | X |  | X | X | X | X | X
44 |  |  |  |  |  |  |  |  | 
45 |  |  |  |  |  |  |  |  | 
46 |  | X | X |  | X | X | X | X | X
47 |  |  |  |  |  |  |  |  | 
48 |  |  |  | X |  |  |  |  | 
49 |  | X | X |  | X | X | X | X | 
50 |  |  |  |  |  |  |  |  | 
51 |  |  |  |  |  |  |  |  | 
52 |  | X | X |  | X | X | X | X | X
53 |  |  |  |  |  |  |  |  | 
54 |  |  |  | X |  |  |  |  | 
55 |  | X | X |  | X | X | X | X | 
56 |  |  |  |  |  |  |  |  | 
57 |  |  |  |  |  |  |  |  | 
58 |  | X | X |  | X | X | X | X | X
59 |  |  |  |  |  |  |  |  | 
60 | X |  |  |  |  |  |  |  | 
61 |  |  |  |  |  |  |  |  | 
62 |  |  |  |  |  |  |  |  | 
63 |  |  | X |  | X | X | X | X | X
64 |  |  |  |  |  |  |  |  | 
65 |  |  |  |  |  |  |  |  | 
66 |  | X | X |  | X | X | X | X | X
67 |  |  |  |  |  |  |  |  | 
68 |  |  |  | X |  |  |  |  | 
69 |  | X | X |  | X | X | X | X | 
70 |  |  |  |  |  |  |  |  | 
71 |  |  |  |  |  |  |  |  | 
72 |  | X | X |  | X | X | X | X | X
73 |  |  |  |  |  |  |  |  | 
74 |  |  |  | X |  |  |  |  | 
75 |  | X | X |  | X | X | X | X | 

## Slide 80
APPENDIX
Table 20: Maintenance Cycles for C2 Roadway Category Pavement (cont’d)
Year | Resurface | Patching | Crack Seal | Seal Coat | Blading Shoulders | Clipping Shoulders | Brush and Tree Removal | Spot Ditching | Culvert Work
76 |  |  |  |  |  |  |  |  | 
77 |  |  |  |  |  |  |  |  | 
78 |  | X | X |  | X | X | X | X | X
79 |  |  |  |  |  |  |  |  | 
80 | X |  |  |  |  |  |  |  | 
81 |  |  |  |  |  |  |  |  | 
82 |  |  |  |  |  |  |  |  | 
83 |  |  | X |  | X | X | X | X | X
84 |  |  |  |  |  |  |  |  | 
85 |  |  |  |  |  |  |  |  | 
86 |  | X | X |  | X | X | X | X | X
87 |  |  |  |  |  |  |  |  | 
88 |  |  |  | X |  |  |  |  | 
89 |  | X | X |  | X | X | X | X | 
90 |  |  |  |  |  |  |  |  | 
91 |  |  |  |  |  |  |  |  | 
92 |  | X | X |  | X | X | X | X | X
93 |  |  |  |  |  |  |  |  | 
94 |  |  |  | X |  |  |  |  | 
95 |  | X | X |  | X | X | X | X | 
96 |  |  |  |  |  |  |  |  | 
97 |  |  |  |  |  |  |  |  | 
98 |  | X | X |  | X | X | X | X | X
99 |  |  |  |  |  |  |  |  | 
100 | X |  |  |  |  |  |  |  | 
101 |  |  |  |  |  |  |  |  | 
102 |  |  |  |  |  |  |  |  | 
103 |  |  | X |  | X | X | X | X | X
104 |  |  |  |  |  |  |  |  | 
105 |  |  |  |  |  |  |  |  | 
106 |  | X | X |  | X | X | X | X | X
107 |  |  |  |  |  |  |  |  | 
108 |  |  |  | X |  |  |  |  | 
109 |  | X | X |  | X | X | X | X | 
110 |  |  |  |  |  |  |  |  | 

## Slide 81
APPENDIX
Table 20: Maintenance Cycles for C2 Roadway Category Pavement (cont’d)
Year | Resurface | Patching | Crack Seal | Seal Coat | Blading Shoulders | Clipping Shoulders | Brush and Tree Removal | Spot Ditching | Culvert Work
111 |  |  |  |  |  |  |  |  | 
112 |  | X | X |  | X | X | X | X | X
113 |  |  |  |  |  |  |  |  | 
114 |  |  |  | X |  |  |  |  | 
115 |  | X | X |  | X | X | X | X | 
116 |  |  |  |  |  |  |  |  | 
117 |  |  |  |  |  |  |  |  | 
118 |  | X | X |  | X | X | X | X | X
119 |  |  |  |  |  |  |  |  | 
120 | X |  |  |  |  |  |  |  | 

## Slide 82
Indiana
Department of Transportation