## Slide 1
Indiana Department of Environmental Management
Office of Air Quality
(800) 451-6027
www.IN.gov/idem/6650.htm
2010 Ozone Season
Summary Report

## Slide 2: 2010 Ozone Season
Purpose
This Ozone Season Summary Report provides an overview of ozone levels
from 2010, as well as ozone trends over the last ten years (2001-2010).
Summary
The ozone season in Indiana lasts from April 1 through September 30. The duration of the ozone season for each state is mandated by the United States Environmental Protection Agency (U.S. EPA).
  • 183 total days in Indiana’s 2010 ozone season.
  • 35 forecasted days (Air Quality Action Days) in 2010.
  • 17 exceedance days in 2010.

## Slide 3: Background of Ground-Level Ozone
What is ground-level ozone?
Ground-level ozone is a gas composed of three oxygen atoms. The chemical structure of ozone is the same whether at ground-level or above the earth, but it is unhealthy to breathe at ground-level.
Where does ground-level ozone come from?
Ground-level ozone is not emitted directly into the air but is created by a chemical reaction between nitrogen oxides (NOX) and volatile organic compounds (VOC) in the presence of sunlight. Emissions from industrial facilities and electric utilities, motor vehicle exhaust, gasoline vapors, and chemical solvents are some of the major sources of NOX and VOC.
Health effects of ground-level ozone:
  • chest pain, coughing, throat irritation, congestion
  • can worsen bronchitis, emphysema, asthma
  • reduces lung function and inflames the linings of the lungs
  • scars lung tissues

## Slide 4: National Ambient Air Quality Standards (NAAQS) for Ozone
Primary Standards
Primary standards, also known as health standards, are limits set to protect public health, including the health of “sensitive” populations such as people with asthma, children, and the elderly.
Secondary Standards
Secondary standards are set to protect public welfare, including protection against decreased visibility and damage to animals, crops, vegetation, and buildings.

## Slide 5: History of the Ozone Standard
U.S. EPA established a 1-hour standard of 0.08 parts per million (ppm) for ground level ozone
U.S. EPA revised the 1-hour standard to 0.12 ppm
U.S. EPA replaced the 1-Hour standard with an 8-hour health standard of 0.085 ppm
Three states and industry challenged the new standard
1997 8-hour health standard for ozone became effective
U.S. EPA significantly strengthened the health standard for ozone to be set at 0.075 ppm
U.S. Supreme Court upheld the 1997 8-hour health standard
U.S. EPA revoked the 1-hour standard
U.S. EPA announced it will reconsider the 2008 8-hour health standard
1971 | 1979 | 1997 | 2001 | 2004 | 2005 | 2008 | 2009 | 2010
U.S. EPA proposes to strengthen the 8-hour primary standard to a level within a range of 0.060 – 0.070 ppm and establish a distinct, cumulative seasonal standard within a range of
7 to 15 ppm-hours
Notes: <number>

## Slide 6: Attaining the Standard
8-Hour Standard
To attain the 8-hour standard, the three-year average of the fourth highest value for the ozone season must be at or below the standard.
Exceedance versus Violation of the Standard
  • An exceedance occurs when an 8-hour average value is measured above the standard.
  • A violation occurs when the three-year average of the fourth highest value for the ozone season exceeds the standard.
  • A monitor can exceed the standard without being in violation.

## Slide 7: Attainment Status
1997 8-Hour Health Standard
U.S. EPA revised the former health standard in 1997 to 0.08 ppm.
  Attainment designations became effective in 2004.
  Initially, 23 counties and one township in Indiana were classified as being in violation.
  At the close of the 2008 ozone season, all Indiana counties met the standard.
  By May 2010, all areas were officially designated attainment under the standard.
2008 8-Hour Health Standard
U.S. EPA revised the 1997 health standard in 2008 to 0.075 ppm.
  In March 2009, IDEM submitted state recommendations to U.S. EPA for attainment status for the 2008 standard.
    Based on monitoring data from 2006 through 2008, the Indiana Department of Environmental Management recommended 12 counties be designated as nonattainment.
  In September 2009, U.S. EPA announced it would reconsider the standard.
  Based on ambient air quality data from 2008 through 2010, NO monitors measured air quality above the revised primary 8-hour ozone standard.

## Slide 8: Attainment Status
2010 Primary and Secondary Ozone Standards
On January 6, 2010, U.S. EPA proposed to strengthen the primary 8-hour standard to a level within the range of 0.060 to 0.070 ppm and establish a distinct cumulative, seasonal standard within a range of 7 to 15 ppm-hours.
• Based on 2008 through 2010 ambient air quality data,
• a total of 39 monitors in 27 counties recorded three-year design values equal to or greater than 0.061 ppm
• 6 monitors in 6 counties greater than or equal to 0.071 ppm
• 17 monitors in 15 counties greater than or equal to 0.066 ppm and less than or equal to 0.070 ppm
• 16 monitors in 12 counties greater than or equal to 0.065 ppm and less than or equal to 0.061 ppm
• Indiana does not anticipate any additional secondary ozone nonattainment areas beyond what would be classified under the revised primary ozone standard.

## Slide 12: Monitoring
Monitors
41 ozone monitors in 27 counties across Indiana.
Placement
U.S. EPA provides guidance on placement of monitors.
Monitors placed based on population density and manufacturing levels.
Calculating the Monitoring Data
Levels are monitored 24 hours per day and rolling 8-hour averages are calculated; highest 8-hour average is reported for the day.
A monitor’s design value is calculated at the end of each ozone season; design values are calculated for each monitor in the state.
  • Design value: three-year average of fourth highest values

## Slide 14: 2010 Monitoring Summary
The Charlestown State Park ozone monitor was the only monitor across the state that recorded a 4th high value equal to or above the 2008 8-hour standard of 0.075 ppm (i.e., 0.077 ppm).
No monitors had a three-year design value that exceeded the 2008 8-hour ozone standard.
None of Indiana’s maintenance areas classified under the 1997 8-hour ozone standard exceeded the warning or action level triggers.

## Slide 15: Ozone Monitors by Area
Area | Counties
Northwest | Lake LaPorte Porter
North Central | Elkhart St. Joseph
Northeast | Allen Huntington
Central | Boone Johnson
 | Delaware Madison
 | Hamilton Marion
 | Hancock Morgan
 | Hendricks Shelby
West Central | Carroll Vigo
Southwest | Greene Vanderburgh
 | Perry Warrick
 | Posey
Southeast | Clark Jackson Floyd

## Slide 16: Annual 4th High Trends 2001-2010
1997 8-hour Health Standard
2008 8-hour Health Standard
Proposed Range of the 2010
8-hour Health Standard (0.060 to 0.070 parts per million)

## Slide 17: Design Value Trends 2001-2010
1997 8-hour Health Standard
Proposed Range of the 2010
8-Hour Health Standard (0.060 to 0.070 parts per million)
2008 8-hour Health Standard

## Slide 18: Additional Information
For additional information regarding the 2010 NAAQS for ground-level ozone please visit U.S. EPA’s Ground-Level Ozone Regulatory Actions Web site: http://www.epa.gov/air/ozonepollution/actions.html#jan10s

## Slide 19: Contact
For more information regarding the ozone designation process, or Indiana’s redesignation petitions and maintenance plans, visit www.in.gov/idem/4654.htm or contact the Office of Air Quality at (800) 451-6027 and ask for the Rule and State Implementation Plan Development Section.