## Slide 1
Indiana Department of Environmental Management
Office of Air Quality
(800) 451-6027
www.idem.IN.gov/6650.htm
2012 Ozone Season
Summary Report
<number>

## Slide 2: 2012 Ozone Season
Purpose
This Ozone Season Summary Report provides an overview of ozone levels
from 2012, as well as ozone trends over the last ten years (2003 through 2012).
Summary
The ozone season in Indiana lasts from April 1 through September 30. The duration of the ozone season for each state is mandated by the United States Environmental Protection Agency (U.S. EPA).
  • 183 total days in Indiana’s 2012 ozone season.
  • 35 exceedance days in 2012.
  • 42 forecasted days (Air Quality Action Days) in 2012.
<number>
Notes: <number>

## Slide 3: Background of Ground-Level Ozone
What is ground-level ozone?
Ground-level ozone is a gas composed of three oxygen atoms. The chemical structure of ozone is the same whether at ground level or above the earth, but it is unhealthy to breathe at ground level.
Where does ground-level ozone come from?
Ground-level ozone is not emitted directly into the air, but is created by a chemical reaction between nitrogen oxides (NOx) and volatile organic compounds (VOCs) in the presence of sunlight. Emissions from industrial facilities and electric utilities, motor vehicle exhaust, gasoline vapors, and chemical solvents are some of the major sources of NOx and VOCs.
Health effects of ground-level ozone:
  • Chest pain, coughing, throat irritation, congestion.
  • Can worsen bronchitis, emphysema, asthma.
  • Reduces lung function and inflames the linings of the lungs.
  • Scars lung tissues.
<number>

## Slide 4: National Ambient Air Quality Standards (NAAQS) for Ozone
Primary Standards
Primary standards, also known as health standards, are limits set to protect public health, including the health of “sensitive” populations such as asthmatics, children, and the elderly.
Secondary Standards
Secondary standards are set to protect public welfare, including protection against decreased visibility, damage to animals, crops, vegetation, and buildings.
<number>

## Slide 5: History of the Ozone Standard
U.S. EPA first established a 1-hour standard of 0.08 parts per million (ppm) for ground-level ozone
U.S. EPA revised the 1-hour ozone standard to a level of 0.12 ppm
U.S. EPA replaced the 1-hour standard with an 8-hour health standard of 0.08 ppm
Three states and industry challenged the new standard
1997 8-hour health standard for ozone became effective
U.S. EPA significantly strengthened the health standard for ozone to a level of 0.075 ppm
U.S. Supreme Court upheld the 1997
8-hour health standard for ozone
U.S. EPA revoked the
1-hour ozone standard
U.S. EPA announced it would reconsider the 2008 8-hour health standard
1971 | 1979 | 1997 | 2001 | 2004 | 2005 | 2008 | 2009 | 2011
U.S. EPA announced it would withdraw its reconsideration of the 2008 8-hour health standard and revisit the standard during the next statutorily required NAAQS review cycle slated for 2013
<number>
U.S. EPA announced it would move forward with implementation of the 2008 8-hour health standard set at a level of 0.075 ppm
Notes: <number>

## Slide 6: Attaining the Standard
8-Hour Standard
To attain the 8-hour standard, the three-year average of the fourth (4th) highest value for the ozone season must be at or below the standard of 0.075 ppm.
Exceedance versus a Violation of the Standard
  • An exceedance occurs when an 8-hour average value is measured above the standard.
  • A violation occurs when the three-year average of the 4th highest value for the ozone season exceeds the standard.
  • A monitor can exceed the standard without being in violation.
<number>

## Slide 7: Attainment Status
1997 8-Hour Ozone Health Standard
U.S. EPA revised the former health standard in 1997 to 0.08 ppm.
  Attainment designations became effective in 2004.
  Initially, 23 counties and one township in Indiana were classified as being in violation of the standard.
  At the close of the 2008 ozone season, all Indiana counties met the standard.
  By May 2010, all areas were officially designated attainment under the standard.
2008 8-Hour Ozone Health Standard
U.S. EPA revised the 1997 health standard in 2008 to 0.075 ppm.
  In March 2009, the Indiana Department of Environmental Management (IDEM) submitted state recommendations to U.S. EPA for attainment status for the 2008 standard.
    Based on monitoring data from 2006 through 2008, IDEM recommended 12 counties be designated as nonattainment.
  In September 2009, U.S. EPA announced it would reconsider the standard.
<number>

## Slide 8: Attainment Status
<number>
2008 8-Hour Ozone Health Standard (continued)
  • In September 2011, U.S. EPA announced it would withdraw its reconsideration of the 2008 standard and revisit the standard during the next statutorily required NAAQS review cycle slated for 2013.
  • On September 22, 2011, U.S. EPA announced its intention to fast-track initial area designations and classification rule.
  • Initial area designations were based on 2008 through 2010 air quality monitoring data and 2009 state recommendations.
  • U.S. EPA also announced it would consider 2011 data if certified early (i.e., by February 15, 2012).
  • U.S. EPA completed designations for the Chicago-Naperville, IL-IN-WI area on May 31, 2012 (2008 through 2010 monitoring data for Indiana and Wisconsin and 2009 through 2011 monitoring data for Illinois).
  • All other area designations were completed on April 30, 2012.
  • Dearborn County (Lawrenceburg Township), Lake, and Porter counties were designated nonattainment effective July 20, 2012.
  • All other areas of the state were classified as unclassifiable/attainment.
  • Lake and Porter counties are pending redesignation with U.S. EPA.

## Slide 9
2012 Indiana Ozone Nonattainment Areas
<number>

## Slide 10
<number>
Ozone 8-Hour
Design Values
(3-Year Average 4th High)
Based on 2010 through 2012 Monitoring Data
Standard at 0.075 ppm

## Slide 11: Monitoring
Placement
• U.S. EPA provides guidance on placement of monitors.
• Monitors placed based on population density and manufacturing levels.
Monitors
• 41 ozone monitors in 27 counties across Indiana.
Calculating the Monitoring Data
• Levels are monitored 24 hours per day and rolling 8-hour averages are calculated; highest 8-hour average is reported for the day.
• A monitor’s design value is calculated at the end of each ozone season; design values are calculated for each monitor in the state.
– Design value: three-year average of fourth highest values.
<number>

## Slide 12: 2012 Monitoring Summary
<number>
• 22 of Indiana’s ozone monitors recorded annual 4th high values above the 2008 8-hour health standard, i.e. equal to or greater than 0.076 ppm. Ozone monitors above the standard include: Charlestown State Park, Dayville, Evansville, Fairland, Gary – Illinois Institute of Technology Research Institutes (IITRI), Granger, Hammond, Indianapolis – East 16th Street, Indianapolis – Harding Street, Indianapolis – Washington Park, Inglefield, LaPorte – East Lincolnway, Leo, Leopold, Michigan City, New Albany, Noblesville, Ogden Dunes, Plummer, South Bend, Whitestown, and Whiting.
• The Charlestown State Park, Michigan City, New Albany, and Plummer ozone monitors had three-year average 4th high design values for the years 2010 through 2012 that exceeded the 2008 8-hour health standard.
• One of Indiana’s maintenance areas classified under the 1997 8-hour health standard exceeded both the one-year and two-year warning level triggers (LaPorte County).

## Slide 13: Ozone Monitors by Area
Area | Counties
Northwest | Lake LaPorte Porter
North Central | Elkhart St. Joseph
Northeast | Allen Huntington
Central | Boone Johnson
 | Delaware Madison
 | Hamilton Marion
 | Hancock Morgan
 | Hendricks Shelby
West Central | Carroll Vigo
Southwest | Greene Vanderburgh
 | Perry Warrick
 | Posey
Southeast | Clark Jackson Floyd
<number>

## Slide 14: Annual 4th High Trends 2003-2012
1997 8-Hour Health Standard
2008 8-Hour Health Standard
<number>

## Slide 15: Design Value Trends 2003-2012
1997 8-Hour Health Standard
2008 8-Hour Health Standard
<number>

## Slide 16: Meteorologically Adjusted Trend Analysis
<number>
• In order to account for variable meteorology, IDEM conducted a meteorologically adjusted trend analysis.
• This type of analysis is necessary to account for variability with critical meteorological conditions among ozone seasons, and verify upward or downward trends.
• The results of this analysis confirm a downward trend in monitored ozone values across the state through 2011.
• Detailed information concerning this analysis is included in the appendix.

## Slide 17: Additional Information
For additional information regarding the NAAQS for ground-level ozone, please visit U.S. EPA’s Ground-Level Ozone Regulatory Actions website: www.epa.gov/air/ozonepollution/actions.html
<number>

## Slide 18: Contact
For more information regarding the ozone designation process, or Indiana’s redesignation petitions and maintenance plans, visit www.idem.IN.gov/4654.htm or contact Ms. Linda McClure of the Office of Air Quality at (800) 451-6027, (317) 232-8449, or lmcclure@idem.IN.gov.
<number>

## Slide 19: APPENDIX
A-1
Meteorologically Adjusted Trend Analysis Results

## Slide 20: Analysis Results
A-2
Central Indiana
North Central Indiana
Important nodes contain the most important individual monitor values over 0.075 ppm: Fort Benjamin Harrison (Node 53) and Bristol (Node 6).

## Slide 21: Analysis Results
Northeast Indiana
Northwest Indiana
A-3
Important nodes contain the most important individual monitor values over 0.075 ppm: Beacon Street (Node 7) and Ogden Dunes (Node 13).

## Slide 22: Analysis Results
Southeast Indiana
Southwest Indiana
A-4
Important nodes contain the most important monitor values over 0.075 ppm: Charlestown (Node 5) and Inglefield (Node 13).

## Slide 23: Analysis Results
A-5
Important nodes contain the most important individual monitor values over 0.075 ppm: Plummer (Node 13).
Rural Background