## Slide 1
Indiana Department of Environmental Management
2009 Fine Particles (PM2.5)
Summary Report
Office of Air Quality

## Slide 2: Purpose
This Fine Particles (PM2.5) Summary Report provides an overview of PM2.5 levels from 2009 as well as PM2.5 trends over the last ten years (2000-2009)
  2009
    2 forecasted days (Air Quality Action Days)
    9 exceedances

## Slide 3: Background of Fine Particles (PM)
What is particulate matter?
Particulate matter is the term for particles found in the air, including dust, dirt, soot, smoke, and liquid droplets
Where does PM come from?
Sources of PM include all types of combustion activities:
  motor vehicles, power plants, wood burning, etc.
  certain industrial processes
Health effects of PM:
  increased respiratory symptoms, such as irritation of the airways, coughing, or difficulty breathing (i.e., decreased lung function, aggravated asthma, and development of chronic bronchitis)
  irregular heartbeat
  nonfatal heart attacks
  premature death in people with heart or lung disease

## Slide 4: Fine Particle Regulations
*µm = micrograms

## Slide 5: National Ambient Air Quality Standards (NAAQS) for PM2.5
Primary Standards
Primary standards are limits set by the U.S. Environmental Protection Agency (U.S. EPA) to protect public health including the health of “sensitive” populations such as asthmatics, children, and the elderly
  Annual standard: 15 µg/m3*
  24-hour standard: 35 µg/m3*
Secondary Standards
Secondary standards are set by the U.S. EPA to protect public welfare, including protection against decreased visibility, damage to animals, crops, vegetation, and buildings
  Annual standard: 15 µg/m3* (same as primary standard)
  24-hour standard: 35 µg/m3* (same as primary standard)
Reconsideration of the Standards
  U.S. EPA is reconsidering the current standards (set in 2006), focusing on a range of 11-14 µg/m3* for the annual standard and a range of 30-35 µg/m3* for the 24-hour standard
*ug/m3 = micrograms per cubic meter

## Slide 6
Timeline of PM Standards

## Slide 7: Attaining the Standard
Annual Standard
To attain the annual standard, the three-year average of weighted annual mean PM2.5 concentrations from a monitor must not exceed 15 µg/m3
  Exceedance versus a Violation of the Standard
  An exceedance occurs when the 98th percentile is measured above the standard. A violation occurs when the three-year average of the 98th percentile is measured above the standard. A monitor can exceed the standard without being in violation.
24-Hour Standard
To attain the 24-hour standard, the three-year average of the 98th percentile of 24-hour concentrations at each monitor must not exceed 35 ug/m3
  Exceedance versus a Violation of the Standard
  An exceedance occurs when the average annual mean is measured above the standard. A violation occurs when the three-year average of the annual means is above the standard. A monitor can exceed the standard without being in violation.

## Slide 8: Attainment Status
Daily Standard
U.S. EPA attainment designations for the 2006 24-hour standard were effective December 14, 2009
  All Indiana counties were designated as attaining the standard and remain in attainment
Annual Standard
U.S. EPA attainment designations for the 1997 annual standard were effective April 5, 2005
12 full and five partial counties were designated as nonattainment
All areas of the state currently meet the annual air quality standard, but have not been formally redesignated
    NW, SW and Central Indiana are pending redesignation.
    SE Indiana and Lawrenceburg Township are eligible for redesignation and IDEM is planning to submit redesignation petitions in 2010.

## Slide 9
*NW, SW and Central Indiana are pending redesignation
*SE Indiana and Lawrenceburg Township are now eligible for redesignation
U.S. EPA Designated Nonattainment Areas under the Annual Standard
Standard: 15 µg/m3

## Slide 10: 2009 Monitoring Network
Placement
U.S. EPA provides guidance on placement of monitors
Monitors placed based on population density and manufacturing levels
Monitors
31 annual fine particle monitors across Indiana
35* 24-hour fine particle monitors across Indiana
Calculating the Monitoring Data
Monitoring data is collected every three days
A monitor’s design value is calculated at the end of the year, once all of the data has been quality assured
  Annual Design Value: three-year average of the weighted annual mean PM2.5 concentrations
  24-Hour Design Value: three-year average of the 98th percentile of 24-hour concentrations
  * Four monitoring sites reflect air quality in a relatively small area, are directly influenced by a specific source, and are intended to be used for attainment status under the 24-hour standard only.

## Slide 11: PM2.5 Monitors by Area
Area | Counties
East Central | Delaware, Henry, Howard, Madison, Marion, Monroe
Northwest | Lake, LaPorte, Porter
Northeast | Allen
North Central | Elkhart, St. Joseph
West Central | Tippecanoe, Vigo
Southwest | Dubois, Gibson, Knox, Spencer, Vanderburgh
Southeast | Clark, Floyd

## Slide 12
Indiana PM2.5
2007-2009
Daily Design
Values
Standard: 35 µg/m3

## Slide 13
Indiana PM2.5
2007-2009
Annual Design
Values
Standard: 15 µg/m3

## Slide 14
PM2.5 Annual Trends 2000-2009

## Slide 15
Annual Standard 15 µg/m3
PM2.5 Annual Trends 2007-2009
Proposed Standard Revision, Range of Consideration, 11 – 14 µg/m3

## Slide 16: Contact
For more information regarding the PM2.5 designation process, or Indiana’s redesignation petitions and maintenance plans, visit www.in.gov/idem/4654.htm or contact Sarah Raymond of the Office of Air Quality at (800) 451-6027 or (317) 232-8449.