## Slide 1
Indiana Department of Environmental Management
Office of Air Quality
(800) 451-6027
www.idem.IN.gov/6650.htm
2011 Fine Particles (PM2.5)
Summary Report
<number>

## Slide 2: Purpose
Purpose
This Fine Particles (PM2.5) Season Summary Report provides an overview of PM2.5 levels from 2011, as well as PM2.5 trends over the last ten years (2002-2011).
Summary
Monitoring and reporting of fine particles occurs on a year-round basis as mandated by the United States Environmental Protection Agency (U.S. EPA).
  • 11 exceedance days in 2011.
  • 1 forecasted day (Air Quality Action Day) in 2011.
<number>

## Slide 3: Background of Fine Particles (PM)
What is particulate matter?
Particulate matter is a complex mixture of small particles found in the air, including dust, dirt, smoke, and liquid droplets.
Where does PM come from?
Sources of PM include all types of combustion activities:
• Motor vehicles, coal-fired power plants, open burning, etc.
• Certain industrial processes.
Health effects of PM:
  • Increased respiratory symptoms, such as irritation of the airways, coughing, or difficulty breathing (i.e. decreased lung function, aggravated asthma, and development of chronic bronchitis).
  • Irregular heartbeat.
  • Nonfatal heart attacks.
  • Premature death in people with heart or lung disease.
<number>

## Slide 4: Fine Particle Regulations
<number>
*µm = micrograms
PM2.5
PM10

## Slide 5: National Ambient Air Quality Standards (NAAQS) for PM2.5
<number>
Primary Standards
Primary standards are limits set by the U.S. EPA to protect public health including the health of “sensitive” populations such as asthmatics, children, and the elderly.
  • Annual standard: 15 µg/m3*
  • 24-hour standard: 35 µg/m3*
Secondary Standards
Secondary standards are set by the U.S. EPA to protect public welfare, including protection against decreased visibility, damage to animals, crops, vegetation, and buildings.
  • Annual standard: 15 µg/m3* (same as primary standard)
  • 24-hour standard: 35 µg/m3* (same as primary standard)
Reconsideration of the Standards
  U.S. EPA is reconsidering the current standards (set in 2006), focusing on a range of 11-14 µg/m3* for the annual standard and a range of 30-35 µg/m3* for the 24-hour standard.
*ug/m3 = micrograms per cubic meter

## Slide 6: History of the PM Standards
U.S. EPA revised the National Ambient Air Quality Standards (NAAQS) and replaced TSP with PM10
Industry and state governments challenged NAAQS
D.C. Circuit Court rejected all remaining legal challenges to the 1997 NAAQS
U.S. EPA strengthened PM2.5 NAAQS
Annual 15 ug/m3
24-hour 35 ug/m3
U.S. EPA revised NAAQS and included PM2.5
Annual 15 ug/m3
24-hour 65 ug/m3
U.S. Supreme Court upheld U.S. EPA‘s authority to enforce Clean Air Act and rules, U.S. EPA not allowed to consider cost
U.S. EPA designated areas under the 1997 PM2.5 NAAQS
(12 counties and 5 partial counties in Indiana designated “nonattainment”)
U.S. EPA scheduled to finalize revisions to the 2006 PM2.5 NAAQS
<number>
U.S. EPA designated areas under the 24-hour 2006 PM2.5 NAAQS (All Indiana counties attain the standard)
1971 | 1987 | 1997 | 2001 | 2002 | 2005 | 2006 | 2009 | 2013
D.C. Circuit Court remanded the 2006 PM2.5 NAAQS to U.S. EPA for reconsideration, but did not vacate the standards
U.S. EPA issued first National Ambient Air Quality Standards (NAAQS) for TSP
Notes: <number>

## Slide 7: Attaining the Standard
Annual Standard
To attain the annual standard, the three-year average of weighted annual mean PM2.5 concentrations from a monitor must not exceed 15 µg/m3.
  Exceedance versus a Violation of the Standard
  • An exceedance occurs when the average annual mean is measured above the standard. A violation occurs when the three-year average of the annual means is above the standard. A monitor can exceed the standard without being in violation.
24-Hour Standard
To attain the 24-hour standard, the three-year average of the 98th percentile of 24-hour concentrations at each monitor must not exceed 35 ug/m3.
  Exceedance versus a Violation of the Standard
  • An exceedance occurs when the 98th percentile is measured above the standard. A violation occurs when the three-year average of the 98th percentile is measured above the standard. A monitor can exceed the standard without being in violation.
<number>
*ug/m3 = micrograms per cubic meter

## Slide 8: Attainment Status
Daily Standard
U.S. EPA attainment designations for the 2006 24-hour standard were effective December 14, 2009.
  • All Indiana counties were designated as attaining the standard and remain in attainment.
Annual Standard
U.S. EPA attainment designations for the 1997 annual standard were effective April 5, 2005.
• 12 full and five partial counties were designated as nonattainment.
• All areas of the state currently meet the annual air quality standard, but not all areas have been formally redesignated.
• Vanderburgh and Warrick counties, as well as Montgomery Township in Gibson County, Ohio Township in Spencer County, and Washington Township in Pike County were redesignated to attainment on October 27, 2011.
• Lawrenceburg Township in Dearborn County, which is part of the Cincinnati- Hamilton OH-KY-IN Fine Particles Nonattainment Area was redesignated to attainment on December 23, 2011.
• Lake and Porter counties were redesignated to attainment on February 6, 2012.
• Clark, Floyd, Hamilton, Marion, Hendricks, Morgan, and Johnson counties, as well as Madison Township in Jefferson County are pending redesignation with U.S. EPA.
<number>

## Slide 9
<number>
PM2.5 Annual
Design Values
(3-Year Average of the Annual Arithmetic Mean)
Based on 2009-2011 Monitoring Data
Standard at 15 ug/m3

## Slide 10
<number>
PM2.5 Annual
Design Values
(3-Year Average of the Annual Arithmetic Mean)
Based on 2009-2011 Monitoring Data
Standard at 14 ug/m3

## Slide 11
<number>
PM2.5 Annual
Design Values
(3-Year Average of the Annual Arithmetic Mean)
Based on 2009-2011 Monitoring Data
Standard at 11 ug/m3

## Slide 12
<number>
PM2.5 Daily
Design Values
(3-Year Average of the 98th Percentile)
Based on 2009-2011 Monitoring Data
Standard at 35 ug/m3

## Slide 13
<number>
PM2.5 Daily
Design Values
(3-Year Average of the 98th Percentile)
Based on 2009-2011 Monitoring Data
Standard at 30 ug/m3

## Slide 14: 2011 Monitoring Network
<number>
Placement
• U.S. EPA provides guidance on placement of monitors.
• Monitors placed based on population density and manufacturing levels.
Monitors
• 31 annual fine particle monitors across Indiana.
• 35* 24-hour fine particle monitors across Indiana.
Calculating the Monitoring Data
• Monitoring data is collected every three days.
• A monitor’s design value is calculated at the end of the year, once all of the data
has been quality assured.
– Annual Design Value: three-year average of the weighted annual mean PM2.5 concentrations.
– 24-Hour Design Value: three-year average of the 98th percentile of 24-hour
PM2.5 concentrations.
  * Four monitoring sites reflect air quality in a relatively small area, are directly influenced by a specific source, and are intended to be used for attainment status under the 24-hour standard only.

## Slide 15: PM2.5 Monitors by Area
<number>
Area | Counties
East Central | Delaware, Henry, Howard, Madison, Marion, Monroe
Northwest | Lake, LaPorte, Porter
Northeast | Allen
North Central | Elkhart, St. Joseph
West Central | Tippecanoe, Vigo
Southwest | Dubois, Gibson, Knox, Spencer, Vanderburgh
Southeast | Clark, Floyd

## Slide 16: 2011 Monitoring Summary
<number>
• No monitors in the state recorded annual arithmetic mean values that exceeded the 2006 annual health standard.
• No monitors in the state had a three-year average annual arithmetic mean value that exceeded the 2006 annual health standard.
• No monitors in the state recorded 24-hour 98th percentile values that exceeded the 2006 24-hour health standard.
• No monitors in the state had a three-year average 98th percentile value that exceeded the 2006 24-hour health standard.

## Slide 17: Annual Arithmetic Mean Trends 2002-2011
<number>

## Slide 18: Annual PM2.5 Design Value Trends 2002-2011
<number>

## Slide 19: 24-Hour 98th Percentile Trends 2002-2011
<number>

## Slide 20: 24-Hour PM2.5 Design Value Trends 2002-2011
<number>

## Slide 21: Additional Information
For additional information regarding the NAAQS for fine particles, please visit U.S. EPA’s Particulate Matter Regulatory Actions website:
http://www.epa.gov/particles/actions.html
<number>

## Slide 22: Contact
For more information regarding the particulate matter designation process, or Indiana’s redesignation petitions and maintenance plans, visit www.idem.IN.gov/4654.htm or contact Mr. Shawn Seals of IDEM’s Office of Air Quality at (800) 451-6027, (317) 233-0425, or sseals@idem.IN.gov.
<number>