## Slide 1: Indiana Department of Environmental Management
2013 Fine Particles (PM2.5)
Summary Report
Office of Air Quality
(800) 451-6027
www.idem.IN.gov/airquality/2391.htm
<number>

## Slide 2: 2013 Fine Particles Monitoring
Purpose
This Fine Particles (PM2.5) Season Summary Report provides an overview of PM2.5 levels from 2013, as well as PM2.5 trends over the last 10 years (2004 through 2013).
Summary
Monitoring and reporting of fine particles occurs on a year-round basis as mandated by the United States Environmental Protection Agency (U.S. EPA).
  • There were 7 exceedance days in 2013.
  • There were no Air Quality Action Days in 2013.
<number>

## Slide 3: Background of Particulate Matter
What is particulate matter?
Particulate matter is a complex mixture of small particles found in the air, including dust, dirt, smoke, and liquid droplets.
Where does PM come from?
Sources of PM include all types of combustion activities:
• Motor vehicles, coal-fired power plants, open burning, etc.
• Certain industrial processes.
Health effects of PM:
  • Increased respiratory symptoms:
  – Irritation of the airways.
  – Coughing or difficulty breathing.
  – Decreased lung function.
  – Aggravated asthma.
  – Development of chronic bronchitis.
  • Irregular heartbeats.
  • Nonfatal heart attacks.
  • Premature death in people with heart or lung disease.
<number>

## Slide 4: How Big Is Particulate Matter?
<number>

## Slide 5: National Ambient Air Quality Standards (NAAQS) for PM2.5
<number>
Primary Standards
Primary standards, also known as health standards, are limits set to protect public health, including the health of “sensitive” populations such as asthmatics, children, and the elderly.
Secondary Standards
Secondary standards are set to protect public welfare, including protection against decreased visibility, damage to animals, crops, vegetation, and buildings.

## Slide 6: History of the PM Standards
<number>
1971 | 1987 | 1997 | 2001 | 2002 | 2006 | 2009 | 2012
U.S. EPA issued first NAAQS for Total Suspended Particles (TSP)
µg/m3 = micrograms per cubic meter
U.S. EPA revised the NAAQS and replaced TSP with PM10
U.S. EPA revised NAAQS and included PM2.5
Annual 15 µg/m3
24-hour 65 µg/m3
Industry and state governments challenged NAAQS
U.S. Supreme Court upheld U.S. EPA‘s authority to enforce Clean Air Act and rules, U.S. EPA not allowed to consider cost
D.C. Circuit Court rejected all remaining legal challenges to the 1997 NAAQS
D.C. Circuit Court remanded the 2006 PM2.5 NAAQS to U.S. EPA for reconsideration, but did not vacate the standards
U.S. EPA strengthened the annual primary PM2.5 NAAQS to 12 µg/m3 and retained the existing secondary standard at 15 µg/m3
Retained existing 24-hour NAAQS at a level of 35 µg/m3
U.S. EPA strengthened the 24-hour NAAQS to 35 µg/m3 and retained the existing annual standard at 15 µg/m3

## Slide 7: Attaining the Standards
Annual Standard
To attain the 2012 annual standard, the three-year average of weighted annual mean PM2.5 concentrations from a monitor must not exceed 12 µg/m3.
  Exceedance versus a Violation of the Standard
  • An exceedance occurs when the annual mean is measured above the standard. A violation occurs when the three-year average of the annual mean is above the standard. A monitor can exceed the standard without being in violation.
24-Hour Standard
To attain the 2006 24-hour standard, the three-year average of the 98th percentile of 24-hour concentrations at each monitor must not exceed 35 µg/m3.
  Exceedance versus a Violation of the Standard
  • An exceedance occurs when the 98th percentile is measured above the standard. A violation occurs when the three-year average of the 98th percentile is measured above the standard. A monitor can exceed the standard without being in violation.
<number>
µg/m3 = micrograms per cubic meter

## Slide 8: Attainment Status
2006 Daily Standard
U.S. EPA attainment designations for the 2006 24-hour standard were effective December 14, 2009.
  • All Indiana counties were designated as attaining the standard and remain in attainment.
1997 Annual Standard
U.S. EPA attainment designations for the 1997 annual standard were effective on April 5, 2005.
• 12 full and five partial counties were designated as nonattainment.
• Dubois, Vanderburgh and Warrick counties, as well as Montgomery Township in Gibson County, Ohio Township in Spencer County, and Washington Township in Pike County were redesignated to attainment on October 27, 2011.
• Lawrenceburg Township in Dearborn County, which is part of the Cincinnati- Hamilton OH-KY-IN Fine Particles Nonattainment Area, was redesignated to attainment on December 23, 2011.
• Lake and Porter counties were redesignated to attainment on February 6, 2012.
• Hamilton, Hendricks, Johnson, Marion, and Morgan counties were redesignated to attainment on July 11, 2013.
• Clark and Floyd counties, as well as Madison Township in Jefferson County are pending redesignation with U.S. EPA.
• All areas of the state currently meet the 1997 annual air quality standard.
<number>

## Slide 9: Attainment Status
2012 Standard
On December 14, 2012, U.S. EPA strengthened the annual primary NAAQS to a level of 12 µg/m3 and retained the existing secondary annual standard at a level of 15 µg/m3 and primary and secondary 24-hour standards at a level of 35 µg/m3. The standards were finalized by U.S. EPA on January 15, 2013, and became effective on March 18, 2013.
Area Designations
• On December 12, 2013, Indiana submitted preliminary recommendations to U.S. EPA concerning air quality designations for the 2012 primary annual PM2.5 standard. Based on quality assured 2010 through 2012 monitoring data, preliminary and projected monitoring data for 2013, and a probability forecast for 2014, Indiana recommended all monitored counties within the state be designated as attainment under the primary annual PM2.5 standard.
• Indiana requested that U.S. EPA designate all other areas attainment/unclassifiable under the standard. U.S. EPA is scheduled to designate areas under the primary annual PM2.5 standard by December 12, 2014.
• U.S. EPA is scheduled to respond to initial state recommendations by August 14, 2014.
• U.S. EPA scheduled to make final designations by December 12, 2014; those designations will likely become effective in early 2015.
• State implementation plans due to U.S. EPA three years after designations become effective.
<number>

## Slide 10: Attainment Status
2012 Standard (continued)
• States are required to meet the standard no later than six years after designations become effective. States may request a possible extension of up to five additional years to attain the standard, depending on the severity of an area’s fine particles pollution problems and the availability of pollution controls.
• Based on 2013 monitoring data, no monitor in the state’s 2013 annual ambient air PM2.5 monitoring network recorded annual arithmetic mean values above the 2012 annual health standard.
• Based on quality assured 2011 through 2013 monitoring data, the Jeffersonville – Walnut Street fine particles monitor (Clark County) was the only monitor in the state’s 2013 annual ambient air PM2.5 monitoring network that recorded a three-year average annual arithmetic mean above the 2012 annual health standard.
<number>

## Slide 11
<number>

## Slide 12
<number>

## Slide 13: 2013 Monitoring Network
Placement
• U.S. EPA provides guidance on placement of monitors.
• Monitors placed based on population density and manufacturing levels.
Monitors
• 27 annual fine particle monitors in 20 counties across Indiana.
• 31* 24-hour fine particle monitors in 20 counties across Indiana.
Calculating the Design Value
• A monitor’s design value is calculated at the end of the year, once all of the data has been quality assured.
– Annual Design Value: three-year average of the weighted annual mean PM2.5 concentrations.
– 24-Hour Design Value: three-year average of the 98th percentile of 24-hour concentrations.
  * Four monitoring sites reflect air quality in a relatively small area, are directly influenced by a specific source, and are intended to be used for attainment status under the 24-hour standard only.
<number>

## Slide 14
<number>

## Slide 15
<number>

## Slide 16: PM2.5 Monitors by Area
Area | Counties
Central | Madison, Marion
East Central | Delaware, Henry
Northeast | Allen, Whitley
Northwest | Lake, LaPorte, Porter
North Central | Elkhart, St. Joseph
Southeast | Clark, Floyd
Southwest | Dubois, Greene, Spencer, Vanderburgh
West Central | Monroe, Tippecanoe, Vigo
<number>

## Slide 17: 2013 Monitoring Summary
• Based on 2013 monitoring data, no monitor in the state’s 2013 annual ambient air PM2.5 monitoring network recorded annual arithmetic mean values above the 2012 annual health standard.
• Based on quality assured 2011 through 2013 monitoring data, the Jeffersonville – Walnut Street fine particles monitor (Clark County) was the only monitor in the state’s 2013 annual ambient air PM2.5 monitoring network that recorded a three-year average annual arithmetic mean above the 2012 annual health standard.
• Based on 2013 monitoring data, no monitor in the state’s 2013 daily ambient air PM2.5 monitoring network recorded 24-hour 98th percentile values that exceeded the 2006 24-hour health standard.
• Based on quality assured 2011 through 2013 monitoring data, no monitor in the state’s 2013 daily ambient air PM2.5 monitoring network recorded a three- year average 98th percentile value that exceeded the 2006 24-hour health standard.
<number>

## Slide 18: Annual Arithmetic Mean Trends 2004-2013
<number>
µg/m3 = micrograms per cubic meter

## Slide 19: Annual PM2.5 Design Value Trends 2004-2013
<number>
Chart excludes monitors with incomplete data and/or less than three full years of monitoring data.
µg/m3 = micrograms per cubic meter

## Slide 20: 24-Hour 98th Percentile Trends 2004-2013
<number>
µg/m3 = micrograms per cubic meter

## Slide 21: 24-Hour PM2.5 Design Value Trends 2004-2013
<number>
Chart excludes monitors with incomplete data and/or less than three full years of monitoring data.
µg/m3 = micrograms per cubic meter

## Slide 22: Additional Information
For additional information regarding the NAAQS for fine particles, please visit U.S. EPA’s Particulate Matter Regulatory Actions website:
http://www.epa.gov/particles/actions.html
<number>

## Slide 23: Contact
For more information regarding the particulate matter designation process, or Indiana’s redesignation petition and maintenance plans, visit www.idem.IN.gov/airquality/2392.htm or contact Mr. Gale Ferris of the Office of Air Quality at (800) 451-6027, (317) 234-3653, or gferris@idem.IN.gov.
<number>