## Slide 1
RTCR
Revised Total Coliform Rule
Notes: In this lesson we are going to introduce the new Revised Total Coliform Rule, known as the RTCR, that will go into effect on April 1st, 2016. During this presentation and additional presentations we are going to go over the key aspects of this new rule.

## Slide 2: RTCR Timeline and Applicability
PWSs must comply no later than April 1,2016
RTCR Final Rule
RTCR applies to all PWSs
Regardless of system type, source, or size
Notes:   On February 13, 2013: The RTCR published
  Starting on April 1, 2016: All PWSs must begin complying with the federal requirements of the Rule [(40 CFR 141.851(c))].
As the name implies the RTCR is a revision of the 1989 Total Coliform Rule (TCR) and maintains the purpose of the TCR to protect public health by ensuring the integrity of the drinking water distribution system and monitoring for the presence of microbial contamination.
The RTCR is the only microbial drinking water regulation that applies to all PWSs. That is, both community water systems (CWSs) and non-community water systems (NCWSs), regardless of the source or population served. (40 CFR 141.851(b)).
Some examples of CWSs are municipalities, mobile home parks, and apartment complexes that provide their own water and serve at least 25 people or have 15 service connections. Examples of NCWSs include schools, factories, office buildings, gas stations, and campgrounds which have their own water systems and serve at least 25 people or have 15 service connections.
EPA anticipates greater public health protection under the RTCR, as PWSs that are vulnerable to microbial contamination are required to identify and fix problems (also known as the “find and fix” model)

## Slide 3: RTCR Purpose
Improve public health protection by reducing the pathways through which fecal contamination and pathogens can enter the distribution system.
TCR & RTCR objectives:
- Evaluate effectiveness of treatment
- Determine effectiveness of treatment
- Signal possible presence of microbial contamination
Notes: The RTCR maintains the objectives of the 1989 TCR, but it uses total coliform as an indicator of system operation and condition rather than an immediate public health concern, and uses E. coli as a fecal indicator.
The objectives of the Rule are to evaluate the effectiveness of treatment, to determine the integrity of the distribution system, and to signal the possible presence of microbial contamination.
The RTCR addresses these objectives by requiring water systems that may be vulnerable to microbial contamination (as indicated by their monitoring results) to do an assessment, to identify whether any sanitary defects are present, and to correct any defects that are found

## Slide 4: What are the RTCR Requirements PWSs Need to comply with?
RTCR
1. Contaminant Levels
2. Monitoring
3. Find & Fix
(Level 1 & 2 Assessments & Corrective Actions)
4. Reporting & Recordkeeping
5. Violations, Public Notification, & Consumer Confidence Reports
Notes: At a glance, this slide presents the category of requirements PWSs must comply with under the RTCR.
Everything on this slide should be familiar except for ITEM #3 (i.e., Level 1 and Level 2 assessments)… we are going to focus more on these assessments in another presentation
Contaminant levels (Maximum Contaminant Level Goal and Maximum Contaminate Level or MCL ) are based on the presence or absence of E.coli. Maximum Contaminate Level Goals are non-enforceable public health goals. An MCL is the highest level of a contaminant that is allowed in drinking water.
  The Maximum Contaminate Level Goal for E. coli is set at zero. Same as under TCR so this did not change.
  The MCL for E. coli is based on the occurrence of a condition. So the system is not in compliance with the MCL if:
    PWS has an EC+ repeat sample following a TC+ routine sample. Or
    PWS has a TC+ repeat sample following an EC+ routine sample.
    PWS fails to take all required repeat samples following an E. coli-positive routine sample.
    PWS fails to test for E. coli when any repeat sample tests positive for total coliforms.
Monitoring:
  Compliance sampling components include Site Sampling Plans as well as routine & repeat sampling with some revisions – and these will be touched on later in the presentation
Find and Fix
  PWSs are required to conduct a Level 1 or Level 2 assessment when certain conditions occur in their system. If any “sanitary defects” are found PWS must correct within a required timeframe. We will go into more depth on the assessments in another presentation.
Reporting and Record Keeping: this is essentially the same as under the TCR with addition of Level 1 and Level 2 assessment requirements.
Violations, PN and CCR: essentially the same with a few changes

## Slide 5: Maximum Contaminant Level (MCL)
MCL for E. coli
Combination of EC+ and TC+ between the routine and repeat results
EC+ routine sample with insufficient repeat samples
Failure to test for E. coli when any repeat sample is TC+
Notes: First we are going to go over what is the maximum contaminant level or MCL according to the RTCR . As I mentioned earlier, an MCL is the highest level of a contaminant that is allowed in drinking water.
An MCL for E. Coli can be reached by
Either a combination of EC+ and TC+ between the routine and repeat results,
an EC+ routine sample with insufficient repeat samples,
or a Failure to test for E. coli when any repeat sample is TC+

## Slide 6: Site Sampling Plans
Required for all systems
Must include upstream and downstream locations from all routine sample sites
    Shows where you plan on taking your total coliform samples
Plan must be submitted to IDEM no later than March 31, 2016.
IDEM will review and approve or request revisions.
Notes: All systems no matter the classification or the size are required to have a site sampling plan. The Site sampling plan is a plan that shows where you can to take your total coliform samples.
The plan has to be representative of the distribution system, identifying ROUTINE sample sites and two REPEAT sample sites for each ROUTINE site indicated. The REPEAT sample sites should be within 5 services connections of the ROUTINE site, with one being upstream and one being downstream.
Your plan must be submitted to IDEM no later than March 31, 2016. Once it is submitted, IDEM will review and approve or request revisions.

## Slide 7: Site Sampling Plans
Example
Notes: This is an example of an acceptable site sampling plan for a Non-community water system. As you can see from the map, they have a Routine sample site located at the Men’s Restroom which is representative of the distribution system. They have acceptable upstream and downstream sample locations at the Women’s Restroom and the Breakroom because they are located within 5 service connections from the routine sample location. So, this system will use this map to know where they need to collect their routine bacti sample as well as where they need to collect their repeats in the case that they have a positive routine sample.

## Slide 8: Monitoring
Samples must be collected based on the written site sampling plan.
Routine Samples
  All systems EXCEPT SEASONAL systems transition to the RTCR under their current monitoring schedule.
  Seasonal System will begin sampling monthly during the months they are in operation beginning April 1, 2016.
Notes: A little bit more about site sampling plans and monitoring.
Samples must be collected from sites located on your site sampling plan that corresponds to the sample you are collecting (whether it is a routine or a repeat sample)
All systems EXCEPT SEASONAL systems transition to the RTCR under their current monitoring schedule.
Seasonal System will begin sampling monthly during the months they are in operation beginning April 1, 2016.

## Slide 9: Monitoring
Routine Samples
  Quarterly Systems will be increased to monthly monitoring if any of the following occurs:
    Trigger a Level 2 or two (2) Level 1 Assessments in a rolling 12 month period
    Total Coliform TT violation (including failure to conduct a Level 1 or 2 assessment and/or correct sanitary defects)
    Two RTCR monitoring violations OR 1 RTCR monitoring violation and one level 1 assessment in a rolling 12 month period
  Monthly systems that wish to return to quarterly monitoring must:
    Have a complete sanitary survey or a voluntary level 2 assessment, within the last 12 months, and be free of sanitary defects
    Clean compliance history for a minimum of 12 months
Notes: More on routine samples.
Quarterly Systems will be increased to monthly monitoring if any of the following occurs:
  The system Triggers a Level 2 or two (2) Level 1 Assessments in a rolling 12 month period
  A Total Coliform TT violation (including failure to conduct a Level 1 or 2 assessment and/or correct sanitary defects)
  or Two RTCR monitoring violations OR 1 RTCR monitoring violation and one level 1 assessment in a rolling 12 month period
Monthly systems that wish to return to quarterly monitoring must:
  Have a complete sanitary survey or a voluntary level 2 assessment, within the last 12 months, and be free of sanitary defects
  And a Clean compliance history for a minimum of 12 months

## Slide 10: Monitoring
Repeat Samples
  Collect 3 repeat samples for each routine TC+
  Location –original site, within 5 connections upstream, within 5 connections downstream
  Collect additional set of repeats for each additional TC+ routine sample
  A Source sample from each well is still required under the GWR.
Notes: You must collect 3 repeat samples for each routine TC+. The location of where these repeats have to be collected from are the original site, one within 5 service connections upstream and one within 5 service connections downstream. These locations will be labeled on your site sampling plan.
You must collect additional set of repeats for each additional TC+ routine sample that your system collects.
Also, you still must collect a Source sample from your source water sample tap in order to comply with the GWR. If you have more questions about the GWR we have presentations focused solely on it.

## Slide 11: Monitoring: Additional Routine
Collect 3 “additional routine” samples in the next month, for PWSs monitoring quarterly:
  PWSs must collect at least 3 “additional routine” samples the month following 1 or more TC+ samples
  Samples must be:
    Collected at regular time intervals throughout the month or on a single day if taken from different sites
    Collected consistent with the site sampling plan
    Used to calculate whether the TT trigger has been exceeded or an E. coli MCL violation has occurred
Notes: Next we are going to talk about additional routine samples.
A system that monitors quarterly for the RTCR must collect 3 additional routine samples in the month following 1 or more TC+ samples.
  The samples must be:
    Collected at regular time intervals throughout the month or on a single day if taken from different sites,
    Collected consistent with the site sampling plan,
    And used to calculate whether the TT trigger has been exceeded or an E. coli MCL violation has occurred

## Slide 12: Questions?
TCR Website:
http://water.epa.gov/lawsregs/rulesregs/sdwa/tcr/index.cfm
RTCR Website:
http://water.epa.gov/lawsregs/rulesregs/sdwa/tcr/regulation_revisions.cfm
Fact Sheets:
Contact IDEM:
317/234-7430
Notes: If you have any questions about the new RTCR please use the links on this slide. If you would like to talk to someone about these new requirements please call the IDEM DWB at 317/234-7430.