POST-CLOSURE PERMIT APPLICATION GUIDANCE

Federal regulations 40 CFR Parts 260 through 270 have been incorporated by reference in Indiana rules.  Where exceptions to incorporated Federal regulations are necessary, these exceptions will be noted in the text of the State rule 329 IAC 3.1-1-7.

A.	FACILITY DESCRIPTION:

A-1	General Description:

40 CFR 270.14(b)(1)

Provide a brief description of the facility, including the nature of the business.  The description should include the types of industries served, and process(es) involved in the generation of hazardous waste.

A-2	Topographic Map:

40 CFR 270.14(b)(19), 40 CFR 270.14(c), 264.95, 264.97

Submit a topographic map which shows the facility and a distance of 1,000 feet around it, at a scale of 1 inch equal to not more than 200 feet.  The map must include:

-	Contours sufficient to show surface water flow around the facility operations;

-	Map date;

-	100-year floodplain area;

-	Surface waters;

-	Surrounding land uses;

-	Map orientation; and

-	Legal boundaries.

The map must also indicate the location of the following:

-	Access control;

-	Injection and withdrawal wells;

-	Buildings and structures;

-	Sewers;

-	Flood control or drainage barriers;

-	Run-on and run-off control systems;

-	Existing hazardous waste management units and solid waste management units;

-	The waste management area boundaries;

-	The point of compliance;

-	Groundwater monitoring well locations;

Note:	Multiple maps may be submitted, but all must be at a scale of 1 inch equal to not more than 200 feet.

A-3	Floodplain Standard:

40 CFR 270.14(b)(11)(iii), 264.18(b)

Document whether or not the closed facility is located within a 100-year floodplain and include the source of the data (Federal Insurance Administration Map or equivalent maps and calculations).

A-3a	Flood Proofing and Flood Protection Measures:

40 CFR 270.14(b)(11)(iv)(A) and (B)

Provide a structural or other engineering study showing how the design of the hazardous waste units and the flood proofing and protection devices at the facility will prevent washout.  For facilities located within the 100-year floodplain that do not comply with the floodplain standard, show how and when the facility will be brought into compliance.

A-3b	Floodplain Standard Waiver:

40 CFR 270.18(b)(1)(i) and (ii)

If a waiver from the Floodplain Standard is requested, the owner or operator must demonstrate that there will be no adverse effects on human health or the environment if washout occurs.  The following factors must be considered in this demonstration:  The volume and physical and chemical characteristics of the waste; the concentration of hazardous constituents that would potentially affect surface waters; the impact of such concentrations on the current uses of, and water quality standards established for, the affected surface waters; and the impact of hazardous constituents on the sediments of affected surface waters or the soils of the 100-year floodplain.

A-4	Post-Closure Notices:

40 CFR 264.116, 265.119(a) and (b), 270.14(b)(14)

Submit a copy of the following:

-	The survey plat indicating the location and dimension of landfill cells;

-	The record of the type, location, and amount of hazardous wastes disposed of within each cell which was submitted to the zoning authority or county land use authority, and the Commissioner;

-	The notice in deed that the land was used to manage hazardous waste and must not be disturbed; and

-	The certification that the information was recorded and a copy sent to the Commissioner.

B.	POST-CLOSURE INSPECTION REQUIREMENTS:

40 CFR 264.15, 264.118(b), and 270.14(b)(5)

The owner or operator must inspect his facility for malfunctions and deterioration, operator errors, and discharges which may be causing or lead to a release to the environment or threaten human health.

B-1	Written Inspection Plan

40 CFR 264.15(b), 270.21(d)

Describe the inspections conducted during the post-closure care period, their frequency, the inspection procedure, the types of problems to be looked for, and the logs to be kept.  The following items, as applicable, should be included as items to check for in the written inspection plan:

-	Security control devices;

-	Erosion damage;

-	Cover settlement, subsidence, and displacement;

-	Vegetative cover condition;

-	Integrity of the run-on and run-off control measures;

-	Cover drainage system function;

-	Leachate collection/detection and removal system;

-	Gas venting system;

-	Well condition; and

-	Benchmark integrity.

The rationale for determining the length of time between inspections should be provided.

B-2	Inspection Remedial Actions:

40 CFR 264.15(c), 264.118(b)(2)

Describe the actions to be taken if any deterioration or malfunctions are noted from inspections at the facility.

B-3	Inspection Log:

40 CFR 264.15(d)

Records of inspection must be kept in an inspection log or summary.  These must be kept for a period of at least three years from the date of the inspection.  At a minimum, these records must include the date and time of the inspection, the name of the inspector, a notation of the observations made, and the date and nature of any repairs or other remedial actions.

C.	POST-CLOSURE PLAN:

40 CFR 270.14(b)(13) and (14), 264.110 through 264.120, 265.110 through 265.120

The post-closure plan must include, but not be limited to the following information.  Note that if an approved post-closure care plan under interim status is available, most of this information will already be included in that plan.

C-1	Post-Closure Contact:

40 CFR 264.118(b)(3)

Provide the name, address, and phone number of the person(s) or office to contact about the facility during the post-closure period.

C-2	Post-Closure Security:

40 CFR 264.14, 270.14(b)(4)

Demonstrate that there is adequate security at the site during the post-closure period.  This consists of fences, barriers, warning signs, or other means to control entry onto the closed portion of the facility.  The facility may provide a justification demonstrating the reasons for requesting a waiver of this requirement.

C-3	Request for Waiver of Preparedness and Prevention Requirements:

40 CFR 264, Subpart C

If any or all of the requirements of 40 CFR 264.30 through 40 CFR 264.37 are inapplicable, a waiver may be requested to eliminate these sections from the post-closure permit application.

C-4	Landfill Maintenance Plan

Note that the unit may have operated as a surface impoundment, waste pile, or other land disposal unit.  However, the unit was closed as a landfill in accordance with 40 CFR 264.118.  For this reason, the unit must be maintained and monitored as if it were a hazardous waste landfill.  For post-closures of non-landfills, references to landfill cells should be used for guidance only.

C-4a	List of Wastes:

40 CFR 270.21(a), 264.309

Provide a list of hazardous wastes placed in each landfill or landfill cell.  If any treatment was accomplished in the landfills during its active life, describe the nature and quantity of the wastes remaining in the landfill after treatment was completed.

C-4b	Liner and Cap System Description:

40 CFR 270.21(b)(1), 264.301, 264.310(b)(1)

Provide a description of the liner and cap system, including the type of liner, its material and thickness, USCS-type data for soil liners, and for synthetics, the manufacturer and product name.  Show the limits of the liner and cap coverage.

C-4b(1)	Liner System Foundation Description:

40 CFR 270.21(b)(1), 264.301(a) or (b), 264.310(b)(1)

Describe the foundation for the liner system, including the foundation design and materials of construction, and a brief description of the procedures used to prepare the foundation before the installation of the liner system.

C-4b(2)	Leachate Collection/Detection System Operation and Design (If Applicable):

40 CFR 270.21(b)(1), 264.301(a) or (b), 264.310(b)(2)

Describe the design features, including drawings, of the leachate detection system showing how the system functions to detect any leakage through the liner system in a timely manner.  Describe the design features, including drawings, of the leachate collection and removal system showing how the system functions to remove collected leachate in a timely manner.

C-4c	Run-On Control System:

40 CFR 270.21(b)(2) and (4), 264.301(f) and (h), 264.310(b)(4)

Describe the system that will be used to prevent run-on onto waste management portions of the landfill.  Indicate any major problems or failures associated with the run-on control system during the active life of the facility, and discuss methods employed to resolve these problems.  If there was a prior release, refer to Section E of the checklist.

C-4d	Run-Off Control System:

40 CFR 270.21(b)(3) and (4), 264.301(g) and (h), 264.310(b)(4)

Describe the run-off control system to be used to collect and control run-off from waste management portions of the landfill.  Indicate if there were any major problems or failures associated with the run-off control system during the active life of the facility that may have resulted in a release of hazardous wastes.  If there was a prior release, refer to Section E of the checklist.

C-4e	Cap Maintenance:

264.310(b)

Describe the preventative and corrective maintenance procedures, equipment procedures, equipment requirements and material needs.  Include the following items in the maintenance plan, as applicable:

•	Erosion damage repair;

•	Correction of settlement, subsidence and displacement;

•	Mowing, fertilization and other vegetative cover maintenance; and

•	Repair of run-on and run-off control structures.

Describe the rationale to be used to determine the need for corrective maintenance activities.

C-5	Post-Closure Cost Estimate:

329 IAC 3.1-15-5

Provide a copy of the up-to-date post-closure cost estimate, calculated to cover the cost, in current dollars, of post-closure monitoring and maintenance of the facility in accordance with the applicable post-closure plan.

C-6	Financial Assurance for Post-Closure Care:

329 IAC 3.1-15-6

Provide a copy of the established financial assurance mechanism for post-closure care of the facility.  The mechanism must be one of the following:

C-6a	Post-Closure Trust Fund:

329 IAC 3.1-15-6(b), 3.1-15-10(a)

Provide a copy of the post-closure trust fund agreement with the wording required by 329 IAC 3.1-15-10(a) and submit a formal certification of acknowledgment.

C-6b	Surety Bond:

329 IAC 3.1-15-6(c) and (d), 3.1-15-10(b) and (c)

C-6b(1)	Surety Bond Guaranteeing Payment into a Post-Closure Trust Fund:

329 IAC 3.1-15-6(c), 3.1-15-10(b)

Provide a copy of the surety bond with the wording required by 329 IAC 3.1-15-10(b), and a copy of the standby trust agreement.  The bond must guarantee that the owner or operator will fund the standby trust fund in an amount equal to the penal sum of the bond before the beginning of final closure of the facility, or fund the standby trust fund in an amount equal to the penal sum within 15 days of an order to begin closure, or provide alternate financial assurance if the bond is canceled.

C-6b(2)	Surety Bond Guaranteeing Performance of Post-Closure Care:

329 IAC 3.1-15-6(d), 3.1-15-10(c)

Provide a copy of the surety bond with the wording required by 329 IAC 3.1-15-10(c), guaranteeing that the owner or operator will perform post-closure care according to the post-closure plan and the requirements of 40 CFR 264, Subpart G.

C-6c	Post-Closure Letter of Credit:

329 IAC 3.1-15-6(e), 3.1-15-10(d)

Provide a copy of the irrevocable letter of credit with the wording required by 329 IAC 3.1-15-10(d) and a copy of the standby trust agreement.  The letter of credit must be issued for a period of at least one year and be for the amount of the estimated post-closure costs.

C-6d	Post-Closure Insurance:

329 IAC 3.1-15-6(f), 3.1-15-10(e)

Provide a copy of the certificate of insurance with the wording required by 329 IAC 3.1-15-10(e).  Each policy must contain a provision allowing assignment of the policy to a successor owner or operator.  The post-closure insurance policy must be issued for a face value at least equal to the current cost estimate, except as provided for in D-3f.

C-6e	Financial Test and Corporate Guarantee for Post-Closure Care:

329 IAC 3.1-15-6(g), 3.1-15-10(f), 3.1-15-10(h)

Submit a letter signed by the owner's or operator's chief financial officer and worded as specified in 329 IAC 3.1-15-10(f), a copy of the independent certified public accountant's report on examination of the applicant's financial statements for the latest fiscal year, and a special report from the certified public accountant.  If a parent corporation is guaranteeing the post-closure care for a subsidiary facility, the corporate guarantee must accompany the preceding items.

C-6f	Use of Multiple Financial Mechanisms:

329 IAC 3.1-15-6(h)

Provide a copy of a combination of financial mechanisms, including trust fund agreements, surety bonds guaranteeing payment into a post-closure trust fund, letters of credit, and insurance, together which provide financial assurance for the amount of post-closure care.

C-6g	Use of Financial Mechanism for Multiple Facilities:

329 IAC 3.1-15-6(i)

Provide a copy of a financial assurance mechanism for more than one facility, showing, for each facility, the EPA ID number, name, address, and amount of post-closure funds assured by the mechanism.  The amount of funds available through the mechanism must be no less than the sum of the funds that would be available if a separate mechanism had been established and maintained for each facility.

D.	GROUNDWATER MONITORING:

D-1	Interim Status Period Groundwater Monitoring Data:

40 CFR 270.14(c)(1), 265.90 thru 265.94

Post-Closure renewals do not need to include the referenced interim status information.  Facilities for which this is the first post-closure permit must provide a summary of the groundwater monitoring data obtained during the interim status period, including:

-	A copy of the topographic map provided for Section 40 CFR 270.14(b) on which the location and identification of each interim status monitoring well are indicated.  An indication of which wells are downgradient of the disposal area, and which are upgradient should also be included.

-	Details of the design and construction of each interim status monitoring well (e.g., depths of screen and casing, depths at which water was encountered, filter pack, and sealing materials placement, dates of construction, boring logs, etc.).  Use of Indiana Department of Environmental Management Guidance is suggested.

-	Copies of each quarterly (from first year) water analysis results for each well, and copies of any subsequent (annual or semi-annual) water analysis reports to date.  Include copies of any notifications of significant change in water analysis parameter values made to the Commissioner pursuant to 40 CFR 265.93.  All interim status period monitoring results must be provided, regardless of any changes made to the facility's groundwater monitoring system after initiation of the monitoring program; groundwater surface elevation measurements must also be provided.

-	A copy of the facility's interim status groundwater sampling and analysis plan (required under 40 CFR 265.92(a)).

-	Calculations of the initial background arithmetic mean and variance for each indicator parameter based on replicate measurements from upgradient wells during the first year.

-	A description of the statistical procedures used (if applicable) in processing the data submitted (as in the use of a Student's t-test and the level of significance used), and results of statistical comparisons between upgradient and downgradient well sampling results and first year background values for each indicator parameter.

-	If required, based on statistical comparison results, the specific plan for a groundwater quality assessment program in addition to the results of implementing such a plan. Include results of the determinations made under the groundwater quality assessment.

-	Whether hazardous waste or hazardous waste constituents have entered the groundwater;

-	The rate and extent of migration of hazardous waste or hazardous waste constituents in the groundwater;

-	The concentrations of hazardous waste or hazardous waste constituents in the groundwater; and

-	Results of the annual evaluations of groundwater surface elevations, and descriptions of the response to those evaluations, where applicable.

D-2	Aquifer Identification:

40 CFR 270.14(c)(2)

Identify the uppermost aquifer and any hydraulically interconnected underlying aquifers (i.e., all likely subsurface flow paths for hazardous constituents which may leak from the facility), and describe their hydrogeologic properties (e.g., hydraulic gradient, groundwater flow, rate and direction); provide the supporting data used to identify this information (i.e., the information obtained from hydrogeologic investigations of the facility area).  This identification must include a report written by a qualified hydrogeologist on the hydrogeologic characteristics of the facility property supported by at least the drilling logs of on-site borings and wells and the available professional literature.  Include a description of the regional geologic and hydrogeologic setting.  In addition, include the following site-specific data:

An analysis of topographic or geomorphic features that might influence the groundwater flow system.

A classification and description of the hydrogeologic properties (hydraulic conductivity, porosity, texture, thickness, etc.) of all of the hydrogeologic units found at the site (i.e., the aquifers and any intervening saturated and unsaturated units).

A description of water level or fluid pressure monitoring, including:

a.	Water level contour maps or vertical sections;

b.	Well or piezometer hydrographs; and

c.	An interpretation of the flow system, including the vertical and horizontal components of flow.

A description of the field methods used in the study, and a summary of which data were collected by each method.

D-3	Contaminant Plume Description:

40 CFR 270.14(c)(4), 264 Appendix IX

For existing facilities suspected of contaminating groundwater, provide a description of any plume of contamination that has entered the groundwater from a regulated unit at the time the application is submitted that:

-Delineates the extent of the plume on the topographic map of 40 CFR 270.14(b)(19).

-Identifies the concentration of each constituent listed in 40 CFR 264, Appendix IX throughout the plume or identifies the maximum concentration of each 40 CFR 264, Appendix IX constituent in the plume.

This requirement is applicable to all existing facilities where interim status monitoring shows the presence of hazardous constituents downgradient from the regulated units, unless it can be proven that such constituents are coming from another source.  In addition, this requirement may be applied to other existing facilities where interim status monitoring data are nonexistent or deficient if these facilities are suspected of contaminating groundwater, or if the Commissioner determines that a facility's interim status monitoring program is incapable of determining whether hazardous constituents have entered the groundwater from a regulated unit.

Note:	In some cases, contaminant plumes may be defined under groundwater quality assessment programs carried out during the interim status period as required by 40 CFR 265.93(d).  Normally, such assessment programs do not address the complete list of Appendix IX constituents as required under 40 CFR 270.14(c)(4)(ii).  Additional monitoring will be required to identify the concentration of each Appendix IX constituent in the plume.

D-4	Detection Monitoring Program:

40 CFR 270.14(c)(6), 264.98

Provide sufficient information, supporting data, and analyses documenting the absence of hazardous constituents in the groundwater to support the implementation of a detection monitoring program at the present time.

D-4a	Indicator Parameters, Waste Constituents, Reaction Products to be Monitored For:

40 CFR 270.14(c)(6)(i), 264.98(a)

Supply a list of indicator parameters, waste constituents, or reaction products that can provide a reliable indication of the presence of hazardous constituents in the groundwater.

D-4a(1)	Hazardous Waste Characterization:

40 CFR 264.98(a)(1)

Identify the type, quantity, and concentrations of constituents in wastes managed at the regulated unit(s).

D-4a(2)	Behavior of Constituents:

40 CFR 264.98(a)(2)

Provide a description of the expected mobility, stability, and persistence of waste constituents, or their reaction products, in the unsaturated zone beneath the waste management area.

D-4a(3)	Detectability:

40 CFR 264.98(a)(3)

Specify the detectability of indicator parameters, waste constituents, or their reaction products in the groundwater.

D-4b	Groundwater Monitoring Program:

40 CFR 270.14(c)(6)(ii), 264.97

Describe in detail the individual elements of the monitoring system to be used during detection monitoring.

D-4b(1)	Description of Wells:

40 CFR 264.97(a) and (c)

Identify the number, location, and depth of each well.  Describe the well construction materials.

D-4b(2)	Representative Samples:

40 CFR 264.97(a)(1) and (2)

Provide details supporting the representative nature of the groundwater quality at (a) the background monitoring points and (b) the compliance monitoring point.

D-4b(3)	Locations of Background Monitoring Wells That Are Not Upgradient:

40 CFR 264.97(a)(1)

For wells that are not located upgradient from the waste management area, demonstrate that either the hydrogeologic conditions do not allow determination that the wells are upgradient, or that sampling at other wells will provide an indication of background groundwater quality that is as representative or more representative than that provided by the upgradient wells.

D-4c	Background Values:

40 CFR 270.14(c)(6)(iii), 264.98(c)

Submit background values for each proposed monitoring parameter or constituent, or procedures to calculate such values.  Submit the information identified in Section D-4c(1) or D-4c(2).

D-4c(1)	Data Currently Available:

40 CFR 264.98(c)

D-4c(1)(a)	Background Groundwater Quality Data:

40 CFR 264.98(a)(4), 264.98(c)

Specify the concentrations and coefficients of variation for each of the proposed monitoring parameters or constituents in the background groundwater quality.

D-4c(1)(b)	Sampling Frequency:

40 CFR 264.97(g)(1)

Demonstrate the background groundwater quality for each parameter or constituent is based on data obtained through quarterly sampling of wells.

D-4c(1)(c)	Sampling Quantity:

40 CFR 264.98(d)

Demonstrate that a minimum of one sample from each well and a minimum of four samples from the entire system is taken each time the system is sampled.  The collection of at least four (4) samples is not necessary if the alternate sampling procedure at 40 CFR 264.97(g)(2) is being used.

D-4c(1)(d)	Background Values:

40 CFR 264.98(c)

Show that the background values for each monitoring parameter or constituent will be expressed in the form necessary to determine statistically significant increases.

D-4c(2)	Plan for Establishing Groundwater Quality Data:

40 CFR 270.14(c)(6), 264.98

Submit a plan for establishing background values.  The plan must address the following items:

D-4c(2)(a)	Well Location:

40 CFR 264.98(a), 264.98(b)

Indicate the wells to be used to collect the background groundwater quality data.

D-4c(2)(b)	Sampling Frequency:

40 CFR 264.97(g)(1)

Demonstrate that background groundwater quality for each parameter or constituent is based on data obtained through quarterly sampling of wells.

D-4c(2)(c)	Sampling Quantity:

40 CFR 264.98(d)

Demonstrate that a minimum of one sample from each well and a minimum of four samples from the entire system is taken each time the system is sampled.  The collection of at least four (4) samples is not necessary if the alternate sampling procedure at 40 CFR 264.97(g)(2) is being used.

D-4c(2)(d)	Background Values:

40 CFR 264.98(c)

Show that the background values for each monitoring parameter or constituent will be expressed in the form necessary to determine statistically significant increases.

D-4d	Sampling, Analysis and Statistical Procedures:

40 CFR 270.14(c)(6)(iv), 264.97(d), (e), and (h), 264.98(d), (e), (f) and (g)

Submit a proposed sampling and analysis plan that includes procedures for  sample collection, sample preservation and shipment, analytical methods, and chain-of-custody controls.  The plan must also describe the statistical comparison procedure(s) to be used.

D-4d(1)	Sample Collection:

40 CFR 264.97(d)(1)

Describe in detail the procedures and techniques for sample collection.

D-4d(2)	Sample Preservation and Shipment:

40 CFR 264.97(d)(2)

Describe the procedures and techniques for sample preservation and shipment.

D-4d(3)	Analytical Procedure:

40 CFR 264.97(d)(3)

Describe the analytical technique that will be used for each monitoring parameter.  (The methods specified in the most recent edition of "Test Methods for the Evaluation of Solid Waste, Physical/Chemical Methods" (SW-846) as referenced in 40 CFR 260.11, must be used.)

D-4d(4)	Chain-of-Custody:

40 CFR 264.97(d)(4)

Describe the procedures for chain-of-custody control for all samples collected.

D-4d(5)	Additional Requirements for Compliance Point Monitoring:

40 CFR 264.98(d)

D-4d(5)(a)	Sampling Frequency:

40 CFR 264.98(d)

Demonstrate that sampling of each monitoring well at the compliance point will be performed semi-annually during the post-closure period.

D-4d(5)(b)	Compliance Point Groundwater Quality Values:

40 CFR 264.98(d)

Show that the groundwater quality values will be expressed in the form necessary to determine statistically significant increases.

D-4d(6)	Annual Determination:

40 CFR 264.98(e)

Specify the procedure for the annual determination of the uppermost aquifer flow rate and direction.

D-4d(7)	Statistical Determination:

40 CFR 264.98(f)

Specify the procedures used to determine whether there has been a statistically significant increase over background values for each parameter or constituent monitored at the compliance point.

D-4d(7)(a)	Statistical Procedure:

40 CFR 264.97(h)

Specify the statistical comparison procedures which will be used to evaluate whether there has been a statistically significant increase over background values for each parameter or constituent monitored at the compliance point.

D-4d(7)(b)	Results:

40 CFR 264.98(f)(2)

Provide an estimate of the time period, subsequent to sampling completion, within which the results of the statistical analysis will be available.

D-5	Compliance Monitoring Program:

40 CFR 270.14(c)(7), 264.99

If the presence of hazardous constituents has been detected in the groundwater at the point of compliance at the time of permit application, submit the following information:

D-5a	Waste Description:

40 CFR 270.14(c)(7)(i)

A description of the wastes previously handled at the facility.  This description must include:

Historical records of volumes, types (including EPA waste code, if applicable), and chemical composition of wastes placed in units in the waste management area;

The results of any direct sampling of the waste (see "Test Methods for the Evaluation of Solid Waste, Physical/Chemical Methods," SW-846);

A list of constituents that are reasonably expected to be in or derived from the waste; and

Identification of the dominant constituents expected to be present and their relative abundance.

If it is expected that some constituents may form a separate, immiscible fluid, the composition of this fluid and its viscosity and density must be included in the application.

D-5b	Characterization of Contaminated Groundwater:

40 CFR 270.14(c)(7)(ii)

Provide a characterization of the contaminated groundwater, including the concentration of identified hazardous constituents.  For each well at the point of compliance, and for each background well, provide the following information:

Concentrations of each constituent in 40 CFR 261, Appendix VIII;

Concentrations of major anions and cations; and

Concentrations of the constituents listed in 40 CFR 264, Appendix IX, if not already determined by the above.

D-5c	Hazardous Constituents to be Monitored:

40 CFR 270.14(c)(7)(iii), 264.93

Specify the hazardous constituents to be monitored and present a rationale for selecting these constituents.

D-5d	Concentration Limits:

40 CFR 270.14(c)(7)(iv), 264.99(a)(2), 264.94(a)

Specify proposed concentration limits for each hazardous constituent (The proposed concentration limit must not exceed the present background level of that constituent in the groundwater nor may it exceed the value of that constituent listed in 40 CFR 264.94(a)(2), Table 1, entitled "Maximum Concentrations of Constituents for Groundwater Protection".  If you wish to petition the Commissioner to establish alternate concentration limits than those specified above, you must supply the information identified in comment D-5e.).

D-5e	Alternate Concentration Limits:

40 CFR 270.14(c)(7)(iv), 264.99(a)(2), 264.94(b)

Provide a justification for establishing alternate concentration limits.  This justification must address each of the following factors:

D-5e(1)	Adverse Effects on Groundwater Quality:

40 CFR 264.94(b)(1)

The adverse effects on groundwater quality, considering:

-	The physical and chemical characteristics of the waste in the regulated unit, including its potential for migration;

-	The hydrogeological characteristics of the facility and surrounding land;

-	The quantity of groundwater and the direction of groundwater flow;

-	The proximity and withdrawal rates of groundwater users;

-	The current and future uses of groundwater in the area;

-	The existing quality of groundwater, including other sources of contamination and their cumulative impact on the groundwater quality;

-	The potential for health risks caused by human exposure to waste constituents;

-	The potential damage to wildlife, crops, vegetation, and physical structures caused by exposure to waste constituents; and

-	The persistence and permanence of the potential adverse effects.

D-5e(2)	Potential Adverse Effects:

40 CFR 264.94(b)(2)

The potential adverse effects on hydraulically-connected surface-water quality, considering:

-	The volume and physical and chemical characteristics of the waste in the regulated unit;

-	The hydrogeological characteristics of the facility and surrounding land;

-	The quantity and quality of groundwater, and the direction of groundwater flow;

-	The patterns of rainfall in the region;

-	The proximity of the regulated unit to surface waters;

-	The current and future uses of surface waters in the area and any water quality standards established for those surface waters;

-	The existing quality of surface water, including other sources of contamination and the cumulative impact on surface-water quality;

-	The potential for health risks caused by human exposure to waste constituents;

-	The potential damage to wildlife, crops, vegetation, and physical structures caused by exposure to waste constituents; and

-	The persistence and permanence of the potential adverse effects.

D-5f	Groundwater Monitoring System:

40 CFR 270.14(c)(7)(v), 264.97, 264.99(b)

Describe in detail the individual elements of the monitoring system to be used during compliance monitoring.

D-5f(1)	Description of Wells:

40 CFR 264.97(a) and (c)

Identify the number, location and depth of each well.  Describe the well construction materials.

D-5f(2)	Representative Samples:

40 CFR 264.97(a)(1) and (2)

Provide details supporting the representative nature of the groundwater quality at (a) the background monitoring points and (b) the compliance monitoring point.

D-5f(3)	Locations of Background Groundwater Monitoring Wells that are not Upgradient:

40 CFR 264.97(a)(1)(i)

For wells that are not located upgradient from the waste management area, provide information for either D-5f(3)(a) or D-5f(3)(b).

D-5f(3)(a)	Inability to Determine Upgradient:

40 CFR 264.97(a)(1)(i)(A)

Demonstrate that the hydrogeologic conditions do not allow determination that the wells are upgradient.

D-5f(3)(b)	Representative Samples of Background Groundwater Quality:

40 CFR 264.97(a)(1)(i)(B)

Demonstrate that sampling at other wells will provide an indication of background groundwater quality that is as representative or more representative than that provided by the upgradient wells.

D-5g	Background Values:

40 CFR 270.14(c)(6), 264.97(g), 264.99(c)

Submit background values for each proposed monitoring parameter or constituent, or procedures to calculate such values.  Submit the information identified in Section D-5g(1) or D-5g(2).

D-5g(1)	Background Groundwater Quality Data Currently Available:

40 CFR 270.14(c)(8), 264.99(c)

D-5g(1)(a)	Background Groundwater Quality Data:

40 CFR 264.97(g), 264.99(c)

Specify the concentrations and coefficients of variation for each of the proposed monitoring parameters or constituents.  Document that the background groundwater quality is based on data from upgradient wells that account for measurement errors in sampling and analysis and accounts, to the extent feasible, for seasonal fluctuation in background groundwater quality if such fluctuations are expected to affect the concentration of the hazardous constituent.

D-5g(1)(b)	Sampling Frequency:

40 CFR 264.97(g), 264.99(f)

Describe the sampling frequency used in developing the data base used to determine a background value for each parameter or constituent for each well.

D-5g(1)(c)	Sampling Quantity:

40 CFR 264.99(f)

Demonstrate that a minimum of one sample from each well and a minimum of four samples from the entire system is taken each time the system is sampled.

D-5g(1)(d)	Background Values:

40 CFR 264.99(c)(2)

Show that the background values for each monitoring parameter or constituent will be expressed in the form necessary to determine statistically significant increases.

D-5g(2)	Plan for Establishing Background Groundwater Quality Data:

40 CFR 264.99(c), 264.97(g)

Submit a plan for establishing background groundwater quality values.  The plan must address the following items:

D-5g(2)(a)	Background Data:

40 CFR 264.97(g)

Document that the background groundwater quality will be based on data from upgradient wells--which will be available before the permit is issued; that the data accounts for measurement errors in sampling and analysis and accounts, to the extent feasible, for seasonal fluctuations in background groundwater quality if such fluctuations are expected to affect the concentration of the hazardous constituent.

D-5g(2)(b)	Well Location:

40 CFR 264.97, 264.99(c)

Indicate the wells to be used to collect the data.

D-5g(2)(c)	Sampling Frequency:

40 CFR 264.99(f)

Describe the sampling frequency to be used in developing the data base used to determine the background water quality for a monitoring parameter or constituent for each well.

D-5g(2)(d)	Sampling Quantity:

40 CFR 264.99(f)

Demonstrate that a minimum of one sample from each well and a minimum of four samples from the entire system is taken each time the system is sampled.

D-5g(2)(e)	Background Values:

40 CFR 264.97(a)(1)(i)

Show that the background values for each monitoring parameter or constituent will be expressed in the form necessary to determine statistically significant increases.

D-5h	Sampling, Analysis and Statistical Procedures:

40 CFR 270.14(c)(7)(vi), 264.98(d), (e), (f), (g) and (h), 264.99(c)

Submit a proposed sampling and analysis plan that includes procedures for sample collection, sample preservation and shipment, analytical methods, and chain-of-custody controls.  The plan must also describe the statistical comparison procedure(s) to be used.

D-5h(1)	Sample Collection:

40 CFR 2674.97(d)(1)

Describe the procedures and techniques for sample collection.

D-5h(2)	Sample Preservation and Shipment:

40 CFR 264.97(d)(2)

Describe the procedures and techniques for sample preservation and shipment.

D-5h(3)	Analytical Procedure:

40 CFR 264.97(d)(3)

Describe the analytical technique that will be used for each monitoring parameter (The methods specified in "Test Methods for the Evaluation of Solid Waste, Physical/ Chemical Methods" (SW-846) as referenced in 40 CFR 260.11, must be used.).

D-5h(4)	Chain-of-Custody:

40 CFR 264.97(d)(4)

Describe the procedures for chain-of-custody control for all samples collected.

D-5h(5)	Additional Requirements for Compliance Point Monitoring:

40 CFR 264.99

D-5h(5)(a)	Sampling Frequency:

40 CFR 264.99(f)

Demonstrate that sampling of each monitoring well at the compliance point will be performed semi-annually during the post-closure period.

D-5h(5)(b)	Testing for Appendix IX Hazardous Constituents:

40 CFR 264.99(g)

Specify the procedure for the annual testing of all monitoring wells at the compliance point for all constituents contained in 40 CFR 264, Appendix IX.

D-5h(5)(c)	Compliance Point Groundwater Quality Values:

40 CFR 264.99(c)(2)

Show that the groundwater quality values will be expressed in the form necessary to determine statistically significant increases.

D-5h(6)	Annual Determination:

40 CFR 264.99(e)

Specify the procedure for the annual determination of the uppermost aquifer flow rate and direction.

D-5h(7)	Statistical Determination:

40 CFR 264.99(d)

D-5h(7)(a)	Statistical Procedure:

40 CFR 264.97(h), 264.99(d)

Specify the statistical comparison procedures which will be used to evaluate whether there has been a statistically significant increase over background values for each parameter of constituent monitored at the compliance point.

D-5h(7)(b)	Results:

40 CFR 264.99(d)(2)

Provide an estimate of the time period, subsequent to sampling completion, within which the results of the statistical analysis will be available.

D-6	Corrective Action Program:

40 CFR 270.14(c)(8)

If hazardous constituents have been measured in the groundwater which exceed the concentration limits established under 40 CFR 264.94, or if groundwater monitoring conducted at the time of permit application at the waste boundary indicates the presence of hazardous constituents from the facility in groundwater over background concentrations, the owner or operator must submit sufficient information, supporting data, and analyses to establish a corrective action program which meets the requirements of 40 CFR 264.100.  (However, an owner or operator is not required to submit information to establish a corrective action program if he demonstrates to the Regional Administrator that alternate concentration limits will protect human health and the environment after considering the criteria listed in 40 CFR 264.94(b)).

Submit the following information to establish a corrective action program:

D-6a	Characterization of Contaminated Groundwater:

40 CFR 264.100(a), 270.14(c)(8)(i)

Provide a characterization of the contaminated groundwater, including the concentration of identified hazardous constituents.  For each well at the point of compliance, and for each background well, provide the following information:

-	Concentrations of each constituent in 40 CFR 264, Appendix IX;

-	Concentrations of major anions and cations; and

-	Concentrations of the constituents listed in Table 1 of 40 CFR 264.94, if not already determined by the above.

D-6b	Concentration Limits:

40 CFR 270.14(c)(8)(ii), 264.99(a)(2), 264.94(a)

Specify proposed concentration limits for each hazardous constituent (The proposed concentration limit must not exceed the present background level of that constituent in the groundwater nor may it exceed the value of that constituent listed in Table 1 of 40 CFR 264.94, entitled "Maximum Concentrations of Constituents for Groundwater Protection" (If you wish to petition the Commissioner to establish alternate concentration limits than those specified above you must supply the information identified in comment D-6c.).

D-6c	Alternate Concentration Limits:

40 CFR 270.14(c)(8)(ii), 264.99(a)(2), 264.94(b)

Provide a justification for establishing alternate concentration limits.  This justification must address each of the following factors:

D-6c(1)	Adverse Effects on Groundwater Quality:

40 CFR 264.94(b)(1)

Address the adverse effects on groundwater quality, considering:

-	The physical and chemical characteristics of the waste in the regulated unit, including its potential for migration;

-	The hydrogeological characteristics of the facility and surrounding land;

-	The quantity of groundwater and the direction of groundwater flow;

-	The proximity and withdrawal rates of groundwater users;

-	The current and future uses of groundwater in the area;

-	The existing quality of groundwater, including other sources of contamination and their cumulative impact on the groundwater quality;

-	The potential for health risks caused by human exposure or waste constituents;

-	The potential damage to wildlife, crops, vegetation, and physical structures caused by exposure to waste constituents; and

-	The persistence and permanence of the potential adverse effects.

D-6c(2)	Potential Adverse Effects:

40 CFR 264.94(b)(2)

Address the potential adverse effects on hydraulically-connected surface water quality, considering:

-	The volume and physical and chemical characteristics of the waste in the regulated unit;

-	The hydrogeological characteristics of the facility and surrounding land;

-	The quantity and quality of groundwater, and the direction of flow;

-	The patterns of rainfall in the region;

-	The proximity of the regulated unit to surface waters;

-	The current and future uses of surface waters in the area and any water quality standards established for those surface waters;

-	The existing quality of surface water, including other sources of contamination and the cumulative impact on surface water quality;

-	The potential for health risks caused by human exposure to waste constituents;

-	The potential damage to wildlife, crops, vegetation, and physical structures caused by exposure to waste constituents; and

-	The persistence and permanence of the potential adverse effects.

D-6d	Corrective Action Plan:

40 CFR 270.14(c)(8)(iii), 264.100(b)

The applicant must include detailed plans and an engineering report on the corrective actions proposed for the facility.  This information must include:

D-6d(1)	Location:

40 CFR 270.14(c)(8)(iii), 264.100(b)

Maps showing the location of engineered barriers, caps, drains, and wells, etc. (Use the topographic map in Section A-2).

D-6d(2)	Construction Detail:

40 CFR 270.14(c)(8)(iii), 264.100(b)

Descriptions and engineering drawings of construction details and specifications of engineered barriers, caps, drains, wells, etc.

D-6d(3)	Plans for Removing Wastes:

40 CFR 270.14(c)(8)(iii), 264.100(b)

If proposed, plans for removing and handling of any hazardous wastes.

D-6d(4)	Treatment Technologies:

40 CFR 270.14(c)(8)(iii), 264.100(b)

A description of the treatment technologies to be used for contaminated groundwater that is pumped or drained from the zone of contamination.

D-6d(5)	Effectiveness of Corrective Action Program Chosen:

40 CFR 270.14(c)(8)(iii), and (iv), 264.100(b)

A prediction and sensitivity analysis on the effectiveness of corrective actions. (For example, anticipated drain flow rates, assuming a range of hydrologic properties.)

D-6d(6)	Reinjection System:

40 CFR 270.14(c)(8)(ii), 264.100(b)

If treated ground or surface water is to be reinjected at the site, the concentration levels of all hazardous constituents to be reinjected.

D-6d(7)	Additional Hydrogeologic Data:

40 CFR 270.14(c)(8)(iii), 264.100(b)

A description and summary of any additional hydrogeologic data collected for use in designing the corrective action.

D-6d(8)	Operation and Maintenance:

40 CFR 270.14(c)(8)(iii), 264.100(b)

Operation and maintenance plans for the correction action measures.

D-6d(9)	Closure and Post-Closure Plans:

40 CFR 270.14(c)(8)(iii), 264.100(b)

If applicable, closure and post-closure care plans for the materials used to handle hazardous wastes as part of the corrective action.

D-6e	Groundwater Monitoring Program:

40 CFR 270.14(c)(8)(iii) and (iv), 264.100(d)

Provide a description of the groundwater monitoring program used to assess the effectiveness of the corrective action measures.  Water quality monitoring must be conducted over the on-site extent of the contaminated groundwater.  Submit the following information:

D-6e(1)	Description of Wells:

40 CFR 264.97(a) and (c)

Identify the number, location, and depth of each well.  Describe the well construction materials and materials used.  Provide maps and diagrams.

D-6e(2)	Representative Samples:

40 CFR 264.97(a)(1) and (2)

Provide details supporting the representative nature of the groundwater quality at (a) the background monitoring points and (b) the compliance monitoring point.

D-6e(3)	Locations of Background Groundwater Monitoring Wells that are not Upgradient:

40 CFR 264.97(a)(1)(A) and (B)

For wells that are not located upgradient from the waste management area, demonstrate either that the hydrogeologic conditions do not allow determination that the wells are upgradient, or that sampling at other wells will provide an indication of background groundwater quality that is as representative or more representative than that provided by the upgradient wells.

D-6f	Background Values:

40 CFR 264.99(c)

Submit background values for each proposed monitoring parameter or constituent, or procedures to calculate such values.  Submit the information identified in Section D-6f(1) or D-6f(2).

D-6f(1)	Data Currently Available:

40 CFR 264.99(c)

D-6f(1)(a)	Background Groundwater Quality Data:

40 CFR 264.98(g), 264.99(c)

Specify the concentrations and coefficients of variation for each of the proposed monitoring parameters or constituents.  Document that the background groundwater quality is based on data from upgradient wells that account for measurement errors in sampling and analysis and accounts, to the extent feasible, for seasonal fluctuation in background groundwater quality if such fluctuations are expected to affect the concentration of the hazardous constituent.

D-6f(1)(b)	Sampling Frequency:

40 CFR 264.97(g), 264.99(f)

Describe the sampling frequency used in developing the data base used to determine a background value for each parameter or constituent for each well.

D-6f(1)(c)	Sampling Quantity:

40 CFR 264.99(f)

Demonstrate that a minimum of one sample from each well and a minimum of four samples from the entire system is taken each time the system is sampled.

D-6f(1)(d)	Background Values:

40 CFR 264.99(c)(2)

Show that the background values for each monitoring parameter or constituent will be expressed in the form necessary to determine statistically significant increases.

D-6f(2)	Plan for Establishing Groundwater Quality Data:

40 CFR 264.99(c), 264.97(g)

Submit a plan for establishing background groundwater quality values.  The plan must address the following items:

D-6f(2)(a)	Background Data:

40 CFR 264.97(a)(1)

Document that the background groundwater quality will be based on data from upgradient wells--which will be available before the permit is issued; that the data accounts for measurement errors in sampling and analysis and accounts, to the extent feasible, for seasonal fluctuations in background groundwater quality if such fluctuations are expected to affect the concentration of the hazardous constituent.

D-6f(2)(b)	Well Location:

40 CFR 264.99(c), 264.97

Indicate the wells to be used to collect the data.

D-6f(2)(c)	Sampling Frequency:

40 CFR 264.99(f)

Describe the sampling frequency to be used in developing the data base used to determine the background water quality for a monitoring parameter or constituent for each well.

D-6f(2)(d)	Sampling Quantity:

40 CFR 264.99(f)

Demonstrate that a minimum of one sample from each well and a minimum of four samples from the entire system is taken each time the system is sampled.

D-6f(2)(e)	Background Values:

40 CFR 264.99(c)(2)

Show that the background values for each monitoring parameter or constituent will be expressed in the form necessary to determine statistically significant increases.

D-6g	Sampling, Analysis and Statistical Procedures:

40 CFR 270.14(c)(7)(v) and (vi), 264.97(d), (e), (f), (g) and (h), 264.99(c), (d), (f) and (g)

Submit a proposed sampling and analysis plan that includes procedures for sample collection, sample preservation and shipment, analytical methods, and chain-of-custody controls.  The plan must also describe the statistical comparison procedure(s) to be used.

D-6g(1)	Sample Collection:

40 CFR 264.97(d)(1)

Describe the procedures and techniques for sample collection.

D-6g(2)	Sample Preservation and Shipment:

40 CFR 264.97(d)(2)

Describe the procedures and techniques for sample preservation and shipment.

D-6g(3)	Analytical Procedure:

40 CFR 264.97(d)(3)

Describe the analytical technique that will be used for each monitoring parameter. (The methods specified in "Test Methods for the Evaluation of Solid Waste, Physical/ Chemical Methods" (SW-846), as referenced in 40 CFR 260.11, must be used)

D-6g(4)	Chain-of-Custody:

40 CFR 264.97(d)(4)

Describe the procedures for chain-of-custody control for all samples collected.

D-6g(5)	Additional Requirements for Compliance Point Monitoring:

40 CFR 264.99

D-6g(5)(a)	Sampling Frequency:

40 CFR 264.99(f)

Demonstrate that sampling of each monitoring well at the compliance point will be performed semi-annually during the active life of a regulated unit.

D-6g(5)(b)	Testing for Appendix IX Hazardous Constituents:

40 CFR 264.99(g)

Specify the procedure for the annual testing of all monitoring wells at the compliance point for all constituents contained in 40 CFR 264, Appendix IX.

D-6g(5)(c)	Compliance Point Groundwater Quality Values:

40 CFR 264.99(c)(2)

Show that the groundwater quality values will be expressed in the form necessary to determine statistically significant increases.

D-6g(6)	Annual Determination:

40 CFR 264.99(e)

Specify the procedures for the annual determination of the uppermost aquifer flow rate and direction.

D-6g(7)	Statistical Determination:

40 CFR 264.99(d)

Specify the procedures to be used to determine whether there has been a statistically significant increase over background values for each parameter or constituent monitored at the compliance point.

D-6g(7)(a)	Statistical Procedure:

40 CFR 264.97(h), 264.99(d)(1)

Specify the statistical comparison procedures which will be used to evaluate whether there has been a statistically significant increase over background values for each parameter or constituent monitored at the compliance point.

D-6g(7)(b)	Results:

40 CFR 264.99(d)(2)

Provide an estimate of the time period, subsequent to sampling completion, within which the results of the statistical analysis will be available.

E.	CORRECTIVE ACTION FOR SOLID WASTE MANAGEMENT UNITS:

This section is to be used for solid waste management units at the facility.  RCRA hazardous waste management units are covered above.

E-1	Solid Waste Management Units:

40 CFR 264.101

Identify all solid waste management units at the facility including inactive units, if known.  A solid waste management unit may include any of the following:

-	Landfill;

-	Surface impoundment;

-	Waste pile;

-	Land treatment unit;

-	Tank (including less than 90 day accumulation);

-	Injection well;

-	Incinerator;

-	Wastewater treatment tank;

-	Container storage area;

-	Waste handling area;

-	Transfer station; and

-	Waste recycling operation.

E-2	Characterization of the Solid Waste Management Unit(s):

40 CFR 270.14(d)(1)

For each solid waste management unit, submit the following information:

-	Type of unit;

-	Location of each existing or closed unit on the topographic map (see comment A-2);

-	Engineering drawings for each unit, if available;

-	Dimensions and materials of construction of each unit, if available;

-	Dates when the unit was in operation, if known;

-	Description of the wastes placed in the unit, if known; and

-	Quantity or volume of waste, if known.

E-3	Lack of Solid Waste Management Units:

40 CFR 264.101

If a claim is made that no solid waste management units exist on-site, describe the methodology used to make that determination (e.g., review of old solid waste permits, blueprints).

E-4	Releases:

40 CFR 264.101, 270.14(d)(2)

Provide all information available, including releases reported under CERCLA §103, on whether or not any releases have occurred from any of the solid waste management units at the facility.  Reasonable efforts to identify releases must be made, even if releases have not been verified (A release may include: spilling, leaking, pumping, pouring, emitting, emptying, discharging, injecting, escaping, leaching, dumping into the environment).

E-4a	Characterize Releases:

40 CFR 264.101, 270.14(d)(3)

Information on releases must include the following concerning prior or current releases:

-	Date of the release;

-	Type of waste or constituent released;

-	Quantity or volume released;

Nature of the release:

-	Spill;

-	Overflow;

-	Ruptured pipe or tank;

-	Result of the unit's construction (e.g., unlined surface impoundment, leaky tank); or

-	Other.

-	Groundwater monitoring and other analytical data available to describe the nature and extent of the release.  If other than groundwater monitoring data, please describe;

-	Physical evidence of distressed vegetation or soil contamination;

-	Historical evidence of releases such as tanker truck accidents;

-	Any federal, state, or local enforcement actions which may address releases;

-	Any public citizen complaints about the facility which would indicate a release; and

-	Any information showing the migration of the release.

E-4b	No Releases:

40 CFR 264.101, 270.14(d)(3)

Describe the methodology used to determine that releases from solid waste management units are not present (e.g., review of groundwater monitoring data).

F.	OTHER FEDERAL LAWS:

40 CFR 270.14(b)(20)

Demonstrate compliance with the requirements of applicable Federal laws such as the Wild and Scenic Rivers Act, National Historic Preservation Act of 1966, Endangered Species Act, Coastal Zone Management Act, and the Fish and Wildlife Coordination Act.

G.	PART B CERTIFICATION:

40 CFR 270.11

Applications must be accompanied by a certification statement as specified in 40 CFR 270.11(d).  The required signatures are as follows:

-	For a corporation, a principal executive officer (at least at the level of vice-president);

-	For a partnership or sole proprietorship, a general partner or the proprietor, respectively;

-	For a Municipal, State, Federal or other public agency, either a principal executive officer or ranking elected official.