# PARTICULATE CONTROL EQUIPMENT: Electrostatic Precipitator – INSTRUCTIONS

The purpose of CE-04 (state form 52621) is to summarize all of the physical and operational parameters of an electrostatic precipitator used to control particulate emissions.  Complete this form once for each control device (or once for each set of identical control devices).  CE-04 is a required form for submitting information about an electrostatic precipitator to IDEM, OAQ.  For the purposes of this form, the term “source” refers to the plant as a whole and NOT to the individual emissions units.

If you have any questions, contact the Office of Pollution Prevention and Technical Assistance (OPPTA) at (317) 232-8172 or (800) 988-7901 extension 2-8172 (toll free call within Indiana).

## Part A: Identification and Description of Control Equipment

Part A identifies the particulate control device and to describe its physical properties.

- Control Equipment ID:
Provide the identification number for each device used to control or limit air pollutant emissions.  The identification numbers listed on this form should correspond to the emissions unit identified on the Plant Layout diagram and Process Flow diagram.

- Installation Date:
Specify when the control equipment was installed.  At a minimum, the month and year of installation is required.

- Device Type:
Specify the type of electrostatic precipitator.

- Mist Eliminator:
Specify if mist eliminators are used, and provide the number of each type used.

- Gas Stream Conditioning Agents:
Identify and agents added to the gas stream for conditioning prior to control.

- Number of Vertical Discharge Electrodes:
Specify the number of vertical discharge electrodes in the electrostatic precipitator.

- Style of Wires:
Briefly describe the style of wires used for the discharge electrodes.

- Number of Transformer – Rectifier (T-R) Sets:
Specify the number of Transformer – Rectifier (T-R) sets for the electrostatic precipitator.

- Number of Fields:
Specify the number of field in the electrostatic precipitator.

- Rapper Type and Amount:
Specify whether the rappers are roof or side mounted, and provide the total number of rappers.

- Rapping Frequency:
Specify the rapping frequency.

- T-R Voltage Rating:
Provide the primary and secondary voltage rating for the T-R sets.

- T-R Current Rating:
Provide the primary and secondary current rating for the T-R sets.

## Part B: Operational Parameters

Part B provides the operational parameters of the control device and the pollutant laden gas stream.  Appropriate units must be included if the standard units are not used.

- Gas Stream Flow Rate:
Provide the volumetric flow rate of the gas stream prior to entering the control device, after leaving the control device, and include the calculation of the difference in flow rate between the inlet and outlet of the device.  You must also include the units for flow rate.  Air flow rates are typically provided in actual cubic feet per minute (acfm).

- Gas Stream Temperature:
Provide the average temperature of the gas stream prior to entering the control device, after leaving the control device, and include the calculation of the difference in temperature between the inlet and outlet of the device.  You must also indicate the temperature scale used.  Air stream temperatures are typically provided in degrees Fahrenheit ((F).

- Gas Stream Pressure:
Provide the pressure applied to the gas stream prior to entering the control device, after leaving the control device, and include the calculation of the difference in pressure between the inlet and outlet of the device.  You must also include the units of pressure.  Air pressure is typically provided in inches of water (in H2O) or pounds per square inch (psi) or millimeters of mercury (mm Hg).

- Moisture Content:
Provide the moisture content of the gas stream prior to entering the control device, after leaving the control device, and include the calculation of the difference in moisture content between the inlet and outlet of the device.  Moisture content is typically provided as a percent (%).

- Particle Size Range:
Provide the average size range of the particulates in the gas stream prior to entering the control device, after leaving the control device, and include the calculation of the difference in size range of particulates between the inlet and outlet of the device.  Particulate size range is typically provided in micrometers ((m).

- Other:
Specify any other parameter of the control device, and provide the appropriate value for the parameter prior to entering the control device, after leaving the control device, and include the calculation of the difference between the inlet and outlet of the device.  Specify the units of measure used for the control device parameter.

## Part C: Pollutant Concentrations

Part C provides the operational parameters of the particulate control device and the pollutant laden gas stream.  Appropriate units must be included if the standard units are not used.

- Units:
For each pollutant controlled, provide the units of measure for each concentration.  Pollutant concentrations are typically provided in pounds per hour (lb/hr), tons per year (tpy), parts per million by volume (ppmv) or in milligrams per liter (mg/L), or in grains per dry standard cubic foot (gr/dscf).

- Inlet:
For each pollutant controlled, provide the concentration of the pollutant in the gas stream prior to entering the control device.

- Outlet:
For each pollutant controlled, provide the concentration of the pollutant in the gas stream after leaving the control device.

- Efficiency:
Provide a capture and control efficiency for each pollutant controlled by the control device.

Capture
The capture efficiency of the control device is the amount of the contaminated gas stream that is collected by the control device.  Provide the particulate capture efficiency for the control device.  Efficiency is typically provided as a percent (%).

Control
The control efficiency of the control device is the amount of contaminant that is removed from the captured gas stream by the control device.  Provide the particulate control efficiency for the control device.  Efficiency is typically provided as a percent (%).

## Part D: Monitoring, Record Keeping, & Testing Procedures

Part D identifies any existing or proposed monitoring, record keeping, & testing procedures that may need to be included in the permit.

- Items Monitored:
Specify what is or will be monitored for each control device.  For example, “pressure drop across the baghouse”.

- Monitoring Frequency:
Specify the frequency for each monitored item (e.g., “once per shift”).

- Items Recorded:
List what records are or will be kept for each listed control device (e.g., “raw material usage”).

- Record Keeping Frequency:
Specify the record keeping frequency for each recorded item (e.g., “daily log of material usage”).

- Pollutants Tested:
For each listed emissions unit, list the performance tests conducted.  For the pressure drop example, the performance test would be for “particulate matter”.

- Test Methods:
If the applicable requirement requires the use of a specific test method, identify the test method.  Standard testing methods are provided by the American Society for Testing and Materials (ASTM) (http://www.astm.org/).  If no specific test method is required, describe the methods used to for the performance test.

- Testing Frequency:
Specify the testing frequency for each performance test (e.g., “annually”).

## Part E: Preventive Maintenance Plan

Part E verifies that a complete Preventive Maintenance Plan (PMP) has been prepared for the control device, if applicable.  Use this table as a checklist to ensure that the PMP is complete.

- Do you have a Preventive Maintenance Plan (PMP)?
Specify whether or not a Preventive Maintenance Plan (PMP) is needed for the control device.  If the PMP is needed, use the checklist items A-D to verify that the PMP is complete.

- Identification of the individual(s) responsible for inspecting, maintaining and repairing emission control devices.
Identify the individual(s) responsible for inspecting, maintaining and repairing emission control devices.

- Description of the items or conditions that will be inspected.
Describe the items or conditions that will be inspected.

- Schedule for inspection of items or conditions described above.
Specify the schedule for inspection of items or conditions described above.

- Identification and quantification of the replacement parts that will be maintained in inventory for quick replacement.
Identify and quantify the replacement parts that will be maintained in inventory for quick replacement.

## ***SUBMISSION OF CONFIDENTIAL RECORDS***

All information submitted to IDEM will be made available to the public unless it is submitted under a claim of confidentiality.  Claim of confidentiality must be made at the time the information is submitted to IDEM, and must follow the requirements set out in 326 IAC 17.1-4-1.  Failure to follow these requirements exactly will result in your confidential information becoming a public record, available for public inspection.  To ensure that your information remains confidential, refer to the IDEM, OAQ information regarding submittal of confidential business information.  For more information on confidentiality for certain types of business information, please review IDEM’s Nonrule Policy Document Air-031-NPD regarding Emission Data.