## Slide 1: Terrestrial Habitat and Endangered Species
Project Area Land Use
  Riparian Forest
  Agricultural
IDNR Natural Heritage Database
  State Species of Special Concern in Area:
    Kidney Shell Mussel (Ptychobranchus fasciolaris)
  No impacts expected to State Species of Special Concern
USFWS
  2013 Interim Policy
    Potential for impacts assumed to be minimal
  Range-Wide Programmatic Informal Consultation for the Indiana Bat and Northern Long Eared Bat
    “Not Likely to Adversely Affect”
    Avoidance, Minimization, & Mitigation Measures to be implemented
[ 1 ]

## Slide 2: Cultural Resources
Archaeological
  Records Check and Phase Ia Field Reconnaissance
  No Archaeological deposits in project area
Historic Properties
  Two resources 50 years or older within the Area of Potential Effects (APE)
    Bridge No. (421)39-12-01792B, which is the focus of this project
    St. Luke Church and Cemetery
Historic Bridge Programmatic Agreement
  Alternatives Analysis:
    Feasible and Prudent Alternative
    Secretary of Interior’s Standards for Rehabilitation
Effect Finding:
  “No Adverse Effect” published November 14, 2019 in The Times
  State Historic Preservation Officer concurred with Finding on December 09, 2019

## Slide 3: Section 4(f)
Historic Properties:
  Bridge No. (421)39-12-01792B
    Programmatic Use Determination
      Will not impair the historic integrity of the bridge
      Currently used for transportation purposes
      No Section 4(f) conversion will take place
  St. Luke Church and Cemetery
    Will not convert property to a transportation use
    Section 106 finding of “No Adverse Effect”
    No Section 4(f) analysis required

## Slide 4: Purpose and Need
Need:
  Advanced deterioration of structure
  Sufficiency Rating of 46.7 out of 100
  Current deficiencies
    Bridge Deck: Exhibiting sings of spalling, transverse and longitudinal cracking, and efflorescence
    Superstructure: Minor section loss, spalling with exposed rebar, and longitudinal cracking with efflorescence. Metal trusses have widespread rust with severe rusting and section loss at four corner connections
    Substructure: Minor section loss, interior piers are exhibiting sings of cracking and have exposed rebar
Purpose:
  Correct the listed deficiencies of the structure
  Provide continued safe vehicular crossing over South Fork Wildcat Creek
  Increase the service life of the structure

## Slide 5: Alternatives
Do Nothing
  No expenditure of capital funds – utilize existing facility
  Result in road closure
  Does not meet Purpose and Need of project
  Not prudent
Preferred Alternative
  Rehabilitation for Continued Vehicular Use
  Meets Secretary of Interior’s Standards for Rehabilitation
  Meets Purpose and Need
  Feasible and prudent

## Slide 6: Preferred Alternative
Replacing reinforced concrete pier pedestals for Spans A and C
Replacing end abutment caps
Replacing the end spans A and C, with new prestressed concrete box beam superstructures, a new reinforced concrete deck and new type FC concrete railing
Abutments 1 & 4 would become semi-integral. New joints would be installed at Pier 2 and Pier 3 where superstructure type changes
Replacing the existing reinforced concrete deck on the steel pony truss main span
Repairing the existing steel pony truss by:
  Replacing steel elements in-kind
  Replacing deteriorated rivets with round-headed bolts
  Repairing deteriorated members by attaching additional steel plates to restore member’s original cross-sectional area Installing new bridge deck drains
Cleaning and painting the existing steel pony truss and attached existing metal bridge railing
Constructing new reinforced concrete bridge approaches
Replacing existing guardrail at all four bridge corners
Wedge and level and/or replacing existing asphalt pavement as necessary
Installing riprap turnouts at the ends of the concrete bridge railing transitions
Adding scour protection

## Slide 7: Preferred Alternative – Plan and Profile View

## Slide 8: Detour

## Slide 9: Right-of-Way
This project will not require the acquisition of any permanent or temporary right-of-way

## Slide 10: Project Schedule
The anticipated schedule is…
  Public Hearing – September 04, 2020
  Environmental Document Completion – October 2020
  Completion of the Design Phase – December 2020
  Project Letting – March 10, 2021
  Construction to Begin – Summer 2021
  Note – Construction completed by Spring 2022

## Slide 11: Public Comment Reminders
Mail to Harlan Ford at GAI Consultants, Inc., 201 N. Illinois Street, Suite 1700, Indianapolis, IN 46204
Fax to: 317-570-6810
Email to h.ford@gaiconsultants.com
Please ensure that comments are postmarked no later than September 19, 2020
All comments will be reviewed, evaluated, and given due consideration during the decision-making process