## Slide 1: U.S. 20 at State Road 2 New Interchange
Indiana Department of Transportation
Wednesday, Aug. 1, 2018
6 p.m.

## Slide 2: Welcome
Purpose/explanation of public hearing
Public hearing format
Visit our sign-in table
Informational handouts
Participate during public comment session
Submit written public comments
Project display area

## Slide 3: U.S. 20 at SR 2 New Interchange
Introduction of INDOT Project Team
  Project Management
  Public Involvement
  LaPorte District – INDOT Regional Office
  Environmental Services
  Troyer Group
    Engineering, Design & Environmental Analysis Team
Recognition of elected and local public officials
Sign-in at attendance table to be added to project mailing list
Legal notice of public hearing was published in the South Bend Tribune 7/16 & 7/23
A notice of the public hearing was mailed to known property owners within project area
Announcement of this hearing was posted to INDOT website. A media release was also issued
A copy of presentation and project documentation are available for review on-line via INDOT website

## Slide 4: Project Stakeholders
Indiana Department of Transportation
Indiana Division Federal Highway Administration
LaPorte County
Elected & local officials
Residents and citizens
Commuters
Businesses
Emergency services
Schools
Churches
Community Organizations

## Slide 5: Project Development
Project Selection
Early Coordination
Environmental phase begins
Purpose & Need
Develop alternatives
Preliminary design phase
Release environmental document for public review and comment
HOLD PUBLIC HEARING
Additional work to finalize environmental document and project design
Communicate Project Decision
Real Estate Acquisition
Project Letting
Construction

## Slide 6: Environmental Analysis Phase
  National Environmental Policy Act (NEPA)
  Requires INDOT to analyze and evaluate the impacts of a proposed project to the natural and socio-economic environments
  NEPA is a decision-making process
    Purpose and Need
    Alternatives Screening
    Preferred Alternative
  Impacts are analyzed, evaluated and described in an environmental document
    What are the impacts this project might have on the community?
    How can impacts be avoided?
    Can impacts be minimized?
    Mitigation for impacts?

## Slide 7: Environmental Analysis Phase
  Notice of Entry for Survey – late 2015
    Letters mailed to properties within general area
      Describing early project proposal
      Project personnel in area, may need to enter properties
      Gather data for environmental analysis
  Section 106 of National Historic Preservation Act – early 2018
    Take into account proposal’s impact to historic & archaeological properties
    Consulting Parties Process – early 2018
    Groups invited to participate
    Public notice issued with 30 day comment period
      South Bend Tribune
      LaPorte Herald Argus
    “No historic properties affected” finding issued by INDOT Cultural Resources Office (CRO) acting on behalf of the Federal Highway Administration (FHWA)
  Draft environmental document released for public involvement – July 2018
    Available for review via public repositories

## Slide 8: Project Resources
INDOT LaPorte District Office
  315 E. Boyd Boulevard, LaPorte, IN 46350
  LaPorteDistrictCommunications@indot.in.gov
  http://www.in.gov/indot/2705.htm
  Planning, Project Development/Delivery, Construction, Maintenance for Northwest Indiana
Rolling Prairie Public Library
1 East Michigan Street, Rolling Prairie, IN 46371
Phone: (219) 778-2390
INDOT Office of Public Involvement
  100 North Senate Avenue, Room N642, Indianapolis, IN 46204
  Phone: (317) 232-6601
  rclark@indot.in.gov
Transportation Services Call Center
Provides citizen and business customers with a single point-of-contact to request transportation services, obtain information, or provide feedback through multiple channels of communications.
855-463-6848 • INDOT4U.com • INDOT@indot.in.gov

## Slide 9: U.S. 20 at SR 2 – Purpose and Need
Purpose
  Increase operational safety at the intersection of U.S. 20 and SR 2
    Decrease points of conflict with highest volume of traffic
    Deter truck traffic from utilizing U.S. 20 through New Carlisle as a shortcut between the western leg of the intersection and U.S. 31
    Maintain and improve operational efficiency
Need
  High rate of traffic accidents
    The existing intersection struggles to provide an acceptable Level of Service (LOS) and the operational efficiency necessary to adequately meet current and future traffic demand

## Slide 10: Crash Data
Crash Data for U.S. 20 at SR 2 |  |  |  |  |  |  |  |  |  |  | 
YEAR SEVERITY | ‘08 | ‘09 | ‘10 | ‘11 | ‘12 | ‘13 | ‘14 | ‘15 | ‘16 | ‘17 | Total
Crash with no Injury | 14 | 12 | 7 | 7 | 9 | 14 | 10 | 12 | 14 | 17 | 159
Non-Incapacitating Injury | 4 | 4 | 3 | 9 | 10 | 5 | 4 | 3 | 1 | 7 | 67
Incapacitating Injury | 1 | - | 1 | 1 | - | 1 | 1 | 2 | - | 3 | 10
Fatal | - | - | 1 | - | - | - | - | - | 1 | - | 2
Total | 19 | 16 | 12 | 17 | 19 | 20 | 15 | 17 | 16 | 27 | 238

## Slide 11: Alternatives Considered
No Build
  Baseline for comparison for build alternatives
  Does not meet purpose and need, does not enhance safety at intersection
Tight Diamond Interchange
  Stop controlled intersections with a bridge carrying the north-south leg over the east-west leg
  May require additional right-of-way
  Does not decrease the number of conflict points to greatest degree
  Does not increase traffic efficiency to the greatest degree
Dog-bone interchange with a 3-sided structure
  East-west roadway would pass over the north-south roadway by means of a three-sided structure (i.e. tunnel).
  Results in more expensive structure, both up-front and long-term (tunnel vs. bridge)
  No right-of-way acquisition necessary

## Slide 12: Alternatives Considered

## Slide 13: Alternatives Analysis – Traffic Capacity
Chart: 20 YEARS RELATIVE GROWTH RATES RESULTING IN FAILURE CONDITIONS
| 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036 | 2037 | 2038 | 2039
DOGBONE DESIGN (G.R. = 5.6%) | 12635 | 13342.56 | 14089.7434 | 14878.769 | 15711.9801 | 16591.8509 | 17520.9946 | 18502.1703 | 19538.2918 | 20632.4362 | 21787.8526 | 23007.9723 | 24296.4188 | 25657.0182 | 27093.8113 | 28611.0647 | 30213.2843 | 31905.2282 | 33691.921 | 35578.6686 | 37571.074 | 39675.0542 | 41896.8572 | 44243.0812 | 46720.6938 | 49337.0526 | 52099.9276
DIAMOND DESIGN (G.R. =3.80%) | 12635 | 13115.13 | 13613.5049 | 14130.8181 | 14667.7892 | 15225.1652 | 15803.7215 | 16404.2629 | 17027.6249 | 17674.6746 | 18346.3123 | 19043.4721 | 19767.1241 | 20518.2748 | 21297.9692 | 22107.2921 | 22947.3692 | 23819.3692 | 24724.5052 | 25664.0364 | 26639.2698 | 27651.5621 | 28702.3214 | 29793.0096 | 30925.144 | 32100.2995 | 33320.1109
NO BUILD - EXISTING SIGNAL (G.R. = 2.75%) | 12635 | 12982.4625 | 13339.4802 | 13706.3159 | 14083.2396 | 14470.5287 | 14868.4682 | 15277.3511 | 15697.4783 | 16129.1589 | 16572.7108 | 17028.4603 | 17496.743 | 17977.9034 | 18472.2958 | 18980.2839 | 19502.2417 | 20038.5534 | 20589.6136 | 21155.828 | 21737.6132 | 22335.3976 | 22949.621 | 23580.7356 | 24229.2058 | 24895.509 | 25580.1355
PROJECTED INTERSECTION GROWTH (G.R. = 1.6%) | 12635 | 12837.16 | 13042.5546 | 13251.2354 | 13463.2552 | 13678.6673 | 13897.526 | 14119.8864 | 14345.8046 | 14575.3374 | 14808.5428 | 15045.4795 | 15286.2072 | 15530.7865 | 15779.2791 | 16031.7476 | 16288.2555 | 16548.8676 | 16813.6495 | 17082.6679 | 17355.9906 | 17633.6864 | 17915.8254 | 18202.4786 | 18493.7183 | 18789.6177 | 19090.2516

## Slide 14: Existing Intersection

## Slide 15: Preferred Alternative – Overall Plan

## Slide 16: Preferred Alternative – Enlarge Plan and Profile

## Slide 17: Truck Turning Movements
WB ‒ 67

## Slide 18: Truck Turning Movements
19-axle Heavy Haul

## Slide 19: Maintenance of Traffic
State Detour Route

## Slide 20: Maintenance of Traffic
Local Detour Routes

## Slide 21: Project Schedule
PUBLIC HEARING
Public comment period
Prepare Public Hearing Transcript
AUGUST 2018
Review public comments
Continue work on preliminary design and environmental document
FALL 2018
Finalize environmental document
Communicate Project Decision
FALL 2018
Complete design
LATE 2018
Project Letting
Construction
2019

## Slide 22: Submit Public Comments
Submit public comments using the options described in first page of information packet:
  Public Comment Form
  Via e-mail
  Participate during public comment session following formal presentation
INDOT respectfully requests that comments be submitted by Friday, Aug. 17, 2018
All comments submitted will become included in an official public hearings transcript and made part of the public record
Comments will be reviewed, evaluated and given full consideration during decision-making process

## Slide 23: Next Steps
Public and project stakeholder input
  Submit comments via options described on page 1 of information packet
INDOT review and evaluation
  All comments given full consideration during decision-making process
  Finalize/approve environmental document, complete project design
Communicate a decision
  INDOT will notify project stakeholders of decision
  Work through local media, social media outlets, paid legal notice
  Make project documents accessible via repositories
Questions? Contact Public Involvement Team

## Slide 24: Thank You
Please visit with the design team and INDOT project officials following the presentation and Q & A.
Project Open House
  Project maps, displays, INDOT project team and informal Q & A
  INDOT LaPorte District page: http://www.in.gov/indot/2705.htm
  LaPorteDistrictCommunications@indot.in.gov

## Slide 25: Project Resources
INDOT LaPorte District Office
  315 E. Boyd Boulevard, LaPorte, IN 46350
  LaPorteDistrictCommunications@indot.in.gov
  http://www.in.gov/indot/2705.htm
  Planning, Project Development/Delivery, Construction, Maintenance for Northwest Indiana
Rolling Prairie Public Library
1 East Michigan Street, Rolling Prairie, IN 46371
Phone: (219) 778-2390
INDOT Office of Public Involvement
  100 North Senate Avenue, Room N642, Indianapolis, IN 46204
  Phone: (317) 232-6601
  rclark@indot.in.gov
Transportation Services Call Center
Provides citizen and business customers with a single point-of-contact to request transportation services, obtain information, or provide feedback through multiple channels of communications.
855-463-6848 • INDOT4U.com • INDOT@indot.in.gov